## Slide 1: TG bh MAC Address Designation (MAAD MAC)
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Outline
AP shows support for MAAD in Extended Capabilities
  STA does not indicate support. Third party observer does not know MAAD is in use.
STA associates
At any time while associated, STA sends MAAD request
  MAD Request Action fame – does not form part of association.
AP sends MAAD response which is a 48 bit MAC address
  Locally administered
  AP stores the allocated MAAD MAC for that STA
  STA stores the allocated MAAD MAC for that AP
When STA comes back it uses the MAAD MAC Address (or not)
AP instantly recognizes the STA from TA.
  AP can identify the STA pre-association – e.g. directed probe
STA Associates using the allocated MAAD MAC as TA
At any time, STA sends MAAD request and gets a new MAAD response with a new MAC Address
  Note that The request/response DOES NOT FORM PART OF ASSOCIATION.
Etc. etc.

## Slide 3: MAAD Action frames
Octets: 1 1
Figure – 9-ccc – MAAD Request Action field format
Category | MAAD Action | MAAD MAC
Category | MAAD Action
Octets: 1 1 6
Figure – 9-ddd – MAAD Response Action field format

## Slide 4: Options for consideration
AP could send unsolicited MAAD Response Action frame with allocated MAAD MAC address.
  AP can do this at any time while STA is associated.
  STA could advertise MAAD support, but need not.
  STA can use or ignore.
  Does mean that STA not initiating the scheme.
  Do we want this?
AP could embed something in MAAD MAC address for recognition purposes.
  Could be simple like a unique OUI
  Could be an embedded code
  AP could instantly know “STA is known”
  Nice, but out-of-scope

## Slide 5: ADVANTAGES
Simple – very simple - Easily implemented
  TA is still the identifier so easy to adapt Apps that have been used prior to RCM
  No crypto requirements,
  Action frame exchange can take place at any time whilst associated - does not form part of the association
No STA spoof possible
  TA changes every association
  3rd party cannot tell scheme in use (STA does not indicate support)
STA initiates (is in control) BUT AP allocates
  No duplications, easy opt-in opt-out for STA.
  STA can use same MAAD MAC across ESS.
AP can recognize STA pre-association
  MAAD MAC as TA in association requests and probes.
  AP can note from a directed probe that a known STA is within range (e.g. Home Use Case).
No calculations required other than AP generating a 48 bit address
Meets all the criteria for Use Cases