## Slide 1: TGbc: Resolution to CID 2074 (Second part) Date: 2022-02-15
Authors:
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
Xiaofei Wang | Interdigital |  |  | 

## Slide 2: Motivation
This is a continuation of the RNR presentation (DCN 249)
There has been several discussions within IEEE 802.11bc about mobility and how to handle STAs moving while receiving EBCS traffic
An EBCS traffic stream is identified by a Content ID which is local to the AP but unique and shared across APs sharing the same AP certificate.
In order to consume an EBCS traffic stream in current specification, from a different AP, an EBCs Info frame needs to be received from target AP.
  This may take some time
  How do we reduce this time?

## Slide 3: Explicitely indicating EBCS Services
An EBCS Content ID is unique per APs sharing same certificate
A certificate can be identified by
  Issuer name
  Serial number
We can signal in a compact way the services available at an AP and its certificate

## Slide 4: New element (Probe, Beacon)
 | Control | EBCS Content ID bitmap Length and Offset | EBCS Content ID bitmap | Length of Issuer Name | Issuer Name | Length of Serial number | Serial Number | Next EBCS Info frame TBTTs
Octets | 1 | 1 | variable | 0 or 1 | Variable | 0 or 1 | Variable | 0 or 2
 | Bitmap Offset | Bitmap Length
Bits | 4 | 4
Bitmap offset indicates the offset (e.g., the EBCS Content ID indicated in the most significant bit of the EBCS Content ID bitmap field), in units of two octets.
For example, when set to 0 it indicates that the most significant bit of the EBCS Content ID bitmap corresponds to EBCS Content ID 0. When set to 1, it indicates that the most significant bit of the EBCS Content ID bitmap corresponds to EBCS Content ID 16.
The Bitmap Length subfield, indicates the length of the EBCS Content ID bitmap field in octets +1.
Up to 128 Content ID simultaneously
EBCS Content ID bitmap contains a bit indicating per Content ID if it is available