## Slide 1: Emergency Preparedness Communication Service (EPCS*): Background and Proposal
Date: 2022-08-18
Authors:
*NSEP is renamed as EPCS (Emergency Preparedness Communication Service) in IEEE 802.11be

## Slide 2: Comment Resolution (CID#2319)
CID # | Comment | Proposed Resolution/Approach
2319 | National Security and Emergency Preparedness (NSEP) priority access feature is introduced in .11be amendment. Within United States, National Security and Emergency Preparedness Priority Service is deployed over Cellular and Wireline networks. Many other countries have similar services as well. While many of the existing deployment infrastructure includes Wi-Fi as last mile access, it lacks the priority access support. Therefore, it is important that NSEP priority access is also supported (e.g.. when the service is offloaded to Wi-Fi access, in particular as a part to 5G services) in current deployment. This will help service providers to provide a seamless NSEP service experience to the users while maintaining the priority and quality of service in Wi-Fi access networks. The proposal is to add the NSEP priority feature in REVme. This is viable because NSEP priority access is a MAC layer feature with no specific PHY dependencies and no reliance on 11be-specific features (e.g., MLO). | Specify NSEP features in REVme. Background of NSEP and a proposal are included in this document.

## Slide 3: Background: Priority Services*
    Emergency Telecommunications Service (ETS) is specified in [ITU-T E.107]: A national service, providing priority telecommunications to the ETS authorized users in times of disaster and emergencies (e.g., floods, earthquakes, hurricanes, terrorist attacks)
    In the United States, the DHS/CISA/ECD Priority Telecommunications Services⁺ programs provide National Security and Emergency Preparedness (NS/EP) and public safety users the ability to communicate using existing telecommunications networks during times of congestion
    Government Emergency Telecommunications Service (GETS)
    Wireless Priority Service (WPS)
    Next Generation Network Priority Services (NGN Priority Services)
    Telecommunications Service Priority (TSP)
  Priority Service in other countries
      Blue Light Mobile service in Belgium,
      Mobile Crisis Communications service in the Czech Republic,
      Mobile Telecommunications Privileged Access Scheme in Great Britain,
      Disaster Priority Telephone (優先電話) in Japan, and
      Wireless Priority Service (WPS) in Australia, and Canada.
* Priority Services differ from the citizen-to-authority type of Emergency Services (e.g. E911in the U.S.) the latter being available to any user.
.

## Slide 4: Background NS/EP Communications Overview in the United States
Commander-In-Chief
PRESIDENT
NATIONAL SECURITY
LEADERSHIP
NATIONAL ESSENTIAL FUNCTIONS
INDUSTRY
STATE & LOCAL
US POPULATION PARTICIPANTS
ALLIES
EMBASSIES
INTEL
Population Warning
Utility Services
Transportation
Food/Essentials Distribution
Threat Assessment and Attack Warning
C2 of Military Forces
Military Mobilization
Military Assist. To Civil Authorities
Worldwide Diplomacy
Worldwide Intelligence
Chief Executive
Head of State

## Slide 5: Background NS/EP Priority Services in the US
GETS
Landline Phone
Satellite Phone
Operational since 1994
Calling Card service
Accessible from any domestic or international PSTN phone.
WPS
Cell Phone
Operational since 2002
Accessible from a WPS subscribed phone of a participating carrier by dialing *272 + Destination Number
NGN PRIORITY
IP Networks
Priority Voice Core Operational: 2014 Wireless Access: 2017 Wireline Access: 2019
Priority Data, Video and Information Services (e.g., Multimedia Priority Service (MPS) in 5G, Wi-Fi): Work in Progress
NS/EP priority services are subscription based, operator controlled, enabled through global Standards, and are offered over commercial network infrastructure. The growing need for priority support over Wi-Fi access networks is currently missing.

## Slide 6: NS/EP Priority Services over Wi-Fi Access Networks Use Case
Disaster event occurs (e.g., Wildfire, Hurricane, Terrorist Attack)
  Network Infrastructure: Physical Damage and/or Congestion Overload
  Response requires coordination among field agents from federal, state, and local entities
    Command center established in a nearby enterprise conference room
    Cellular service in the conference room is poor/unavailable
    Field agents use enterprise’s managed Wi-Fi access network for communications
    Wi-Fi becomes congested with competing traffic
    Field agents invoke NS/EP Priority Service on enterprise’s Wi-Fi access network
    Wi-Fi priority access is enabled and field agents (authorized) obtain successful communications
To support the Priority Services in Wi-Fi networks, Priority Access to the medium is required

## Slide 7: Current Status EPCS in IEEE 802.11be
Emergency Preparedness Communications Service (EPCS) features have been defined in IEEE 802.11be as an on-demand capability that allows access points (APs) and authorized stations (STAs) to communicate with a higher priority
  Enhanced priority for access to the wireless medium
  The definition describes how service functions are negotiated with an Multi-Link Device

## Slide 8: Motivation for Introducing the Features into REVme
To satisfy the growing need to support Priority Services features in existing deployments (where possible via software/firmware updates)
  The issue is that there is no such technical specification existing today in the base IEEE 802.11 specification
This talk describes a proposal for adding Priority Access capabilities within REVme so that the stakeholders can enable the Service over existing deployments.

## Slide 9: Key EPCS Features
EPCS involves three primary features
  Advertisement: AP indicating support in Beacon/Probe Response and STA indicating support in Probe and (Re)Association Requests
  Enable/Teardown: AP or STA initiating process to turn priority functionality on or off
  Priority Access: STA makes use of dedicated EDCA parameters that provide priority in access in obtaining access to the wireless medium

## Slide 10: A Strawman Proposal to REVme in Support of EPCS
The initial proposal⁺ may address the following sub-clauses in REVme
  4.5 Overview of the services: Add sub-clause describing EPCS functionality
  6.3 MLME SAP interface: Add sub-clauses for EPCS-specific services
  9.6.3 QoS Action frame details: specify action frames to enable/tear down EPCS
  11 MLME: Add sub-clause to specify behavior necessary to support EPCS
Subsequent proposal may address several other REVme sub-clauses*
  3.1 Definitions and 3.4 Abbreviations and acronyms: define key EPCS terms
  9.4.1.9 Status Code field: Add EPCS-specific status codes to Table 9-78
  9.4.2.26 Extended Capabilities element: Add EPCS support element to Table 9-190
⁺ If the TG accepts adding the EPCS features, we can discuss and decide how to prioritize the effort to meet the REVme schedule
* May find additional sub-clauses as we progress

## Slide 11: Straw Poll #1
Do you support to incorporating Priority Access features into REVme?
Y:
  N:
  A:

## Slide 12: References
[1] IEEE P802.11be™/D1.5, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, Amendment 8: Enhancements for extremely high throughput (EHT)”, March 2022