## Slide 1: Harmonization for TGbf NDPA
Date: 2022-03-31
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | yan.xin@Huawei.com

## Slide 2: NDPA Issues
Format
  The same Frame Control field subtype as the 802.11 baseline NDPA
    The first two digits in Dialog Token field set to 00 (VHT)
    The first two digits in Dialog Token field set to 10 (Ranging)
  Different Frame Control field subtype from the 802.11 baseline NDPA
    Using the Control Frame Extension subtype
Parameters
  Is the Common Info field (or Special STA Info field) necessary?
    Size of the Measurement Set-up ID and Instance ID
    How to utilize 6 bit Dialog Token Number in the Dialog Token field
    I2R NDP TX Power, R2I NDP Target RSSI
  STA Info field
    Feedback Bandwidth, I2R N_STS, R2I N_STS
    Ng, Scale Factor, CSI FB Bit Size

## Slide 3: Format: Using the same subtype in the Frame Control field
STA Info # 1
STA Info # n
FCS
NDPA
Version
ID
MAC
Header
Sounding
Dialog
Token
Octets
:
1 Common Field (4 ?) 4?
4? 4?
Reserved
Disambi-
guation
B0
B11
Reserved
Measurement
Set-up ID
B0
(Ranging)
Bits
:
1 1 6
Sounding Dialog
Token Number
B2
B7
STA Info # 1
STA Info # n
FCS
Dummy
AID (?)
MAC
Header
Sounding
Dialog
Token
Octets
:
1 Common Field (4) ? 4
4 4
Measurement
Set-up ID
Disambi-
guation
B0
B11
B15
0 0
1 0
VHT NDPA based Sensing NDPA
Ranging NDPA based Sensing NDPA
B1
(HE)
Measurement Instance ID
Reserved

## Slide 4: Comparison: VHT NDPA based vs. Ranging NDPA based
 | Pros | Cons
VHT NDPA based Sensing NDPA | 11bit dummy AID is not necessary in the Common Info field Can be extended for future amendments through Version ID Any size of Common Info field and (or) the STA Info field is supported  Any size (multiple of 2 bytes) | The legacy 11ac, 11ax and new 11be devices need to parse the Sensing NDPA until the end of the frame Common field is required
Ranging NDPA based Sensing NDPA | Keeping the Ranging NDPA format unchanged | 11bits wasted for dummy AID in case of Common Info field HE devices only checks B1, so the legacy 11az, 11ax and 11ac devices need to parse the Sensing NDPA until the end of the frame A couple of bits are needed in every STA Info field for the Sensing NDPA indication Size of the STA Info field should be fixed to 4 bytes Size of the Common Info field should be a multiple of 4 bytes

## Slide 5: Format: Using the different subtype in the Frame Control field
The Control Frame Extension subtype in the Frame Control field shall set a TBD value in the Control Frame Extension subfield which is located immediately following the Subtype subfield in the Frame Control field to introduce a new NDPA Frame.
Name of the new NDPA Frame is TBD
In the new NDPA Frame, the Common field (corresponding to the Sounding Dialog Token field in the incumbent NDPA) may be larger than 1 byte and consist of NDPA Version subfield followed by Measurement Instance ID subfield
  Name of Common field is TBD
  Name and length of NDPA Version subfield is TBD
  Name and length of Measurement Instance ID subfield is TBD
  Size of the STA Info field is TBD
Frame
Control
STA Info # 1
STA Info # n
FCS
Duration
TA
Common Info field
RA
Octets
:
2 2 6 6 2? 4
4 4
NDPA Variant /
Bits:
8?
8?
Measurement Instance ID /
Measurement Set-up ID /
B0
B1
B2
B3
B4
B7
B8
B11
B12
B15
Protocol
Version
Type
Subtype
(0110)
Control
Frame
Extension
Power Management /
More Data /
Protected Frame / +HTC
I2R NDP TX Power/
R2I NDP Target RSSI

## Slide 6: NDPA Parameters
Parameters | Size (bits) | Description
Measurement Set-up ID | TBD | Common Info Field (?)
Measurement Instance ID | 6 | Dialog Token Number (Common Info Field)
Feedback Bandwidth | 9 | STA Info Field (?): Sub-channel Indication for Feedback with 20 MHz resolution and 40 MHz Resolution for 320 MHz
I2R N_STS | 3 | STA Info Field: Number of TX Streams
R2I N_STS | 3 | STA Info Field: Number of RX Streams
Ng | 2 | Measurement Set-up: Subcarrier size for feedback
Scale Factor | 1 | Measurement Set-up: Scale size for the normalization of CSI FB
CSI FB Bit Resolution | 2 | Measurement Set-up
I2R NDP TX Power | TBD | Common Info Field
R2I NDP Target RSSI | TBD | Common Info Field

## Slide 7: Proposal
We need two modes of NDPA available to accommodate both the EHT PPDU based NDP and Ranging NDP
  EHT NDP supports 320 MHz and Preamble Puncturing along with the extension of the Number of LTF Symbols
  Ranging NDP provides the R2I NDP format
We propose to use a New NDPA frame for the case the EHT NDP needs to be transmitted
  This New NDPA frame can be transmitted along with the Ranging NDP as well
    It may need more than 4 bytes in STA Info field (?)
We suggest to use the Ranging NDPA in case the Ranging NDP needs to be transmitted

## Slide 8: New NDPA frame
For the STA Info field (4 byte)
  AID (11 bits)
  Feedback Bandwidth (9 bits)
  I2R N_STS (3 bits)
  R2I N_STS (3 bits)
  Reserved (6 bits)
Frame
Control
STA Info # 1
STA Info # n
FCS
Duration
TA
Common Info field
RA
Octets
:
2 2 6 6 4 4
4 4
NDPA Variant /
Measurement Instance ID /
Measurement Set-up ID /
B0
B1
B2
B3
B4
B7
B8
B11
B12
B15
Protocol
Version
Type
Subtype
(0110)
Control
Frame
Extension
Power Management /
More Data /
Protected Frame / +HTC
I2R NDP TX Power/
R2I NDP Target RSSI/
Reserved
Control Frame Extension
  0000: Next Generation NDPA
  Name is TBD
  0001 ~ 1111: Reserved

## Slide 9: Reuse of Ranging NDPA
B26 and/or B31 indicates the Sensing NDPA
B0
(Ranging)
Bits
:
1 1 6
Sounding Dialog
Token Number
B2
B7
STA Info # 1
STA Info # n
FCS
AID:
2045
MAC
Header
Sounding
Dialog
Token
Octets
:
1 Special STA Info Field (4) 4
4 4
Measure-ment
Set-up ID
Disambi-
guation
B0
B11
B31
1 0
Ranging NDPA based Sensing NDPA
B1
(HE)
Measurement Instance ID
I2R NDP
TX Power
R2I NDP
Target RSSI
B10
B18
B19
B26
B27
B28
Sensing
Sensing
(Reserved)

## Slide 10: SP 1
Do you agree to support two modes of NDPA depending on the type of NDP PPDU?
  One mode of reusing the Ranging NDPA
  The other mode of the new NDPA Frame using the Control Frame Extension subtype in the Frame Control Field

## Slide 11: SP 2
Do you support the new NDPA frame using the Control Frame Extension subtype in the Frame Control field as shown in slide 8?

## Slide 12: SP 3
Do you agree to support reusing the Ranging NDPA for Sensing as shown in slide 9?

## Slide 13
from 11ax, P802.11ax D8.0
Appendix