## Slide 1: Stopping a Particular Responder in SBP
Date: 2022-04-27
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Need 1: Stop/pause/resume/add a particular responder
At a certain point in an SBP, the SBP initiator may find sensing measurements associated with a particular sensing responder to be problematic (e.g. CSI being too noisy, unstable, unreliable, faulty). To avoid wasting resources (TXOP usage and data bandwidth to transmit sensing results), the particular sensing responder needs to be stopped.
Sometimes, the problematic situation may be temporary. Instead of being stopped, the particular sensing responder needs to be paused, and then resumed later.
Sometimes, a newly introduced device needed to be added.
SBP initiator needs to be able to request the SBP responder (AP) to, and the AP needs to be able to,
  Stop sensing procedure with a particular sensing responder,
  Pause sensing procedure with a particular sensing responder,
  Resume sensing procedure with a paused sensing responder,
  Add sensing procedure with a particular sensing responder,

## Slide 3: Example: stop/pause/resume/add a particular responder
AP=Sensing Initiator
Sensing Transmitter
Sensing PPDU transmission
Optional CSI transmission
Use Case 1: Sensing by Proxy (SBP)
AP= sensing initiator/transmitter (SBP responder)
Non-AP STAs=sensing responder/receiver
A particular responder (e.g. noisy, unstable, unreliable, faulty) to be stopped/paused/resumed/ added
Non-AP STAs=
Sensing Responder
Sensing Receiver
SBP initiator
SBP request
AP=Sensing Initiator
Sensing Receiver
Use Case 2: Sensing by Proxy (SBP)
AP= sensing initiator/receiver (SBP responder)
Non-AP STAs=sensing responder/transmitter
A particular responder (e.g. noisy, unstable, unreliable, faulty) to be stopped/paused/resumed/ added
Non-AP STAs=
Sensing Responder
Sensing Transmitter
SBP initiator
A particular Sensing Responder to be stopped/ paused/resumed/added
A particular Sensing Responder to be stopped/ paused/resumed/added

## Slide 4: Straw Poll 1 (SP1)
Do you agree to add the following to SFD (and/or D0.1)?
“The SBP initiator should be able to request to, and the SBP responder (an AP) should be able to, stop a sensing procedure with a particular sensing responder.”
Yes
No
Abstain

## Slide 5: Straw Poll 2 (SP2)
Do you agree to add the following to SFD (and/or D0.1)?
“The SBP initiator should be able to request to, and the SBP responder (an AP) should be able to, pause a sensing procedure with a particular sensing responder, and resume a sensing procedure with a paused sensing responder.”
Yes
No
Abstain

## Slide 6: Straw Poll 3 (SP3)
Do you agree to add the following to SFD (and/or D0.1)?
“The SBP initiator should be able to request to, and the SBP responder (an AP) should be able to, add a sensing procedure with a particular sensing responder.”
Yes
No
Abstain