## Slide 1: TG bh MAAD MAC Outline
Date: 2022-06
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Introduction - 1
TGbh Straw Poll indicated a good majority support for a scheme that satisfied all the Use Cases including pre-association, but still had a sizable anti-vote
Subsequent follow up has revealed some misunderstandings of the MAAD scheme and some encouragement to keep going
MAAD is very simple, requires no computations or calculations
MAAD - Network designates the identity
IRMA – STA provides the identity

## Slide 3: Introduction - 2
MAAD - MAC Address Designation
MAAD MAC has been presented a few times, but it has been realized, based upon questions I have received, that the details are still somewhat not understood by several.
MAAD satisfies all Use Cases as it uses the MAC address as the identifier, but this is only known by the AP.
This Outline’s objective is to try to make it clear that MAAD MAC scheme is simple, secure, and an apt solution for TGbh.
Text is in 22/0427r6

## Slide 4
BASICS:
MAAD MAC Both STA and AP advertise support
AP assigns a new MAAD MAC address at every RSN association
STA uses that NEW allocated address the NEXT time it associates
  New MAC Address EVERY Association
  Cannot be followed
AP recognizes STA pre-association
  AP “knows” the MAC Address
Reassociation uses MAC address used for the association
  Must, that’s the rule
  No problem if new address is allocated.
STA can use ANQP and pre-association “as usual”
  the MAC address is known/recognized by the AP.

## Slide 5: Outline
AP and STA show support for MAAD in Extended Capabilities
STA associates first time using 4 W HS
A MAAD MAC Address sent by AP in EAPOL-Key msg 3/4 (as per NG ID)
  AP and STA store the allocated MAAD MAC for that STA/AP
When STA comes back it uses that previously allocated MAAD MAC Address as TA
AP instantly recognizes the STA from TA in Association Request etc.
  AP can identify the STA pre-association – ANQP and directed probes
STA Associates using the allocated MAAD MAC as TA
At association, AP provides new MAAD MAC address in EAPOL-Key msg 3/4
  New MAC Address used for the NEXT association.
NOTES (as per network generated device ID):
For FILS new MAAD MAC address is received in Association Response frame
For FT new MAAD MAC address is received in EAPOL-Key msg 3/4, but not during the FT protocol reassociations within the same ESS

## Slide 6: ADVANTAGES
SECURE - TA changes every time, and is identified only by the AP
  STA cannot be tracked
TA can be identified pre-association
Existing Apps, affected by RCM, can be easily adapted (a true TGbh solution)
  Applications as per Use Cases use the MAC Address as identifier
  MAC address again used BUT ONLY THE AP KNOWS IT.
SIMPLE – NO COMPUTATIONS or CALCULATIONS
No link between a STA ID and the (changing) MAC Address.
From outside, MAC Address is Random
AP and STA just store the latest MAAD MAC allocation
No calculations!!

## Slide 7: Comparisons
MAAD
  AP allocates the Address
  No computations
  Address included in every msg 3
  Probes use same address
IRM
  STA controls its address
  Computations required
    IRMK Check reduces number of computations
  IRMK included in every msg 4
  Probes use different address every probe

## Slide 8: Straw Polls
Do you agree that TGbh should have solution(s) for pre-association Use Cases?
Yes/No/Abst
Do you agree that TGbh should have a solution where the STA controls the identity?
Yes/No/Abst

## Slide 9: Straw Poll/MOTION
Do you agree that the MAAD scheme, as described in <this document> (text is in 22/0427r6), is included in the TGbh Amendment?