## Slide 1: TG bh Identifiable Random MAC Address (latest)
Date: 2022-06
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This is a presentation on “Identifiable Random MAC Address”, IRMA
TGbh Straw Poll indicated a good majority support for a scheme that satisfied all the Use Cases including pre-association, but still had a sizable anti-vote
Subsequent follow up has revealed some misunderstandings of the IRMA scheme and some encouragement to keep going.
This new proposal removes the need for Robust Action frames and sends the IRMK in message 4 of the 4 w HS.
IRM is a STATION allocated scheme. STA has control over the MAC Address used.
Note that
MAAD is a NETWORK allocated scheme. Network allocates the MAC address to be used (changes every association)
BOTH schemes cover all the Use Cases.

## Slide 3: IRM Definitions
  Identifiable Random MAC (IRM) : a scheme where a non-AP STA uses identifiable random medium access control (MAC) addresses (IRMA) to prevent third parties from tracking the non-AP STA while still allowing trusted parties to identify the non-AP STA.
Identifiable Random MAC Address (IRMA) – a random MAC address used by a STA using IRM
Identifiable Random MAC Key (IRMK) – a Key used to resolve an IRMA

## Slide 4: CAPABILITY BIT
An IRM Capability field is used in the STA and AP
The AP looks for the IRM Capability AND the IRM Hash in IRM element
AP can use the IRM Capability bit to indicate to STAs that there may be a reason to be identified, i.e., “I provide a service”

## Slide 5: IRM element
STA can use “private” address
IRM element sent in Association Request
AP then knows if STA IRMK already known (stored) or not
Thinking about adding indicators such as “ID”. Tells AP STA has an ID.

## Slide 6: Outline
STA uses a random MAC address, IRMA, and a ‘IRM Hash’ (or IRM OKM)
  STA uses a key , IRMK, that it provided to the AP at the last association.
  IRM Hash = function {IRMA, IRMK}
Every time the STA associates, the STA provides a new key, IRMK.
AP identifies STA by checking the stored IRMKs.
An IRMK Check can be used to reduce the list of keys that AP checks by a factor of 256.

## Slide 7: Basic Steps for IRM
STA and AP indicates IRM support in Extended Capability Field
First Time Association
STA generates 48 bit IRMA
  Generates a random 46 bit number
  Appends I/G = 0, U/L = 1 (Compatible with 12.2.10)
STA sends the IRM element in Association Request
  IRM Indicator set to “Unknown”
  IRM OKM field is omitted.
During Association, STA sends an IRMK in message 4
  AP stores this IRMK

## Slide 8: STA Associates again
Subsequent Associations
STA generates 48 bit IRMA
STA calculates IRM OKM using the IRMA and the IRMK previously provided to that AP
  IRM OKM= HKDF-Expand (IRMK, IRMA, 9)
STA sends the IRM element in Association Request
  IRM Indicator set to “Known” and IRM OKM is included
  IRM Check field may be included (Down-selects IRMK list by factor of 256)
AP uses IRMA and stored IRMKs to calculate IRM OKM and identifies the STA IRMK.
During Association STA sends a new IRMK to AP in msg 4
  For use the NEXT TIME the STA associates or probes
AP and STA update their lists.

## Slide 9: Pre-Association
Identification from Association Request:
  AP can identify the STA from the Association Request
  AP can decide if STA is a ‘wanted STA’ and allow association
  When STA associates, the IRMK is changed
Identification from Probes
  STA can send a different IRMA (TA) and plus IRM OKM, every probe (based on same IRMK)
  When STA associates, the IRMK is changed
ANQP
  IRM element includes IRM OKM and IRM Check
  Hence STA can be identified

## Slide 10: Important Points
STA uses a different MAC Address for every association
STA uses a different MAC address for every directed Probe
Brute strength decoding of the IRMK is a waste of time as the IRMK changes EVERY ASSOCATION
  Impossible to track a STA.
Effectively the MAC address is the “identifier” BUT only known by the AP.
  Makes adoption by existing Apps easy.

## Slide 11: STA details and Storage
IRM enables the AP to identify the STA,
  i.e. STA “123”
AP can exchange frames or higher layer APP can then associate STA 123 with some other specific details/IDs
  Membership ID , customer ID, guest ID, family member, employee ID, etc.
  AP stores 9 octets for the IRMK for each STA.

## Slide 12: Straw Poll/Motion
Do you agree that an Identifiable Random MAC scheme, along the lines as described in <this document>, is included in the TGbh Amendment?

## Slide 13: IRMK and IRM OKM function
IRMK (Identifiable Random MAC Key)
STA generates the IRMK
  Random 72-bit number .
STA provides an IRMK with AP when first associated
STA provides IRM OKM in “IRM element”
The IRMK is used to resolve the identity of the STA
  verifies that the OKM included in the IRM element matches the output of the local OKM computation
  IRM OKM= HKDF-Expand (IRMK, IRMA, 9)
  This produces a 9 octet, 72 bit, output key
Alternative is use IRM hash = SHA-256/128 (IRMK, IRMA)
OR any other candidate (not my area of expertise, happy to accept advise)
NOTE: Only the HKDF-Expand is used because the IRMK is already a “good” pseudorandom key. i.e. the HKDF-Extract is not required.
NOTE: 72 bit key is considered secure enough for this application. Only real need is to prevent duplicates. Determining the key is not useful as it changes every association.

## Slide 14: IRMK Check field
IRMK Offset takes a value N, from 0 to 56 (Note: IRMK is 72 bits)
The Check field contains the 8 bits representing the EX-OR of the 8 bits of the IRMK, bN to bN+7 with the following 8 bits (bN+8 to bN+15)
i.e. For n = 0 to 7
Bits in Check field are bn = EX-OR (bN+n, bN+n+8) where bN is Nth bit in IRMK
Note: Could keep it simpler by just providing 8 bits of the key. Same basic integrity.
Acts as a “Hint” to the AP so AP can quickly find a stored IRMK.
Reduces the list of IRMKs by 1/256
e.g. correct key in a list of 1000 IRMKs found in just 2 calculations (average)
Reduces the integrity of key from 72 bits to 64 bits.
Brute force determination of the key is a waste of time as key changes every association – cannot track the STA.