## Slide 1: Enhancements for massive TSN
Date: 06-07-2022
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP RAS |  |  | 
Dmitry Bankov | IITP RAS |  |  | 
Ilya Levitsky | IITP RAS |  |  | 
Kirill Chemrov | IITP RAS |  |  | 

## Slide 2: TSN with 802.11be
According to PAR:
Users expect improved integration with Time Sensitive Networks (TSN) to support applications over heterogeneous Ethernet and Wireless LANs. This amendment aims to build on the current and emerging WLAN technologies by providing further improvement of aggregate throughput and latency to ensure competitiveness of IEEE Std 802.11 in coming years.
Does 11be really support integration with TSN?
The main feature of 802.11be for TSN is RTWT,
Initially designed for low-power operation
Requires auxiliary mechanisms to work with legacy devices
Optional support
Too heavy and not suitable for massive real-time transmissions of short packets

## Slide 3: Industrial Automation is a killer APP for TSN
High Reliability: 0.99..9
Short packets: 10s of bytes
Dozens of STAs connected to an AP
Low delays: <1ms
No Jitter: <10us
Although 5G targets 1ms delays, by now, it is not able to satisfy these requirements because of design limitations, but Wi-Fi has no such drawbacks

## Slide 4: Current Status in 802.11be
100 sensors
10 byte (in UL & DL) per device per cycle
Video 5Mbps each
AP
Many solutions proposed are left out of consideration or optional, which complicates support of industrial internet applications and guaranties in delays
High time granularity of channel reservation mechanism (e.g., Quiet Element: 1 ms) is not efficient for short packet transmission
The overhead to transmit a short packet is huge.
  At least SIFS+Preamble+MAC header+CRC
  The headers in new standards are long
    802.11ah designed a short packet format (PV1), but it works only in S1G with long timing.
Mac overhead = 34+10 byte (including QoS+HT) = 45.3+13.3 us = 64us @MCS5 (6 Mbps in 26 tone)
PHY + Protocol overhead = 40 us (Preamble) + TF +ACK + 2 SIFS + DIFS >106us+TF+Multi STA BA
Effective rate in UL = 370 bytes per >250 us = 12Mbps in 80MHz channel @MCS5 (too low!)

## Slide 5: Example
≈1 380us
≈468 us
The approach proposed in this submission
DL DATA
MU-RTS
CTS
16
16
16
200
UL DATA
16
200
DL DATA
16
200
UL DATA
16
200
DL DATA
16
200
UL DATA
200
DATA
IRTS
CTS
16
16
104
16
ACK+DATA (x3)
88
88
88
2
2
*MCS3
Existing approaches

## Slide 6: Key Ideas
For repetitive traffic patterns, we can avoid the same repeating overhead in procedures
  Introduce I-TXOP during which special short frames are only transmitted with scheduled access
  Squeeze overhead by removing useless headers and repetitive information, i.e., send repetitive information only once
Short or removed interframe space
IMPDU as a type for aggregation for multiple receivers within a common codeword
Observation: Industrial Wi-Fi does not need MU-MIMO and DL OFDMA

## Slide 7: A possible scheme for industrial frame exchange
NAV .
IRTS
CTS
SIFS
IMPDU
IMPDU
IMPDU
IMPDU
IMPDU
0 ≤ xIFS <SIFS
PHY HEADER
MAC Header
Data + Check Sum
Industrial-TXOP .
I-TXOP .
I-TXOP .
Legacy operations
Legacy operations
IMPDU
IMPDU
IMPDU

## Slide 8: IMPDU format
 | Header | Payload | FCS | … | Header | Payload | FCS
Octets: | 2 | Length | 4 |  | 2 | Length | 4
The header contains only
Sequence Number (12 bits)
Immediate ACK bit (1 bit) – acknowledges the reception of the previous frame scheduled for the STA
Reserved (3 bits)
RX address, TX address, the number of MPDU within IMPDU are determined by the schedule

## Slide 9: Schedule
A list mapping an offset time to a scheduled frame info
Offset time is measured from the end of CTS (or the end of the previous schedule if several schedules are used within ITXOP)
The schedule can be sent via the IRTS frames.
Offset
Frame info
Frame #0
Offset
Frame info
Frame #1
Offset
Frame info
Frame #n
…
Schedule
2
2
2
variable
variable
variable
Octets:
9

## Slide 10: Example of using a schedule
Offset #0 Frame #0
Offset #1 Frame #1
Offset #4 Frame #4
NAV .
IRTS
SIFS
IMPDU
IMPDU
IMPDU
Offset #2 Frame #2
Offset #3 Frame #3
IMPDU
(destined for multiple sensors)
SIFS
IMPDU
IMPDU
SIFS
(“BA” for multiple sensors)
Schedule #1
Schedule #1
The schedule is broadcasted via IRTS frames.
Frame #0 offset
Frame #1 offset
CTS
SIFS

## Slide 11: Scheduled frame info template
Not used
Let us try to reuse User info field of the Trigger frame
Used only
for OFDMA MU
Not used
Only N_SS

## Slide 12: Scheduled Frame Info
*For RU Allocation see Table 9-29i
802.11ax D8.0
 | DL=1 | Number Of User Fields | N of SS | MCS | FEC | RX AID12 | Type | Length | … | RX AID12 | Type | Length
Bits: | 1 | 7 | 3 | 4 | 1 | 12 | 4 | 16 |  | 12 | 4 | 16
common
per user
 | DL=0 | Number Of User Fields | RX AID12 | TX AID12 | Type | MCS | *RU Allocation | Length | N of SS | FEC | UL Target Receive power (TBD) | … | RX AID12 | TX AID12 | … | … | FEC | UL Target Receive power (TBD)
Bits: | 1 | 7 | 12 | 12 | 4 | 4 | 8 | 16 | 3 | 1 | 4 |  | 12 | 12 |  |  | 1 | 4
Note 1: for Groupcast frames, Groupcast AIDs are needed
DL
UL
16 32
8 64
A per user info may repeat multiple times (with the same RU Allocation) to signal that multiple MPDUs for the receiver are present.
Data, Data+ACK, BlockAck, etc.
Octets

## Slide 13: Schedule broadcast in beacons
The schedule is broadcasted via beacons. A beacon has one or several Schedule IEs, each containing one schedule.
 | Schedule ID | Duration | Schedule
Octets: | 1 | 2 | variable
 | Element ID | Length | Schedule Info
Octets: | 1 | 1 | variable
Schedule ID can be from 1 to 127
Schedule ID = 0 is used for ad hoc schedule

## Slide 14: IRTS frame format
The schedule can be sent in IRTS.
It is a Control frame
As for 802.11be, there are three Control Subtypes left: 0000, 0001, 1111.
Address 1 is a group address of multiple sensors that will response to IRTS with a synchronous CTS.
Address 2 is the address of the STA sending the IRTS (we assume that IRTS are sent by the AP)
Tetrapartial Timestamp is included for synchronization
Tetrapartial Timestamp field contains the value of the 4 least significant octets of the STA’s TSF timer at the time that the start of the data symbol containing the first bit of the Tetrapartial Timestamp field appears at the transmit antenna connector.
 | Frame Control | Duration/ID | Address 1 | Address 2 | Tetrapartial Timestamp | Schedule | FCS
Octets: | 2 | 2 | 6 | 6 | 4 | variable | 4
Tetrapartial Timestamp inspired by 802.11-2020, 9.8.4.2 STACK frame format

## Slide 15: IRTS (cont’d)
IRTS triggers one or several schedules defined in beacons (so the AP can combine multiple schedules in one TXOP)
  IRTS can still define an ad hoc schedule (ID = 0), which will not be stored for future.
  IRTS can also define a new schedule (with ID>0) on the fly
    It is useful if the AP needs to update a schedule before the next beacon, and then to reuse it
 | Schedule Present + ID | Duration | Schedule
Octets: | 1 | 0 or 2 | variable
 | Schedule Present | Schedule ID
Bits: | 1 | 7
The IRTS frame format contains Schedule Info.
  If Schedule Present is 1
      If Schedule ID is 0, the schedule is ad hoc
      Otherwise, the schedule shall be remembered
  If Schedule Present is 0
      Schedule ID shall contain a valid identifier
      The Duration and Schedule field are absent
 | Frame Control | Duration/ID | Address 1 | Address 2 | Tetrapartial Timestamp | Schedule Info list | FCS
Octets: | 2 | 2 | 6 | 6 | 4 | variable | 4
Schedule Info | Schedule Info
…
Schedule Info

## Slide 16: Example of Multiple schedules in one TXOP
NAV .
IRTS
Frame #0
Frame #1
Frame #4
Frame #2
Frame #3
Schedule #1
Schedule #1, #1
Frame #0
Frame #1
Frame #4
Frame #2
Frame #3
Schedule #1
CTS

## Slide 17: Summary
In case of quasi-periodic traffic of multiple STAs
  We do not need to start every UL MU TXOP with full TF (the TF can be compressed as all parameters are exchanged in advance)
  We do not need to have full PHY and MAC headers of the frames
  More flexible packet/frame aggregation
  Shorter interframe spaces thanks to no need to wait for the end of the frame

## Slide 18: Straw Poll
Do you agree that the support of Industrial TSN Applications for multiple STAs shall be provided by
Further TGbe activities
More Discussion within WNG
Need more info
Abstain