## Slide 1: Discussion on Connection between AI/ML & Wireless LAN
Date: 2022-07-11
Authors:

## Slide 2
Abstract
In this contribution, we discuss how Artificial Intelligence (AI)/Machine Learning (ML) can connect with WLANs

## Slide 3: Introduction
AI/ML has been extensively studied in academia and industry and found its way into many different scientific fields [1], [2]
  3GPP Release 18 will study AI/ML for NR air interface to enhance performance or reduce complexity/overhead [3]
The 802.11 specifications have been regularly updated with more demanding requirements and new features
  Next generation of Wi-Fi may require higher throughput (>100 Gbps [4], > 2x 11be [5]), lower latency (<=1ms [4] ), extra reliability (> 99.999999% [6], [7], [8])
  Multiple generations of Wi-Fi network with different applications need to co-exist efficiently
How can AI/ML connect with 802.11?

## Slide 4: Study Topics of Connection Between AI/ML and WLAN
Different topics about AI/ML vs WLAN have been extensively studied and summarized in [1] [2] [9]
The main topic areas include
  Topic 1: Using AI/ML to improve IEEE 802.11 features
    Better one specific feature or jointly optimize multiple features across layers [1] [2]
    Optimize the use of WM resources for individual BSS’s, ESS’s, and multiple BSS/ESS interactions
  Topic 2: Creating a communication efficient wireless network to facilitate AI/ML implementation
    802.11 protocol may need to be updated to facilitate the data sharing (Distributed ML) or model parameters sharing (Federated Learning) between AP(s) and non-AP STAs [9]
  Topic 3: Deploying AI/ML enabled structure to optimize 802.11 network slicing
    Network slicing in 802.11 networks - meet the diverse set of requirements for multiple applications under a flexible infrastructure [10]

## Slide 5: AI/ML Enhanced Wi-Fi Features - AI/ML on AP and Non-AP STAs
Use cases:
  CSI feedback enhancement [1], [11], [12]
    AI/ML technology can be used for the enhancements of different CSI feedback types
    More details will be discussed later
  Single link optimization [1]
    Rate selection (MCS, MIMO mode and BW) – monitoring the service time ratio of an A-MPDU, improved SNR prediction
  Access optimization
    CW optimization – reducing both collisions and idle time periods to maximize the throughput [1]
  Multi-link optimization
    Traffic distribution among different links, e.g., 5 GHz and 6 GHz [1]
In above use cases, AP and Non-AP STAs may perform the AI/ML algorithm independently

## Slide 6: AI/ML Enhanced Wi-Fi Features - Study Scope
Use case: Identify a list of use cases (e.g., one or two) as the preliminary study of AI/ML enhancement of Wi-Fi features
Framework: Unify the structure of AI/ML implementation
  AP side only or all STAs or non-AP STAs only
KPI metric: Define an KPI metric or KPI metrics to evaluate an AI/ML enhanced WiFi feature
  Different WiFi features may need different KPI metrics
AI/ML algorithm types: Select one AI/ML algorithm type (e.g., supervised, unsupervised or reinforcement learning) to compare different proposals
  An AI/ML algorithm may need to be implemented among different STAs to get fair access to the channel, e.g., CW optimization

## Slide 7: One Example of AI/ML Enhanced WLAN Features - CSI Feedback Enhancement
CSI feedback enhancement, e.g., overhead reduction, improved accuracy/prediction, has been identified as one of the initial AI/ML study cases in 3GPP Release 18 [3]
ML/AI enabled CSI feedback in Wi-Fi:
  One potential solution is to use an index-based CSI [11]or compressed CSI feedback scheme [12] via real time or offline training
    Reduced overhead may lead to higher sensitivity to the CSI accuracy
  Possible standardization area:
    Uniform CSI compression algorithm
    Singling candidate CSI vector set

## Slide 8: Example of AI/ML Enabled Index Based CSI Feedback Scheme - Intelligent Feedback Overhead Reduction (iFOR) via Online Learning [11]
Phase 1 – CSI ML Training Phase: Algorithms such as K-means clustering enable choosing a set of number of candidate CSI feedback vectors, each of which contains index values of quantized {𝝓} and {𝝍 } per subcarrier group
Phase 2 – Index-based CSI Reporting Phase: Non-AP STA only needs to report the index of the selected vector among the candidate vector set after AP distributes the CSI candidate vector set

## Slide 9: Example of AI/ML Enabled Index Based CSI Feedback Scheme - Intelligent Feedback Overhead Reduction (iFOR) using Offline Training [11]
CSI Offline Training: Algorithms such as K-means clustering enable choosing a set of number of candidate CSI feedback vectors, each of which contains index values of quantized {𝝓} and {𝝍 } per subcarrier group; AP broadcasts Nk candidate vectors to associated non-AP STAs.
Index-based CSI Reporting: Non-AP STA only needs to report the index of the selected vector among the candidate vector set

## Slide 10: Summary and Way Forward
Discuss the possible study topics on how AI/ML interacts with WLAN
Focus on the topic on how AI/ML improves Wi-Fi features
  List multiple uses cases of AI/ML enhanced Wi-Fi features
  Discuss the potential impact on 802.11 specs
  Present CSI feedback reduction as one example of AI/ML enhanced feature and illustrate the framework of AI/ML deployed in WLAN to reduce CSI feedback
Way forward
  Identify the list of use cases
  Unify the simulation baseline and reference model
  Define the evaluation metric(s)

## Slide 11
References
[1] S. Szott, K. Kosek-Szott, P. Gawłowicz, J. T. Gómez, B. Bellalta, A. Zubow, F. Dressler, “WiFi Meets ML: A Survey on Improving IEEE 802.11 Performance with Machine Learning”, IEEE Communications Surveys & Tutorials
[2] M. Kulin, T. Kazaz, I. Moerman, E. de Poorter, “A Survey on Machine Learning-Based Performance Improvement of Wireless Networks: PHY, MAC and Network Layer,” Electronics. 2021; 10(3):318.
[3] 3GPP TR, 38.843, “Study on AI/ML for NR air interface”
[4] 11-22/0030, Look ahead to next generation
[5] 11-22/0032, Next Gen After 11be
[6] 11-22/0694, Thoughts on Next Gen WLAN
[7] 11-22/0729, 802.11 GEN8 Study Group
[8] 11-22/0708, Beyond ‘be’ – Proposed Next Step
[9] H. Hellström, J. M. B. Silva Jr., M. M. Amiri, M. Chen, V. Fodor. H. Vincent Poor and C. Fischione, “Wireless for Machine Learning: a Survey” https://arxiv.org/pdf/2008.13492.pdf
[10] S. d. Bast, R. Torrea-Duran, A. Chiumento, So. Pollin, H. Gacanin, “Deep Reinforcement Learning for Dynamic Network Slicing in IEEE 802.11 Networks”, IEEE Inforcom, April 2019
[11] M. Deshmukh, Z. Lin, H. Lou, M. Kamel, R. Yang, I. Güvenç, “Intelligent Feedback Overhead Reduction (iFOR) in Wi-Fi 7 and Beyond,” in Proceedings of 2022 VTC-Spring
[12] P. K. Sangdeh, H. Pirayesh, A. Mobiny, H. Zeng, “LB-SciFi:Online Learning-Based Channel Feedback for MU-MIMO in Wireless LANs, ” in Proceedings of 2020 IEEE 28th ICNP