## Slide 1: Requirement for Changing TSF
Date: 2022-07
Authors:

## Slide 2: Background
The Time Service Function TSF Field is transmitted in the (regularly transmitted) beacon
The TSF Field can be used to track an AP across changes to BSSID
  Observe beacons transmitted immediately before and after changing BSSID
    Record the value difference between the TSF values in beacons.
    Record the time difference between the transmission of the beacons.
  If the value difference matches to the time difference, then the two transmissions can be assumed to be from the same AP.
The above issue can be mitigated by changing TSF by random value whenever BSSID changes

## Slide 3: Proposed a New Requirement Related to Issue 6 Mobile AP privacy
 | Requirement | Issue | Status | Information
40a | 11bi shall define a mechanism for a BPE AP to change the OTA TSF (e.g., the TSF that is transmitted in the beacon) by a random value when its OTA BSSID is changed. | I6 | Approved for Motion (7/12/2022) |