## Slide 1
Triggered TXOP Sharing Error Recovery
CID 12420
Date: 2022-09-12
Authors:
Name | Affiliation | Address | Phone | Email
Sunghyun Hwang | ETRI |  |  | shwnag@etri.re.kr
Kyumin Kang | ETRI |  |  | kmkang@etri.re.kr
Juseong Moon | KNUT |  |  | jsmoon0211@ut.ac.kr
Ronny Yongho Kim | KNUT |  |  | ronnykim@ut.ac.kr

## Slide 2: Introduction
Triggered TXOP sharing procedure is defined in the Draft 2.1.1 [1].
  The Triggered TXOP sharing procedure allows an AP to allocate a portion of the time within an obtained TXOP to only an associated non-AP EHT STA for transmitting one or more non-TB PPDUs.
AP’s procedure during or after TXOP sharing is defined but a non-AP STA’s procedure using a shared TXOP is not fully defined.
CID 12420 addresses the error recovery issue
  In Triggered TXOP Sharing, error recovery method by a non-AP STA is not defined. Since the non-AP STA is not a TXOP holder in the shared TXOP, when the intended receiver of the non-AP STA doesn't respond, the transmission can not be recovered and medium may be released. An appropriate error recovery mechanism like PIFS recovery needs to be defined.
In this contribution, non-AP STA’s error recovery in triggered TXOP sharing is discussed.

## Slide 3: CID 12420
12420 | Yongho Kim | 35.2.1.2.3 | 402.30 | In Triggered TXOP Sharing, error recovery method by a non-AP STA is not defined. Since the non-AP STA is not a TXOP holder in the shared TXOP, when the intended receiver of the non-AP STA doesn't respond, the transmission can not be recovered and medium may be released. An appropriate error recovery mechanism like PIFS recovery needs to be defined. | Please make the follwoing changes in order to clarify the error recovery mechanism of a non-AP STA during a TXOP sharing period. During the time allocated by an associated AP, the non-AP EHT STA may transmit non-TB PPDUs to the AP or another STA if the TXOP Sharing Mode subfield value is 2. The non-AP EHT STA may perform the PIFS recovery as described in 10.23.2.8 when the non-TB PPDU is not properly transmitted. The non-AP EHT STA may transmit a QoS Data or QoS Null frame to an associated AP to terminate the allocated time, if the RDG/More PPDU subfield in CAS Control subfield of the HE variant HT Control field is equal to 0. NOTE 1--For example, the other STA can be a peer STA of a peer-to-peer link. During the time allocated by an associated AP, the non-AP EHT STA may transmit non-TB PPDUs and only to its associated AP if the TXOP Sharing Mode subfield value is 1. The non-AP EHT STA may perform the PIFS recovery as described in 10.23.2.8 when the non-TB PPDU is not properly transmitted.

## Slide 4: Non-AP STA’s error recovery issue in triggered TXOP sharing
In case of transmission error of the non-AP STA (both mode 1 and 2), non-AP STA’s behavior is not defined in Draft 2.0.
  When the intended receiver of the non-AP STA doesn't respond, the transmission can not be recovered and medium may be released.
  Since the non-AP STA is not TXOP holder, the non-AP STA is not able to perform PIFS recovery.
How to recover error?

## Slide 5: Non-AP STA’s error recovery in mode 1
Error recovery similar to PIFS recovery can be considered.
  TXOP acquisition requirement of PIFS recovery can be relieved for triggered TXOP sharing.
  When there is no response to the non-AP STA1’s data frame for PIFS, the non-AP STA1 can retransmit the data frame.

## Slide 6: Non-AP STA’s error recovery in mode 2
Error recovery similar to PIFS recovery can also be considered for mode 2.
  TXOP acquisition requirement of PIFS recovery can be relieved for triggered TXOP sharing.
  When there is no response from the non-AP STA2 for PIFS, the non-AP STA1 can retransmit the data frame.

## Slide 7: Conclusion
How to recover an error during the shared TXOP is not defined for triggered TXOP sharing in the Draft 2.0.
Since the non-AP STA is not a TXOP holder in the shared TXOP, when the intended receiver of the non-AP STA doesn't respond, the transmission can not be recovered and medium may be released.
In this contribution, error recovery procedure similar to PIFS recovery is proposed.

## Slide 8: Reference
[1] Draft P802.11be D2.1.1