## Slide 1
End time alignment of Sync PPDUs medium access - CID 12415, 12426, 12431
Date: 2022-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Ronny Yongho Kim | KNUT |  |  | ronnykim@ut.ac.kr
Juseong Moon | KNUT |  |  | jsmoon0211@ut.ac.kr
Hyojin Jung | Hyundai Motor Company |  |  | hyojin@hyundai.com

## Slide 2: Introduction
Start time sync PPDUs medium access is defined in the Draft 2.0 [1].
  Each STA of an MLD operating on a pair of NSTR links for that MLD that aligns the start times of the PPDUs scheduled for transmission on more than one link shall ensure that the EDCA rules on each link permit access to the medium on all the links at the time of issuance of the PHY-TXSTART.request for each link.
However, end time alignment requirement of start time sync PPDUs medium access is not defined (CID 12415).
  End time alignment by non-AP STA is also needed in case of non-AP STAs' sync transmission. If end time is not aligned, APs' BA frames reception can be interrupted. Clear description on the end time alignment of sync transmission needs to be added.
When the end time alignment is adopted, there is more efficient way(e.g, Multi-TID A-MPDU) to use the resource than padding (CID 12426).
  Because end time shall be aligned in case of non-AP STAs' sync transmission, MPDU transmitted on one link might need padding to align the end time with the other link's transmission. Mult-TID A-MPDU with the TID of the selected EDCAF and the other TIDs whose backoff counter reached zero is more efficient than just padding. In order to allow flexibility in forming multi-TID A-MPDU with different ACs, multi-TID A-MPDU construction rule needs to be eased to construct multi-TID A-MPDU regardless of AC priority.
When the end time alignment is adopted and 8us margin is allowed in the end time alignment, PIFS recovery can not be used (CID 12431).
  In UL synched PPDU transmission, after successful TXOP setup, PIFS recovery can be performed for the consecutive frame in one of the NSTR links. Since 8us margin is allowed in end time alignment, retransmitted data with PIFS recovery may collide with BA on the other link. A solution to this issue needs to be defined.

## Slide 3: End time alignment of start time sync PPDUs medium access
In start time sync PPDUs transmission, there is no requirement on end time alignment.
If end time is not aligned, BA may not be correctly received due to NSTR interference from the other link as shown in the figure below.
End time of start time sync PPDUs transmission can be aligned with padding.

## Slide 4: End time alignment of start time sync PPDUs medium access
Multiple EDCAF backoff counters can reach zero and one of them can be selected for start time sync PPDUs transmission.
  A STA that chooses not to transmit after the backoff counter reached zero on a link of NSTR link pair may have one or more EDCAF backoff counters with value zero on that link. The STA that initiates transmission on that link following condition a) or b), and has one or more EDCAF backoff counters that already reached zero shall choose only one implementation specific EDCAF for the transmission.
In end time alignment, there is more efficient way(e.g, Multi-TID A-MPDU) to use the resource than padding (CID 12426).
  Because end time shall be aligned in case of non-AP STAs' sync transmission, MPDU transmitted on one link might need padding to align the end time with the other link's transmission. Mult-TID A-MPDU with the TID of the selected EDCAF and the other TIDs whose backoff counter reached zero is more efficient than just padding. In order to allow flexibility in forming multi-TID A-MPDU with different ACs, multi-TID A-MPDU construction rule needs to be eased to construct multi-TID A-MPDU regardless of AC priority.

## Slide 5: End time alignment of start time sync PPDUs medium access
If the end time of start time sync PPDUs is aligned, PIFS recovery may cause BA reception error
  In end time alignment, 8us margin is allowed.
  As shown in the figure below, block ack transmitted on link 2 can not be received due to the retransmitted data with PIFS(25us) recovery on link 1.
When the end time alignment of start time sync PPDUs medium access is adopted, PIFS recovery shall not be used.
In case of error recovery, instead of PIFS recovery, new backoff shall be invoked.

## Slide 6: Conclusion
In this contribution, end time alignment of start time sync PPDUs medium access is discussed.
End time of start time sync PPDUs medium access shall be aligned in order to prevent NSTR interference error.
If the end time alignment of start time sync PPDUs medium access is adopted, multi-TID A-MPDU can be used to align the end time.
If the end time alignment of start time sync PPDUs medium access is adopted, PIFS error recovery shall not be used and backoff shall be invoked.

## Slide 7: Reference
[1] Draft P802.11be D2.0