## Slide 1: [Device ID Synchronization and Control]
Date: 2022-08-08
Authors:

## Slide 2: Abstract
This submission proposed methods on how the Device ID shall be synchronized between the non-AP STA and the network. It also modifies the informational element proposed in 802.11-22/1084r0.

## Slide 3: Device ID Synchronization and Control
In the comment collection process for IEEE P802.11bh Draft 0.2 several comments addressing the passing of the ID and synchronization between the non-AP STA and the network. This submission seeks to address these comments.
This proposal seeks to modify the Device ID Element and bit settings therein to allow for control of the Device ID.
If the methods suggested herein are agreed upon, a text submission will be prepared to codify these methods in the text.
Seeks to address: CR-4,CR-6, CR-10, CR-11, CR-15, CR26, CR30, CR31

## Slide 4: Proposed Modification to Device ID Element
ID Activated: 0b1 = Device is allowed to be ID’d 0b0 = Device is not allowed to be ID’d
ID Source:
0b0 = Network Generated ID
0b1 = Non Network Generated ID
ID Blob (variable length):
  Identifier previously assigned by the Network
  Identifier provided by the Device
  Blank, no identifier provided or assigned
Reserved
(6 bits)
Device ID Element
Element ID Extension
Length
ID Blob
ID Control
Element ID
ID Source
(1 Bit)
ID Activated (1 Bit)

## Slide 5: Further Explanations
The proposed changes to the Device ID Element will allow for:
The Network to determine if the non-AP STA allows itself to be identified by a Device ID (dot11MIB set as identification is activated)
Provide the source of the ID
  Network Generated ID
  Non-AP STA Generated ID

## Slide 6: Device ID Implemented / Device ID Activated Truth Table
Device ID Implemented | Device ID Activated | Result
0 | Don’t Care | The bit will not be set in the Extended Capabilities field. No Device ID will be exchanged. If the Informational element is provided in the exchange, then the Device ID Activated = 0, and the blob will be empty.
1 | 0 | Indicates that the device has implemented Device ID but has chosen not to be identified. ID blob will always be empty. Network will not assign an ID.
1 | 1 | Indicates that the device has implemented Device ID and is allowed to be identified within the network.

## Slide 7: Message 2 of 4-Way Handshake
Device ID Activated | ID Source | ID BLOB | Result (message 2 of 4)
0 | Don’t care | EMPTY | Indicates device has chosen not to be identified. ID blob will always be empty. Network will not assign an ID.
1 | 0 | EMPTY | Indicates the device has chosen to be identified by a network generated ID, but the ID for this network has not been assigned
1 | 0 | ID | Indicates the device has chosen to be identified by a network generated ID, and the network has previously assigned this ID to the device
1 | 1 | ID | Indicates the device has chosen to be identified, and is using a Device assigned ID.
1 | 1 | Empty | This is an error condition. Network shall not store an ID or assign an ID to the device.

## Slide 8: Message 3 of 4-Way Handshake
Device ID Activated | ID Source | ID BLOB | Result (message 3 of 4)
0 | Don’t Care | EMPTY | The AP should return nothing in Message 3 of the handshake
1 | 0 | EMPTY | AP shall return a network generated ID in Message 3 of the handshake with ID Source = 0. The device shall store and return this ID at the next exchange.
1 | 0 | ID | Indicates the device has chosen to be identified by a network generated ID, and the network has previously assigned this ID to the device.
 |  |  | If the device is recognized by the network no Message 3 is sent.
 |  |  | If the device is NOT recognized by the network, a Message 3 is sent with a newly generated ID with ID Source = 0. The device shall store and return this ID at the next exchange.

## Slide 9: Message 3 of 4-Way Handshake Continued
Device ID Activated | ID Source | ID BLOB | Result (message 3 of 4)
1 | 1 | ID | Indicates the device has chosen to be identified, and is using a Device generated ID. No Message 3 is necessary.
 |  |  | If the network has the ID, it identifies the Device.
 |  |  | If the network does not have the ID, it stores the ID for subsequent identification of the device.
1 | 1 | Empty | This is an error condition. AP shall not store an ID or assign an ID to the device.

## Slide 10: References
IEEE 802.11-22/1084r0
IEEE 802.11-22-0832r6
IEEE 802.11-22-0973r6