## Slide 1: Device ID Synchronization and Control
Date: 2022-08-11
Authors:

## Slide 2: Revisions
R0 – Initial Version
R1 – Simplification of logic and removal of Informational Element changes. No need to modify Device ID KDE. Logic reworked as well as additions for FILS.
R2 – Modify AP not recognize non-AP STA identifier.
R3 – Updates made during presentation. Modified Text for Supported/Active to move into one variable.

## Slide 3: Abstract
This submission proposes methods on how the Device ID shall be synchronized between the non-AP STA and the network. It also suggests a method to determine if a non-AP STA has Activated Device ID for the network.

## Slide 4: Device ID Synchronization and Control
In the comment collection process for IEEE P802.11bh Draft 0.2 several comments addressing the passing of the ID and synchronization between the non-AP STA and the network. This submission seeks to address these comments.
If the methods suggested herein are agreed upon, a text submission will be prepared to codify these methods in the text.
Seeks to address: CR-4,CR-6, CR-10, CR-11, CR-15, CR26, CR30, CR31
Suggests update to 9.4.2.241 RSN Extension Element

## Slide 5: Suggested Change to 9.4.2.241
Suggest changing Notes to read as follows:
The STA sets the Device ID Support bit to indicate that it has implemented and activated the Device ID feature. Otherwise, the STA sets the Device ID Support field to 0.

## Slide 6: Device ID Support Truth Table AP STA
Device ID Support | AP STA Result for a given network
0 | Indicates Device ID has either not been implemented or it is not active for this SSID No Device ID Element is sent in the Association Response frame for FILS No Device ID KDE will be passed in message 3 of the 4-Way handshake for FT No Device ID KDE will be passed in message 3 of the 4-Way handshake for or other exchanges.
1 | Indicates that the AP STA has implemented Device ID and it is active for this SSID Device ID Element with ID Blob sent in the Association Request frame for FILS Device Device ID KDE with ID Blob passed in message 3 of the 4-Way Handshake for FT. Device ID KDE with ID Blob passed in message 3 of the 4-Way Handshake for other exchanges.

## Slide 7: Device ID Support Truth Table non-AP STA
Device ID Support | Non-AP STA Result for a given network
0 | Indicates Device ID has either not been implemented or it is not active for this SSID No Device ID Element is sent in the Association Request frame for FILS No Device ID KDE will be passed in message 2 of the 4-Way handshake for FT No Device ID KDE will be passed in message 2 of the 4-Way handshake for or other exchanges.
1 | Indicates that the device has implemented Device ID and it is active for this SSID Device ID Element with ID Blob sent in the Association Request frame for FILS Device Device ID KDE with ID Blob passed in message 2 of the 4-Way Handshake for FT. Device ID KDE with ID Blob passed in message 2 of the 4-Way Handshake for other exchanges.

## Slide 8: Non-AP STA Indication of Device ID
Device ID Support | ID BLOB | Result for the network
0 | Don’t Care | Indicates device has chosen not to be identified. Network will not assign an ID to the device. No Device ID Element sent in the Association Request frame for FILS No Device ID KDE passed in message 2 of the 4-Way Handshake for FT No Device ID KDE passed in message 2 of the 4-Way Handshake for other exchanges.
1 | EMPTY | Indicates the device has chosen to be identified by a network generated ID, but the ID Blob for this network has not been assigned. Device ID Element with an empty ID Blob sent in the Association Request frame for FILS Device ID KDE with an empty ID Blob sent in message 2 of the 4-Way Handshake for FT Device ID KDE with an empty ID Blob sent in message 2 of the 4-Way Handshake for other exchanges.

## Slide 9: Non-AP STA Indication of Device ID Activated
Device ID Support | ID BLOB | Result Per Network
1 | ID | Indicates the device has chosen to be identified with this ID. Device ID Element with ID Blob sent in the Association Request frame for FILS Device ID KDE with ID Blob sent in message 2 of the 4-Way Handshake for FT Device ID KDE with ID Blob sent in message 2 of the 4-Way Handshake for other exchanges.

## Slide 10: AP Actions
Device ID Support | ID BLOB | AP Actions
0 | N/A | AP should not insert Device ID Element in the Association Response frame for FILS AP should not return Device ID KDE in Message 3 of the 4 way handshake for FT AP should not return Device ID KDE in Message 3 of the 4 way handshake for other exchanges
1 | EMPTY | AP shall insert a network generated ID Blob in the Device ID Element in the Association Response frame for FILS. AP shall insert a network generated ID Blob in the Device ID KDE in message 3 of the 4 Way handshake for FT AP shall insert a network generated ID Blob in the Device ID KDE in message 3 of the 4 Way handshake for other exchanges The non-AP STA shall store and subsequently return this ID for this network.

## Slide 11: AP Response
Device ID Active | ID BLOB | Result
1 | ID | Indicates the non-AP STA has chosen to be identified with this ID for this SSID.
 |  | If the ID Blob is recognized: AP may insert the ID in the Device ID Element in the Association Response frame for FILS AP may insert the ID in the Device ID KDE in Message 3 of the 4-Way handshake for FT or others
 |  | If the ID Blob is NOT recognized: AP may allow this ID to be utilized to identify the device. AP may insert the ID in Device ID Element in the Association Response frame for FILS AP may insert the ID in the Device ID KDE in Message 3 of the 4-Way handshake for FT or others
 |  | AP may assign a new ID. If so: The new ID is inserted in the ID Blob in the Device ID Element in the Association Response frame for FILS. The new ID is inserted in the ID Blob in the Device ID KDE in message 3 of the handshake for FT and others. The non-AP STA shall store and subsequently return this ID for this SSID.

## Slide 12: References