## Slide 1: TGbh, TGbi, Stop association to a Spoof AP
Date: 2022-07
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: The “Problem”
Dastardly people set up APs that spoof the “home BSS” of the target X.
  The “J Lo” paparazzi attack
If X’s mobile, STA X, comes in range, it will attempt to Associate
It does not matter what MAC Address STA X is using, the mere fact it sent an Association Request exposes that it (or someone from X’s home) is in the area.
TASK - Is it possible to know that the AP is the “real deal” BEFORE attempting to Associate?
Still ‘early days’ but looking for comments and feedback

## Slide 3: How to stop the STA from sending Association Request to a spoof?
“Protected Beacons” – Only works after Association
Is this being considered in TGbi (Requirement 34)?
Could this be considered in TGbh?
Three basic IDEAS:
Location based
SSID Profile
Identifiable Beacon

## Slide 4: Location based
Basically, knowing location of your ‘favorite’ SSID(s).
  Maybe most applicable to Home network and/or office
  User sets this up
GPS linked
Use the GPS to save the location when first setting up the scheme.
  STA/User prompted to save GPS co-ordinates of the BSS.
STA gets probe response or Beacon from spoof “Home AP”.
Before sending Association Request, STA check GPS co-ordinates
  If matches saved location, then send Request
  If does not match location, do not send Request.
Advantage – simple, seems to be very secure
Disadvantage – not 802.11 related, relies on higher layer application.
Could be described in an informative way?
Just leave it to someone to write the APP?
If STAs using a “pre-scheme” at home (say), saved the location when being set up, STA checks location and only attempts association if location matches.
STA saves a “SSID list/profile” of networks in vicinity of “home”. Any new or unexpected SSIDs, e.g., obvious new SSIDs such as “Fleapit Hotel”, indicates ‘not at home’.
  Absence of ‘expected’ SSIDs plus presence of unexpected would indicate ‘take care’.

## Slide 5: “SSID Profile”
STA saves a “SSID list/profile” of networks in vicinity of “home” and creates an “SSID profile”
When spoof AP appears, STA checks other SSIDs in range and checks them against the stored “profile”
STA can decide if the AP meets the “SSID profile”.
For example:
Any new or unexpected SSIDs, e.g., obvious new SSIDs such as “Bedbug Hotel”, would indicate ‘not at home’.
Absence of ‘expected’ SSIDs (plus presence of unexpected) would indicate ‘take care’.
This could be 802.11 -
User or maybe the BSS/AP instructs STA to carry out ‘Neighbor Report’, which is saved.
STA performs Neighbor Report activity (does not send it) before sending Association Request.

## Slide 6: SSID Profile
Pretty simple. An algorithm should be pretty simple to compare “Neighbor Reports”.
  Save “Home SSID” list, need to match say 3 and no more than 1 “new”
Could the spoof somehow set up other spoofs to re-create the same SSID list? – seems doubtful.
Could be described as part of 802.11 in the Privacy section.

## Slide 7
Present protected Beacon scheme seems to only work after association (BIGTK)
  BIPN is initialized to zero and increments every beacon.
  Disclosure, by no means am I a crypto or PMF expert, so I might have this all wrong
Identifiable Beacon – Beacon Protection ID
BASIC IDEA
Inclusion of a ‘Beacon protection ID’ (BPID) in Beacon frames
  STA first associates (User knows this is ‘Home”) and receives a BPID Key (fixed key for that AP). “BPIDK”
  AP includes a Beacon IE with BIPNa, Random number, and BIC (beacon integrity check)
    BIPNa is incremented every X beacons
    STA calculates BIC = function {BIPN, Random Number, BPIDK} AND records BIPN/time
  If BICs match, Beacon is genuine
Everytime BIPNa changes, a new random number and hence a new MIC.
  Something like 60-minute updates may be good enough?
Identifiable Beacon

## Slide 8
Basic ,
AP includes an ID (BIC) in its beacons which changes periodically
  IE includes BIPNa, a Random number, and BIC.
STA checks the BIPNa and the BIC and matches to the Key (BPIDK) that the AP provided.
  BIC = function {BIPNa, Random number, BPIDK}
  BIPNa makes sense, i.e., is advanced from last time at home.
Possible attacks
Attack – Spoof records a series of Beacons with BIPNa and BICs and replays this at the spoof AP.
Counter - STA can check time and estimate the BIPNa to confirm BIPNa is correct.
  BIPN 48 bits, repeats every 90,000 years
Attack - Beacons can be recorded, and Key found by brute strength. How long to do this?
Counter - Add a mechanism to change the BPIDK regularly.
  Needs to cater for multiple ‘home’ STAs