## Slide 1: Additional 11bi Requirements for Issue 2 and Issue 7
Date: 2022-07-29
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Ido Ouzieli |  |  |  | 
Johannes Berg |  |  |  | 
Ilan Peer |  |  |  | 
Robert Stacey |  |  |  | 
Notes: September 2012

## Slide 2: Additional Requirement for Issue 2
11 bi has approved the following requirement for Issue 2
802.1X authentication is currently done using data frame after association. To achieve above requirement, we propose the following requirement to handle 802.1X authentication
 | Requirement | Issue | Status | Information
4 | 11bi shall define a mechanism for a CPE Client and CPE AP to establish keys from an Authentication exchange which can then be used to protect the (Re)Association Request/Response. | I2 | Approved | Proposed - 22/107r2 (9 March 2022) To be motioned –agreed by unanimous consent 4/21/2022 Approved (Motion #13, 13 May 2022)
 | Requirement | Issue | Status | Information
XXX | 11bi shall define a mechanism for a CPE Client and CPE AP to tunnel 802.1X EAPOL PDUs in Authentication frames to perform IEEE 802.1X authentication. | I2 | Proposed | 

## Slide 3: Additional Requirement for Issue 7
11bi has agreed on the following for Issue 7
  Different client device implementations have identifiable characteristics during association
  These characteristics are externally visible in unprotected signaling, and hence can be used to fingerprint and track the device, e.g.
    non-robust action frames
To obtain specific parameters after association, the current mechanism of using probe request/response and multi-link probe request/response can not be protected
  What you request in the request frame is very specific and has privacy issues
  What you get as response is specific to the request and has privacy issues
  Probe Response frame needs to be sent by transmitted BSSID under multiple BSSID mechanism, which makes encryption of individually addressed frame difficult
We propose the following additional requirement for Issue 7
 | Requirement | Issue | Status | Information
XXX | 11bi shall define a mechanism for a 11bi non-AP STA to request capabilities and operation parameters of the associated 11bi AP or a 11bi non-AP MLD to request capabilities and operation parameters of APs affiliated with the associated 11bi AP MLD using an individually addressed protected request/response action frame. | I7 | Proposed |