## Slide 1: TGbi, Beacon Protection against Spoof AP
Date: 2022-08
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: The “Problem”
Dastardly people set up APs that spoof the “home BSS” of the target X.
  The “J Lo” paparazzi attack
If X’s mobile, STA X, comes in range, it will attempt to Associate
It does not matter what MAC Address STA X is using, the mere fact it sent an Association Request exposes that it (or someone from X’s home) is in the area.
TASK - Is it possible to know that the AP is the “real deal” BEFORE attempting to Associate?
Still ‘early days’ but looking for comments and feedback

## Slide 3: How to stop the STA from sending Association Request to a spoof?
“Protected Beacons” – Only works after Association
Is this being considered in TGbi (Requirement 34)?
Could this be considered in TGbh?
Three basic IDEAS:
Location based
SSID Profile
Identifiable Beacon

## Slide 4: Location based
Basically, knowing location of your ‘favorite’ SSID(s).
  Maybe most applicable to Home network and/or office
  User sets this up
GPS linked
Use the GPS to save the location when first setting up the scheme.
  STA/User prompted to save GPS co-ordinates of the BSS.
STA gets probe response or Beacon from spoof “Home AP”.
Before sending Association Request, STA check GPS co-ordinates
  If matches saved location, then send Request
  If does not match location, do not send Request.
Advantage – simple, seems to be very secure
Disadvantage – not 802.11 related, relies on higher layer application.
Could be described in an informative way?
Just leave it to someone to write the APP?
If STAs using a “pre-scheme” at home (say), saved the location when being set up, STA checks location and only attempts association if location matches.
STA saves a “SSID list/profile” of networks in vicinity of “home”. Any new or unexpected SSIDs, e.g., obvious new SSIDs such as “Fleapit Hotel”, indicates ‘not at home’.
  Absence of ‘expected’ SSIDs plus presence of unexpected would indicate ‘take care’.

## Slide 5: “SSID Profile”
STA saves a “SSID list/profile” of networks in vicinity of “home” and creates an “SSID profile”
When spoof AP appears, STA checks other SSIDs in range and checks them against the stored “profile”
STA can decide if the AP meets the “SSID profile”.
For example:
Any new or unexpected SSIDs, e.g., obvious new SSIDs such as “Bedbug Hotel”, would indicate ‘not at home’.
Absence of ‘expected’ SSIDs (plus presence of unexpected) would indicate ‘take care’.
This could be 802.11 -
User or maybe the BSS/AP instructs STA to carry out ‘Neighbor Report’, which is saved.
STA performs Neighbor Report activity (does not send it) before sending Association Request.

## Slide 6: SSID Profile
Pretty simple. An algorithm should be pretty simple to compare “Neighbor Reports”.
  Save “Home SSID” list, need to match say 3 and no more than 1 “new”
Could the spoof somehow set up other spoofs to re-create the same SSID list? – seems doubtful.
Could be described as part of 802.11 in the Privacy section.

## Slide 7
Present protected Beacon scheme seems to only work after association (BIGTK)
  Disclosure, by no means am I a crypto or PMF expert, so I might have this all wrong
Identifiable Beacon – Beacon Protection ID
BASIC IDEA
Inclusion of a ‘Beacon Protection IE’ in Beacon frames
  STA first associates (User knows this is ‘Home”) and receives a “BPID” (fixed key for that AP).
  “BPPN” Beacon protection packet number, incremented approx. every hour.
  AP includes a Beacon Protection IE with BPPN, Random number, and BPC (beacon protection check)
    BPPN is incremented every X beacons
    STA calculates BPC = function {BPPN, Random Number, BPID} AND notes BPPN value
  If BPCs match, AND BPPN value is “OK”, then Beacon is genuine
Everytime BPPN changes, a new random number and hence a new MPC.
  Something like 1 hour updates may be good enough?
Identifiable Beacon

## Slide 8: Details
Beacon Protection Packet Number BPPN
A beacon is every 102400 us or 9.765625 per second
Assume BPPN increments every 32768 beacons (2^15)
Assume 16 bit BPPN, then rolls over every 2524 days (6.97 years)
Beacon Protection ID BPID
Assume 64 bits
Assume 10 Thash/sec (is that too high?) then >5 years – Is it worth the effort?
What’s a good function?
BPC = function {BPPN (16 bit), seed (48 bit?), BPID (64 bit)}

## Slide 9
Basic ,
AP includes a BP IE in its beacons which changes periodically
  IE includes BPPN, a Random number, and BPC.
STA checks the BPPN and the BIC and matches to the Key (BPID) that the “known good” AP provided.
  BPC = function {BPPN, Random number, BPID}
  STA checks that BPPN makes sense, i.e., is advanced from last time at home.
Possible attacks
Attack – Spoof records a series of Beacons with BP IEs and replays this at the spoof AP.
Counter - STA can check time and estimate the BPPN to confirm BPPN is correct.
  BPPN 16 bits, repeats every 6.9 years - updates every hour
Attack - Beacons can be recorded, and Key found by brute strength. How long to do this?
Counter - Add a mechanism to change the BPIDK regularly (each week, each month, each year?)
  Needs to cater for multiple ‘home’ STAs

## Slide 10: Changing BPID
BPID is provided post Association. Hence, not having the latest is not a problem for association, but it could see the “home AP” as a spoof.
BPID can be provided together with TTL (time to live)
  STA knows if it is out-of-date and “takes a chance?”
AP could provide the next BPID in advance with TTS (time to start) and TTL.
  Doubles the validity time
BUT
With BPID 64 bits and BPPN 16 bit and Seed 48 bit Then make TTS/ TTL 1 year? OR not change it at all?
  Beacon is showing a solution every hour, how does that lessen the time to brute strength it?

## Slide 11: Conclusion
The Beacon Protection ID seems to work.
It solves the spoof AP problem
With BPC changing, say, every hour, not too much work for the AP
STA can check the BP IE in the beacon to confirm authenticity of the AP/BSS
Need to determine optimal lengths of BPPN, BPID and Seed
Need to determine best ‘function’.

## Slide 13: Straw Poll
Do you support the Beacon Protection ID scheme as outlined in <this presentation> for inclusion in the TGbi Draft?
Y/N/A