## Slide 1: WLAN Sensing Measurement CSI Report with Rx Frequency Response Category Index
Date: 2022-08-03
Authors:
Name | Affiliation | Address | Phone | Email
Shuling (Julia) Feng | Mediatek Inc | 2840 Junction Ave, San Jose, CA 95134, USA |  | julia.feng@mediatek.com
Jianhan Liu |  |  |  | jianhan.liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
Kevin Tsai |  |  |  | kevin.tsai@mediatek.com

## Slide 2: Introduction
Sensing receiver adjusts LNA, VGA, and digital gain settings when receiving a NDP frame [1].
  Due to power measurement errors, the receiver may use different LNA, VGA, and digital gain settings receiving different sensing NDP frames even if they are transmitted at the same power level in the same channel environment.
LNA switches / VGA adjustments may cause RF / analog filter changes and result in variations of normalized Rx frequency response.

## Slide 3: Categorize Rx Frequency Response Variations
Rx frequency response variations are product dependent.
  Some receivers may have frequency response variations significant enough to affect CSI estimation accuracy, and further affect sensing performance, especially when small CSI variations are expected between sensing instances [1].
  Some receivers have consistent frequency response, and variations can hardly be distinguished.
Normalized Rx frequency response may only vary in limited patterns and can be further categorized with underlying circuit conditions.
  If a receiver’s frequency responses vary with LNA/VGA gain settings, they can be categorized into major patterns. Each pattern corresponds to a group of the LNA/VGA gain settings, and it can be numbered with a Rx frequency response index, say Rx_FR_Index.
  For example, limit magnitude variation of Rx frequency response ≤ 0.5dB in each category

## Slide 4: Benefit of Rx_FR_Index in 11bf Sensing
Sensing initiator may use Rx_FR_Index to control combination or comparison of CSIs obtained from different sensing NDPs for the same measurement setup ID in a sensing session
  Rx_FR_Index is fed back to sensing initiator along with CSI during sensing measurement report.
  Rx_FR_Index field may help sensing initiator to detect small CSI variations reliably.
  CSIs with the same Rx_FR_Index (≠ FR_NV) are generated with the same category of normalized receiver frequency response, and they can be combined for better sensing performance or compared for sensing detection if necessary.
  Depending on types of applications, initiator can also choose to combine or compare CSIs with different Rx_FR_Index after assessing CSI variation risks caused by Rx frequency response changes.
  Rx_FR_Index mapping is determined by sensing receiver with its best effort. And initiator doesn’t need mapping rules to use Rx_FR_Index.

## Slide 5: Proposal
We propose to add a field Rx_FR_Index along with CSI in 11bf sub-7GHz sensing measurement report to index category of normalized Rx frequency response
  Rx_FR_Index is category index of normalized receiver frequency response
  Rx_FR_Index: size TBD
    For example: a 3 bits Rx_FR_Index indicates up to 8 Rx frequency response categories

## Slide 6: Rx_FR_Index Values
A chip vendor has flexibility with Rx_FR_Index depending on normalized Rx frequency response variations.
  A chip vendor may not category Rx frequency response and will set Rx_FR_Index = FR_NV to indicate this status. Rx_FR_Index field doesn’t carry any Rx frequency response category information in this case.
    For example, FR_NV = 0
  A chip vendor may set Rx_FR_Index = k (k is a fixed number and k ≠ FR_NV) to indicate its Rx frequency response doesn’t vary significantly across all gain settings.
  For example, if a chip vendor finds its Rx frequency response varies in 4 major patterns, it can categorize these variations and their underlying circuit conditions into 4 categories and map them to 4 values (≠ FR_NV) of Rx_FR_Index.

## Slide 7: Summary
Rx_FR_Index field helps to improve sensing performance when small CSI variations are concerned by allowing combination or comparison of CSIs obtained from different NDPs with the same Rx_FR_Index value (≠0).
Rx_FR_Index field also provides chip vendors flexibility to categorize Rx frequency response variations.
  Rx_FR_Index = 0 indicates Rx frequency response is not categorized.
  Rx_FR_Index ≠ 0 indicates Rx frequency response doesn’t vary significantly with the same Rx_FR_Index value.

## Slide 8: SP1
Do you agree to add a field Rx_FR_Index along with CSI in 11bf sub-7GHz sensing measurement report to index category of Rx frequency response?
  Rx_FR_Index is category index of receiver frequency response
  Rx_FR_Index: number of bits is TBD

## Slide 9: SP2
Do you agree with the following definitions for Rx_FR_Index field in 11bf sub-7GHz sensing measurement report?
  Rx_FR_Index = 0 indicates Rx frequency response is not categorized.
  Rx_FR_Index ≠ 0 indicates Rx frequency response doesn’t vary significantly with the same value of Rx_FR_Index.

## Slide 10: Reference
[1] IEEE doc 802.11-22/0647r7, Information Exchange of WLAN Sensing Link