## Slide 1: WLAN Sensing Measurement CSI Report with Rx Frequency Response Category Index
Date: 2022-08-03
Authors:
Name | Affiliation | Address | Phone | Email
Shuling (Julia) Feng | Mediatek Inc | 2840 Junction Ave, San Jose, CA 95134, USA |  | julia.feng@mediatek.com
Jianhan Liu |  |  |  | jianhan.liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
Kevin Tsai |  |  |  | kevin.tsai@mediatek.com

## Slide 2: Introduction
Sensing receiver adjusts LNA, VGA, and digital gain settings when receiving a NDP frame [1].
  Due to power measurement errors, the receiver may use different LNA, VGA, and digital gain settings receiving different sensing NDP frames even if they are transmitted at the same power level in the same channel environment.
LNA switches / VGA adjustments may cause RF / analog filter changes and result in variations of normalized Rx frequency response.
  Rx frequency response can be obtained as CSI in a loopback test. It can further be normalized with total gain in the receiver chain leading to CSI estimation.
  Rx frequency response vs gain variations my change with bandwidth

## Slide 3: Rx frequency response variations are product dependent
Some receivers may have frequency response variations significant enough to affect CSI estimation accuracy, and further affect sensing performance, especially when small CSI variations are expected between sensing instances [1].
Some receivers have consistent frequency response, and variations can hardly be distinguished.
  It maybe achieved by chip vendors design consistency
  It maybe achieved by chip vendors specially designed calibrations and compensations
Some receivers have frequency response variations only in limited cases
Since 11bf targets minimum PHY changes, we need to have a scheme to accommodate all these existing Rx frequency response cases.

## Slide 4: Categorize Rx Frequency Response Variations
Rx frequency responses can be categorized into limited groups with underlying circuit conditions based on their variations
  If a receiver’s frequency responses vary with LNA/VGA gain settings, they can be categorized into major groups. Each group corresponds to one or multiple of the LNA/VGA gain settings, and it can be numbered with a Rx frequency response index, say Rx_FR_Index.
  Within each group, Rx frequency response variation is considered insignificant.
  Categorization could be based on metric(s) derived from magnitude and/or phase variations of the Rx frequency response
  The details of rules to categorize Rx frequency response will be further discussed

## Slide 5: Benefit of Rx_FR_Index in 11bf Sensing
Sensing initiator may use Rx_FR_Index to control combination or comparison of CSIs obtained from successive sensing NDPs for the same measurement setup ID in a sensing session
  Rx_FR_Index is fed back to sensing initiator along with CSI during sensing measurement report.
  Rx_FR_Index may help sensing initiator to detect small CSI variations reliably.
    CSIs with the same valid Rx_FR_Index are generated with the same category of normalized receiver frequency response, and they can be combined for better sensing performance or compared for sensing detection if necessary.
  Depending on types of applications, initiator can also choose to combine or compare CSIs with different Rx_FR_Index after assessing CSI variation risks caused by Rx frequency response changes.
  Rx_FR_Index is determined by sensing receiver with its best effort. And initiator doesn’t need knowledge of mapping rules to use Rx_FR_Index.

## Slide 6: Proposal
We propose to add Rx_FR_Index along with CSI in 11bf sub-7GHz sensing measurement report to indicate categorization of normalized Rx frequency response variations
  Rx_FR_Index is a category index of normalized receiver frequency response
  Rx_FR_Index: size TBD
    For example: a 3 bits Rx_FR_Index indicates up to 7 Rx frequency response categories

## Slide 7: Rx_FR_Index Values
A chip vendor has flexibility with Rx_FR_Index depending on normalized Rx frequency response variations.
  A chip vendor may not category Rx frequency response variations and will set Rx_FR_Index to an invalid value to indicate this status. Rx_FR_Index field doesn’t carry any Rx frequency response variation category information in this case.
    For example, Rx_FR_Index = 0 signals invalid index
  A chip vendor may set Rx_FR_Index = k (k≠0 is a fixed valid index) to indicate its Rx frequency response doesn’t vary significantly across all gain settings.
  For example, a chip vendor finds its Rx frequency responses vary in 4 major patterns in lab sample tests or selected gain setting product tests. It can categorize these variations and their underlying circuit conditions into 4 categories and map them to 4 valid index values of Rx_FR_Index.

## Slide 8: Summary
Rx_FR_Index field helps to improve sensing performance when small CSI variations need to be detected by allowing combination or comparison of CSIs obtained from successive NDPs with the same Rx_FR_Index value (≠0).
Rx_FR_Index field provides chip vendors flexibility to categorize Rx frequency response variations.
  Rx_FR_Index = 0 indicates Rx frequency response is not categorized.
  Rx_FR_Index ≠ 0 indicates Rx frequency response doesn’t vary significantly with the same Rx_FR_Index value.

## Slide 9: SP1
Do you agree to add a field Rx_FR_Index along with CSI in 11bf sub-7GHz sensing measurement report to index category of Rx frequency response?
  Rx_FR_Index is a category index of receiver frequency response
  Rx_FR_Index: number of bits is TBD
  Rx_FR_Index per receive antenna is TBD

## Slide 10: SP2
Do you agree with the following definitions for Rx_FR_Index field in 11bf sub-7GHz sensing measurement report?
  Rx_FR_Index = 0 indicates Rx frequency response is not categorized.
  Rx_FR_Index ≠ 0 indicates Rx frequency response doesn’t vary significantly with the same value of Rx_FR_Index.

## Slide 11: Reference
[1] IEEE doc 802.11-22/0647r7, Information Exchange of WLAN Sensing Link