## Slide 1: NDP formats for 802.11bf
Date: 2022-08-23
Authors:
Name | Affiliation | Address | Phone | Email
Yan Xin |  | Ottawa, Ontario |  | yan.xin@huawei.com
Junghoon Suh |  |  |  | Junghoon.Suh@huawei.com
Mengshi Hu |  |  |  | humengshi@huawei.com

## Slide 2: Introduction
One of outstanding topics in 802.11bf D0.2 is the NDP format for sensing.
Based on the SENS SG PAR [1], an NDP format for 802.11bf sensing in the sub-7 GHz systems should be selected from the NDP formats specified in 11ax, 11az, 11be amendments and the IEEE P802.11 revision standard.
Discussion on the pros and cons of alternative NDP formats for sensing has been extensively discussed in TGbf [2], [3]. No decision has been made yet on which type of NDP format shall be used in 802.11bf.
TGbf should move forward on this topic since it impacts on the design of other parameters and features resulting in a potential risk for a delay of 802.11bf development.
This contribution recommends the NDP formats for 802.11bf.

## Slide 3: HE (TB) Ranging NDP vs. EHT Sounding NDP
 | HE (TB) Ranging NDP | EHT Sounding NDP
Support of PPDU BWs | 20, 40, 80, and 160 MHz | 20, 40, 80, 160, and 320 MHz
Support of preamble puncturing | Not supportive | Supportive of preamble puncturing with 20 MHz or 40 MHz resolution
Support of LTF repetition | Supportive of LTF repetition (up to 8 HE LTF Repetition Blocks, each of which can include up to 8 HE LTF symbols) | Indirectly supportive of LTF repetition. Support maximum 16 EHT-LTF symbols (when maximum N_STS=8). (note: this is equivalent to a repetition factor of 2 in HE (TB) Ranging NDP) Supporting additional EHT-LTF is optional.
Support of NDP transmissions for both I2R and R2I | Supportive of NDP transmissions for both I2R and R2I | EHT Sounding NDP is implemented only for DL.
STA supporting level | An HE STA may support HE (TB) Ranging NDP. | An EHT STA shall support EHT sounding NDP.

## Slide 4: Discussion (1)
The following requirements on NDP for 802.11bf sub-7 GHz sensing should be considered:
- a sensing NDP can be transmitted over the maximum frequency resource available so far for sub-7 GHz WLAN, i.e., 320 MHz
- preamble puncturing can be deployed for efficient sensing measurement and sensing measurement feedback transmissions
- flexible LTF configurations can be achievable by a sensing NDP
- sensing NDP is available for I2R and R2I transmissions
36.1.1 Introduction to the EHT PHY [4]
An EHT STA shall support the following features:
- Single spatial stream EHT-MCSs 0 to 7 (transmit and receive) in all supported
channel widths and RU and MRU sizes of EHT PPDU.
- Single spatial stream EHT-MCSs 8 and 9 (transmit and receive) in all supported
channel widths and RU and MRU sizes of EHT PPDU if the STA is not a 20
MHz-only non-AP STA.
- 20 MHz channel width and all RU and MRU sizes and locations applicable to the 20
MHz channel width in the 2.4 GHz, 5 GHz, and 6 GHz bands (transmit and receive).

## Slide 5: Discussion (2)
Based on the comparison of HE (TB) Ranging NDP and EHT Sounding NDP on the previous slide, neither HE (TB) Ranging NDP nor EHT Sounding NDP can fully satisfy the requirements above.
Recommend to take both HE (TB) Ranging NDP and EHT Sounding NDP into account in 802.11bf

## Slide 6: SP1
Do you agree to include the following text in 802.11bf SFD?
- To use the HE Ranging NDP and HE TB Ranging NDP formats for 802.11bf sub-7 GHz sensing when PPDU BW ≤ 160 MHz
To use the EHT sounding NDP format (including specified preamble puncturing) for 802.11bf sub-7 GHz sensing when PPDU BW = 320 MHz
Yes:
No:
Abstain:

## Slide 7: SP2
Do you agree to include the following text in 802.11bf SFD?
Optionally to use the EHT sounding NDP format (only for preamble puncturing) for 802.11bf sub-7 GHz sensing when PPDU BW ≤ 160 MHz
Note: HE Ranging NDP and HE TB Ranging NDP formats are used for 802.11bf sub-7 GHz sensing when PPDU BW ≤ 160 MHz without preamble puncturing.
Yes:
No:
Abstain:

## Slide 8: References
[1] IEEE 802.11-19/2103r12, 802.11 SENS SG proposed PAR.
[2] IEEE 802.11-22/0415r2, NDP Selection for 802.11bf.
[3] IEEE 802.11-22/0421r0, Discussion on the NDP format for sensing.
[4] IEEE P802.11be/D2.0.
[5] IEEE P802.11az/D5.0