## Slide 1: Thoughts on High Frequency Band
Date: 2022-10-21
Authors:

## Slide 2: Introduction
In a previous Montreal meeting, the formation of UHR (Ultra High Reliability) SG was approved to develop PAR and CSD for a new 802.11 MAC/PHY amendment [1].
  The study group investigates technology which may improve reliability of WLAN connectivity, reduce latencies, increase manageability, increase throughput including at different SNR levels, and reduce device level power consumption.
  With a target start of the task group in May 2023
Common objective which has been mainly mentioned in various contributions [2-7] on UHR is to further improve the throughput and latency performance with respect to EHT.

## Slide 3: Consideration on Operating Band above 45 GHz for UHR
As one of the ways to improve the throughput and latency performance, considering the unlicensed mmWave bands above 45 GHz band was proposed in [8-9].
In both contributions, the authors proposed to reuse the 2.4/5/6 GHz design in the higher frequency band.
The reason for reusing the 2.4/5/6 GHz design is to keep complexity within the bounds of lower band 802.11.
In this contribution, we introduce several aspects that we need to discuss to include the mmWave bands above 45 GHz for UHR.

## Slide 4: HW Design Challenges
Antenna and RF components, such as power amplifier (PA), low-noise amplifier (LNA), mixer, and voltage-controlled oscillators, which are used for below 7 GHz may not be shared with mmWave systems.
Depending on how to reuse the lower frequency band design, the baseband also needs to be updated/redesigned.
Algorithms may be reused. But that is a very small portion.
Thus, reusing a lower frequency design in a higher frequency band may not help to reduce the complexity of the system.
However, reducing bandwidth from minimum 2.16 GHz (.11ay) to low (e.g. 160 MHz) can help to reduce the complexity.

## Slide 5: Legacy Support
In the 60 GHz band, there are .11ad/.11ay devices.
If the new system does not need to support legacy .11ad/.11ay devices, then we may reuse the 2.4/5/6 GHz design (11a/n/ac/ax/be).
So, the question that we need to consider to utilize the unlicensed mmWave bands above 45 GHz for UHR is whether we want to support .11ad/.11ay as a legacy.

## Slide 6: Influence of CFO in mmWave
Carrier frequency offset (CFO) occurs when STA’s local oscillator signal for down conversion does not synchronize with the carrier frequency of the received signal.
CFO problem becomes more critical in mmWave systems compared with sub-6 GHz bands because the maximum CFO value increases linearly with the carrier frequency.
  E.g., if the transmit and the receive oscillators run at a frequency that is 20 ppm above and 20 ppm below the identical carrier frequency, respectively, the received baseband signal will have a CFO of 40 PPM. For a carrier frequency of 70 GHz, the CFO is thus up to ±2.8 MHz while the CFO is up to 280 kHz with a carrier frequency of 7 GHz.
Thus, we need to have a subcarrier spacing of at least ±2.8 MHz or need to define a tighter requirement. Note that .11ay subcarrier spacing is 5.156 MHz.

## Slide 7: Influence of Phase Noise in mmWave
Phase noise caused by random fluctuations in the frequency of the local oscillators of AP and STA can incur the effect of ICI in OFDM-based mmWave system, which degrades SINR.
To reduce the impact of phase noise, the subcarrier spacing should be increased compared to 11ac/11be [10].
  E.g., subcarrier spacing should be larger than 500 kHz at 70 GHz, i.e. the subcarrier spacing should be about 2x wider than that of 11ac (or 8x wider than that of 11be) to support 64 QAM considering performance loss caused by phase noise.
  From the PN model in [10], subcarrier spacing of 500 kHz, 1.25 MHz, 2.5 MHz will result in -27 dBc, -31 dBc, and -33 dBc ICI, respectively.
Therefore, to support the higher MCS level, a much larger subcarrier spacing (thus larger bandwidth) is required, which will cause higher power consumption and a larger fabrication area due to the higher chip speed.

## Slide 8: Possible Numerologies for mmWave
 | .11ay OFDM | 4x .11ac | 8x .11ac | 16x .11be
BW | 2.16/4.32/6.48/8.64 GHz | 80/160/320/640 MHz | 160/320/640/1280 MHz | 320/640/1280/2560/5120 MHz
Subcarrier Spacing | 5.156 MHz | 1.25 MHz | 2.5 MHz | 1.25 MHz (for 11be portion)
Guard Interval | 36.36 ns | 100/200 ns | 50/100 ns | 50/100/200 ns
IDFT/DFT period | 194 ns | 800 ns | 400 ns | 800 ns
IDFT/DFT size | 512/1024/1536/2048 | 64/128/256/512 | 64/128/256/512 | 256/512/1024/2048/4096
Modulation | BPSK to 64QAM | BPSK to 256QAM | BPSK to 256QAM | BPSK to 4096QAM

## Slide 9: Summary
In this contribution, we discussed several aspects that need to be considered to include mmWave operation in UHR.
  HW design challenges
  Legacy support
  Influence of CFO
  Influence of phase noise

## Slide 10: SP #1
Do you agree that mmWave operation is a promising feature for UHR?
  This SP is for information gathering.

## Slide 11: Reference
[1]11-22/0708r3, beyond ‘be’ - proposed next step
[2] 11-22/0030r1, look-ahead-to-next-generation
[3] 11-22/0032r0, next-gen-after-11be
[4] 11-22/0046r1, next-generation-after-802-11be
[5] 11-22/0059r0, beyond-be
[6] 11-22/0418r0, considerations-of-next-generation-beyond-11be
[7] 11-22/0458r1, looking-ahead-to-next-generation-follow-up
[8] 11-22/1083r1, next generation SG formation.
[9] 11-22/0729r1, 802.11 GEN8 study group
[10] Lei Huang, Yi Wang, Zhenyu Shi, and Rong Wen, (2016), “Radio parameter design for OFDM-based millimeter-wave systems,” 2016 IEEE 27th Annual International Symposium on Personal, Indoor, and Mobile Radio Communications (PIMRC), 2016.