## Slide 1: Multi AP Coordination and Residential Wi-Fi
Date: 2022-09-13
Authors:
Name | Affiliation | Address | Phone | Email
James Yee | MediaTek | 2840 Junction Ave, San Jose, CA 95134 USA | +1-408-526-1899 | james.yee@mediatek.com
Gabor Bajko | MediaTek |  |  | gabor.bajko@mediatek.com
Yonggang Fang | MediaTek |  |  | yonggang.fang@mediatek.com
Yongho Seok | MediaTek |  |  | yongho.seok@mediatek.com
Kaiying Lu | MediaTek |  |  | kaiying.lu@mediatek.com

## Slide 2: Outline
Background and Motivation
Multi-AP Coordination models
Summary & Strawpoll

## Slide 3: UHR SG and Multi-AP
Multi-AP Coordination has been studied and included as a main feature in the TGbe PAR [1], and further explored in several subsequent TGbe submissions, including [9][10][11][12][13][14].
Multi-AP has also been highlighted in WNG discussions [5][8][6] leading up to the creation of the UHR SG.
A comprehensive Multi-AP Coordination solution needs to address not just Enterprise but also Residential use cases. Here we look at possible solutions for different use cases.

## Slide 4: What is a representative Use Case for Multi-AP?
Ultra High Reliability (UHR) SG Scope
  [1] defines the scope of UHR SG for next gen Wi-Fi. Various KPIs and corresponding use cases have also been presented [2][3][4][5][6].
  The Dense Environment Use Case calls for meeting all KPIs and is an important Use Case to address. We believe Coordinated Multi-AP MLD is a solution for the Use Case.
KPIs | Use Cases |  |  |  |  | 
 | Video / Cloud Gaming | P2P / Fast Data Transfer | AR/VR/XR | AI / ML | Dense Environment | IIoT / Robotics
Throughput |  |  |  |  |  | 
Efficiency |  |  |  |  |  | 
Latency |  |  |  |  |  | 
Reliability |  |  |  |  |  | 
Mobility |  |  |  |  |  | 
Coverage |  |  |  |  |  | 
Power consumption |  |  |  |  |  | 
Manageability |  |  |  |  |  | 
Connectivity |  |  |  |  |  | 
Scalability |  |  |  |  |  | 

## Slide 5: Current Operation of multiple AP MLDs
With currently defined 11be, Uncoordinated AP MLDs operate independently with each other.
  Uncoordinated use of spectrum, time, and space/power
  risk of OBSS interference
  potential inefficient use of spectrum
  Lack of support for manageability and mobility
Coordination at higher layer are being defined (E.g., EasyMesh) but lack tools to coordinate lower layer resources with finer granularity.
2.4GHz
5GHz

## Slide 6: Coordinated Multi-AP Benefits
Extend Coverage
  A single AP has a limited coverage, due to limited TxP in unlicensed bands.
  For 6GHz SP, FCC requires the device to use AFC when operating using SP to avoid frequency overlap with fixed services so as to avoid interference to incumbent services. AFC is still under reviewing process. Regulatory progress of other countries are behind FCC.
  For 6GHz LPI or VLP with no AFC requirements, AP coverage is further reduced due to restricted TxP and high path loss comparing to 2.4/5 GHz.
  Therefore, the multi-AP network is a desirable mechanism to extend the coverage of Wi-Fi home network, enterprise, and public network to meet UHR KPI requirements.

## Slide 7: Coordinated Multi-AP Benefits
Provide ultra high reliability
  A wireless connection is not be very reliable
    weak RSSI/SINR when a receiving STA is far away from a transmitting STA, or
    interference from other transmitters in coverage area, especially on unlicensed bands.
  A single AP is difficult to meet ultra high reliability requirement (e.g. 99.99…%?)
    When the transmission path of the AP MLD is interfered or failed, associated non-AP would not be able to access to the network. Similar to AP MLD.
  Difficult to meet high reliability and low latency requirements at the same time
    Re-transmission can improve reliability but increase latency and reduce throughput.
  Multi-AP network and coordinated operation can provide redundant paths and transmissions to improve reliability and performance
Redundant Paths
A2
B2
Single Path
A1
B1

## Slide 8: Coordinated Multi-AP Benefits
Improve Efficiency, Manageability and Mobility
  Efficiency: Coordinated Multi-AP operation provides ways
    improve spectrum use efficiency in shared TXOP, via C-SR, C-TDMA, C-OFDMA
    reduce cross interference from OBSS via C-BF to further improve spectrum use efficiency
  Manageability: dense deployments found in residential, public or enterprise settings have different management requirements.
    Residential management issues are fewer.
  Mobility:
    enhanced mobility via MLO to reduce transition delay or avoid BSS transition

## Slide 9: Multi-AP and Dense Residential Use Case
We consider especially the dense residential use case for Multi-AP, where:
  Whole house/lot/backyard coverage is desired.
  Large number (hundreds) of fixed and mobile devices, including smartphones, computers, appliances, streaming devices, IoT, etc.
  Small number (~3-5) of AP MLDs.
  OBSS interference likely from neighbors.
  Availability of trusted client devices in physical control. I.e., smartphone or appliances.
  Cost sensitive.

## Slide 10: Coordination Models

## Slide 11: Multi-AP MLDs coordination for Residential Use Cases
Several High-Level Multi-AP Coordination solutions have been presented in TGbe:
  C-SR, C-BF, C-OFDMA . . .[12]13][15][16][17]
  Virtual BSS encompassing multiple MLDs [9][10][14]
We identify Multi-AP MLD Coordination models useful for Residential Use Cases:
  MLD Coordinating distributed Affiliated APs
  MLD to MLD Coordination
    Exchange measurements, reports, announcements using Unicast and/or Broadcast frames between MLDs
  MLDs coordination through a non-AP STA
  Note: more than 1 coordination model may be used at any time.
Multi-AP solution depends on the coordination model used.

## Slide 12: Multi-AP MLD coordination models
  1. MLD Coordinating distributed Affiliated APs
    Improves coverage for the non-AP MLD
    Reduces roaming necessity for non-AP MLD
    Reduces or avoids wideband interference present in one location
    Allows one MLD to control many affiliated APs (A-APs)
    Frequency reuse possibility
Pros:
  Manageability, where:
    MLD as the single coordination point between A-APs
    Information exchange between A-APs through MLD
    Coordination of A-APs by the MLD
    Time sync across A-APs by the MLD if needed
  seamless mobility (without BTM or FT)
Cons:
  Standardize new interface between MLD and A-APs.
A-AP2
A-AP1
EML ESS Manager
/ Gateway
link 1
link 2
IP
UMAC
LMAC
PHY
Non-AP-MLD
LMAC
LMAC
PHY
PHY
UMAC/MLD
Wired or wireless backhaul connection
MLD
LMAC
PHY
A-AP3
Non-AP-MLD
LMAC
PHY

## Slide 13: Multi-AP MLD coordination models
2. MLD to MLD coordination
  MLDs directly coordinate with each other via unicast/broadcast Measurements, reports, announcement frame exchanges.
  With or without time sync across the MLDs
Pros:
  Suitable for small # of AP-MLDs
  Retains on builds on current MLD definition
  Improves coverage for the non-AP MLD
  improves efficiency for non-AP MLD
  Improves spectral efficiency
Cons:
  not scalable

## Slide 14: Multi-AP MLD coordination models
3. MLDs coordinating via non-AP STA(s).
  Each non-AP MLD can provide solicited or unsolicited information to MLDs for coordinating the transmission between it and MLDs
  a non-AP MLD can communicate with multiple AP MLD at the same time and help coordinate ESS resources.
Pros:
  Leverages existing measurement & reports
  Non-AP MLD(s) provide relevant measurements from users/clients
Cons:
  Non-AP STA(s) may not always be available.

## Slide 15: Summary
Coordinated Multi-AP MLD can provide many benefits for Residential use cases:
  Extended coverage
  Reduced cross-interference and improved data throughput & efficiency via C-SR, C-TDMA, C-OFDMA, C-BF
  Seamless mobility to reduce service interruptions
  Enhanced Reliability
Residential Multi-AP Use Case is an important one, for which coordination can be achieved thru:
  MLD Coordinating distributed Affiliated APs
  MLD to MLD Coordination
  MLD coordination through a non-AP STA

## Slide 16: Straw Poll
Do you agree that the UHR SG should include the 3 Multi-AP MLD coordination models on slides 12-14 of 11-22-1512 in the study on PAR and CSD development?
Yes
No
Abstain

## Slide 17: References
11-18/1231r4, “EHT Draft Proposed PAR”
11-22/0708r3, “Beyond be Next Step”
11-22/0961, “Network Operators Perspective on Next Generation WLAN”
11-22/0418, “Considerations of Next-Generation Beyond 11be”
11-22/0685, “Discussion on Next Generation Wi-Fi”
11-22/0932, “Thoughts on Beyond 802.11be”
11-22/0032, “Next-Gen After 11be”
11-22/0965r1, “View on Beyond be”
11-19/1019r0, “Virtual BSS for Multi-AP Coordination”
11-19/1451r1, “Virtual BSS for Multi-AP Coordination Follow-up”
11-19/0772r1, “Multi AP Collaborative BF in IEEE 802.11”
11-20-0107r1, “Multi AP Coordination For Spatial Reuse”
11-20/1040r2, “Coordinated SR For Uplink”
11-20-1247r2, “Virtual BSS for Multi AP Coordination”
11-20/0576r1, “Coordinated Spatial Reuse Protocol”
11-20/0099r1, “Coordinated beamforming for 802-11be”
11-19-1582r2, “Coordinated AP time-and-frequency-sharing-in-a-transmit-opportunity-in-11be”