## Slide 1: Multi AP coordination for next-generation Wi-Fi
Date: 09-12-2022
Authors:

## Slide 2: Abstract
In this contribution, we illustrate how coordination among multiple access points (APs) , especially on time domain, can improve overall system performance and user experience.

## Slide 3: Motivation
IEEE 802.11 has been very popular, and widely deployed in both—
  Personal areas such as home
  Public areas such as office, station, stadium, airport
At a crowded location, several tens of APs are probed at a single location
Interference among different APs’ BSS has been a critical issue for user experience
  STAs in overlapping areas suffer extra interference (e.g., STA2 and STA3 in the figure)
Coordination among neighboring APs may significantly reduce the interference encountered by the STAs [1, 2].
STA2
STA1
STA3
STA4
AP1
AP2
BSS1
BSS2

## Slide 4: TWT Information Sharing (1)
Neighboring APs can share their TWT information in the BSSs for coordinating their transmissions
Such coordination maybe through announcing TWT information of the victim link by the information-sharing AP
Once the neighboring AP receives the TWT information, it can manage its transmission such that interference experienced by the victim STA is reduced.
The neighboring AP can help by--
    muting its transmission to nearby STAs during victim STA’s SP,
    by orthogonalizing its transmission, in time, with SP of the victim STA, or
    backing-off power during the victim STA’s SP(i.e., time-selective spatial reuse).

## Slide 5: Example Scenario
Consider an overlapping BSS scenario where BSS1 is formed by AP1 and BSS2 is formed by AP2.
  STA1 and STA2 are associated with AP1; STA3 and STA4 are associated with AP2
  STA2 has established TWT schedule with AP1
  STA2 is in the cell edge and suffers from interference from AP2
  STA2 recognizes this interference from AP2 and informs AP1 about this perceived interference
  Assuming AP1 and AP2 are within a coordinating set, AP1 shares STA2’s TWT information to AP2, and requests AP2 adjust its transmission so that the transmission window doesn’t overlap with STA2’s TWT SP
STA2
STA1
STA3
STA4
AP1
AP2
BSS1
BSS2

## Slide 6: TWT Information sharing (2)
Synchronized uplink and downlink service times among BSSs involved in coordination can reduce OBSS interference experienced by a STA.
The victim STA may share the TWT information to the interfering AP, which can subsequently adjust its transmission to reduce the interference.
For downlink, a client device can recognize interfering APs during its downlink TWT service times.
  Then, it can transmit an action frame containing its TWT information.
  The neighboring AP can perform sounding in response to the action frame.
  Then, it mitigates interference based on the TWT information and channel information retrieved from sounding.
For uplink, an AP can recognize interfering clients of neighboring BSSs.
  Then, it transmits an action frame requesting those neighboring clients’ TWT information.
  Neighboring clients transmit action frames in response to the request.
  The AP mitigates interference based on the TWT information.

## Slide 7: Coordinating AP
There can be a central AP in the multi-AP coordination set that can collect MAP coordination requests from different APs (or victim STAs), and distribute the TWT information pertaining to the victim STAs among the APs
Coordination can also be contingent on negotiation between.
For example, the neighboring AP may be unable to adjust its transmission based on the coordination request.
Coordinating AP
AP1
rTWT Info of AP 1
rTWT Info of AP 1
AP2
BlockAck
BlockAck
rTWT Info of AP 2
rTWT Info of AP 2
BlockAck
BlockAck

## Slide 8: Quieting neighbour AP’s STAs
STA2
STA1
STA3
STA4
AP1
AP2
BSS1
BSS2
R-TWT
R-TWT
For R-TWT operation, an AP may request to quiet transmission in a neighbor AP’s BSS.
Based on the received coordination request, the neighbor AP can control its transmission in its BSS
  For example, in the figure, STA2 is the victim STA, and informs AP1 about the interference it experiences
  AP1 can request AP2 for coordination to reduce interference to STA2 during its R-TWT SP.
  AP2 may establish a (variant of) quiet interval during the R-TWT SP of STA2;
    STA3 in BSS2 can ignore the (variant of) quiet interval that is intended to protect STA2’s R-TWT SP if STA3’s R-TWT SP overlaps with STA2’s R-TWT SP.
    STA4 can observe the (variant of) quiet interval

## Slide 9: Summary
Multi-AP coordination can be an enabling technology for next generation WLAN systems
Time domain coordination among coordinating APs can provide a simple way to improve overall systems performance.
Neighboring APs can share TWT information of their BSS to reduce OBSS interference experienced by the STAs.

## Slide 10: References
[1] IEEE 802.11-22/932r0, “Thoughts on Beyond 802.11be”, June 2021
[2] IEEE 802.11-22/1046r3, “Multi-AP: TWT Information Sharing”, Sept 2021