## Slide 1: AP initiated EML Operating Mode Change
Date: 2022-09-15
Authors:
Name | Affiliation | Address | Phone | Email
Sunghyun Hwang | ETRI |  |  | shwnag@etri.re.kr
Kyumin Kang | ETRI |  |  | kmkang@etri.re.kr
Juseong Moon | KNUT |  |  | jsmoon0211@ut.ac.kr
Ronny Yongho Kim | KNUT |  |  | ronnykim@ut.ac.kr

## Slide 2: Abstract
CID 12410, 14077, 10157, 10158:
  In certain cases, such as link disablement, etc, AP may need to change EMLSR links with EML OMN procedure.
TID-to-Link mapping may not match with EMLSR Links, when AP MLD changes TID-to-Link mapping (especially, group based TID-to-Link mapping)
  In document 22/1023r5[1], AP Link Disablement, TGbe discussed about broadcast TID-to-Link mapping method
IEEE 802.11be needs to define AP initiated EML Operating Mode changing method

## Slide 3: Issue
If broadcast TID-to-Link mapping is applied, EMLSR Operation in relation with TID-to-Link mapping might be affected.
From 11/1023r5, Page 22 and 23:
An AP MLD may advertise a mandatory TID-to-link mapping by including a TID-To-Link Mapping element in the Beacon and Probe Response frames that the APs affiliated with the AP MLD transmit.
At the time indicated by the Mapping Switch Time field of a TID-To-Link Mapping element in a Beacon or a Probe Response frame received by a STA affiliated with a non-AP MLD from an AP affiliated with its associated AP MLD, the non-AP MLD shall update its TID-to-link mapping according to the rules that establish a TID-to-link mapping in this subclause and with the consequences of the updated mapping defined in 35.3.7.1.1 (General).

## Slide 4: Issue (Continued)
When TID-to-Link mapping is changed, in a certain case, EML Operating mode (EMLSR links) should be reconfigured.
If there are many EMLSR operating non-AP STA MLDs, that are affected from changed TID-to-Link mapping, it’s inefficient for the non-AP STA MLDs to send unicast EML OMN frames.
  Before EML OM reconfiguration, communications for some TID(s) can be blocked due to newly changed TID-to-Link mapping.
  AP initiated method is needed to enhance the inefficiency of unicast STA initiated MLD OMN procedure.

## Slide 5: AP Initiated EML Operating Mode
After TID-to-Link mapping is changed via broadcast method, AP MLD may
  Send unicast EML OMN frames to EMLSR operating non-AP STA MLDs to change or terminate EMLSR operation
  Send broadcast EML OMN frame to EMLSR operating non-AP STA MLDs to change or terminate EMLSR operation

## Slide 6: Conclusion
We discussed AP-initiated EML Operating Mode changing method.
When TID-to-Link mapping is changed by an AP MLD, it’s efficient that the AP MLD initiates to reconfigure EML operation.

## Slide 7: References
[1] 802.11be, Pooya Monajemi, 22/1023r5, “AP Link Disablement”