## Slide 1: Multi-AP Coordination for Low Latency Traffic Delivery
Date: 2022-09-06
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com

## Slide 2: Introduction
Achieving determinism and guaranteed latency over wireless links is challenging especially for Wi-Fi using unlicensed spectrum. Although 11be has specified some features to provide predictable latency and jitter for the delivery of latency sensitive traffic, further enhancements are also expected in future project.
This contribution focuses on the multi-AP coordination for low latency traffic delivery, which may be considered as a candidate technology to reduce latencies, increase manageability for UHR (Ultra High Reliability).

## Slide 3: Background
802.11be Features | Benefits for the delivery of latency sensitive traffic | Application Scope and limitations
Multi-Link Operation (MLO) | increase throughput by aggregating multiple links across different channels or bands (2.4, 5 and 6 GHz). reduce latency by providing multiple channel access opportunities the usage of preferred link(s) for the TID(s) corresponding to latency-sensitive traffic by TID-to-link mapping | Limited to the communication between MLD devices with multiple links. operates using one or more affiliated APs(or STAs) , but has one MAC data service and a single MAC SAP to the LLC sublayer for a MLD each link is located on different nonoverlapping channels
QoS signaling enhancements | QoS parameters in the QoS Characteristics elements carried in SCS Descriptor Multi-link SCS procedure: creation, modification, or deletion of an SCS stream at the MLD level | Limited to QoS signaling between AP and its associated STAs, or AP MLD and its associated non-AP MLD
Restricted TWT (R-TWT) | enables the BSS to use enhanced medium access protection and resource reservation mechanisms | Limited to STAs supporting r-TWT in one BSS OBSS interference is not considered.

## Slide 4: Multi-AP Coordination
Multi-AP operation in Wi-Fi Alliance
  The goal is to expand the network coverage range
  Form a unified network that provides efficient Wi-Fi throughout
  Network architecture, system level functionality
  MAC level coordination of APs’ operation, such as channels, Bandwidth, Security, etc.
Multi-AP Coordination discussed in EHT SG
  The goal is to achieve higher efficiency and higher throughput.
  Multiple modes, such as coordinated OFDMA/MU-MIMO/Beamforming, Joint Transmission etc.
  Strict Time/frequency synchronization is required.
A suggested mode of Multi-AP coordination for UHR
  One suggested goal is to provide higher reliability for delivering low latency traffic including enhanced medium access protection for reserved resource during scheduled time
  The information for the reserved resource and scheduled time needs to be shared among APs
  The operations of APs in their respective BSSs needs to be coordinated to provide enhanced medium access protection
moderate time / frequency synchronization accuracy requirements
Decrease the signaling and data transmissions among multiple APs
Enhance MAC level coordination of APs’ operation
Provide more flexible ways of signaling among APs

## Slide 5: Scenario
Low latency traffic for applications including XR (AR/VR/..) accounts for a large part of the network traffic
More P2P links and transmissions proliferate due to the diversity of client devices, such as phones/watches/glasses/helmet/gaming consoles/displays/cameras, etc.
Overlapping BSS seems to exist unavoidably especially in dense environment due to limited unlicensed spectrum and the application of MLO

## Slide 6: Candidate Solution
Multi-AP Coordination for Low Latency Traffic Delivery
Multiple APs are coordinated to provide enhanced medium access protection
The related information is shared among APs, such as the resource to be protected and the interfering STAs
Action to protect the resource reserved by neighboring BSS is taken for the interfering STAs, such as
the interfering STAs stop its TXOP before the start time of the scheduled time
limit the transmission initiated by the interfering STAs during the scheduled time.

## Slide 7: Summary
Further enhancements to the features for the delivery of low latency traffic are expected in UHR SG.
A mode of Multi-AP coordination is suggested to provide higher reliability for delivering low latency traffic including enhanced medium access protection for reserved resource during scheduled time across different co-channel BSSs.

## Slide 8: Reference
[1] IEEE 802.11be Draft 2.1.1
[2] 11-22-0729-01-0wng-next-generation-after-802-11be-follow-up
[3] 11-22-0779-00-0wng-802-11bx-enabling-metaverse-metaverse-ar-vr-and-wearables
[4] 11-22-0634-02-00be-802-11be-enhancements-for-tsn-time-aware-scheduling-and-network-management-considerations
[5] 11-18-1509-00-0eht-features-for-multi-ap-coordination
Liuming Lu (OPPO)