## Slide 1: Discussion on LB266 CR for CID 13942
Date: 2022-10-17
Authors:
Name | Affiliation | Address | Phone | Email
Yanyi Ding | Panasonic Corporation |  |  | yanyi.ding@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 
Rajat Pushkarna |  |  |  | 

## Slide 2
CID 13942
CID | Clause | Category | Page | Comment | Proposed change
13942 | 35.5.2.4 | T | 489.29 | In 26.5.2.5 UL MU CS mechanism, it is regulated that in a TB UL MU transmission, if CS requirement is indicated, ED-based CCA shall be performed by STAs on 20MHz subchannels overlapping the allocated RU/MRU. If any of the 20MHz subchannels is detected as busy, STA does not transmit TB PPDU at the allocated RU/MRU. Large-size RU/MRU is wasted even if a small number of 20MHz subchannels is detected as busy. (Refer to 20/1886r1 for more details.) | STAs should be enabled to adapt allocated RU/MRU according to ED-based CCA results. Commenter will bring a contribution.

## Slide 3
Background
In TB UL MU transmission described in 26.5.2.5, if CS requirement is indicated in the Trigger frame, ED is used to sense the medium by STAs on 20MHz subchannels overlapping the allocated RU/MRU.
If any of the 20MHz subchannels is indicated as busy by ED-based CCA or virtual CS, the STA does not transmit TB PPDU at the allocated RU/MRU.
Whole allocated large-size RU/MRU is wasted even if only a small number of 20MHz subchannels are detected as busy, which would degrade system throughput.

## Slide 4
Recap of the proposed solution
In 20/1886r1 we analyzed the problem and proposed an RU Adaptation procedure to address it.
In an RU adaptation procedure, a non-AP STA may puncture allocated RU/MRU according to the state of the medium. (Not applicable to MU-MIMO transmission)
  Only the RU/MRU is punctured, other parameters for TB UL transmission remain unchanged.
In this case, the waste of large-size RU/MRU can be avoided.
Example

## Slide 5
SP Result

## Slide 6
Signaling options
Signaling options for the EHT TB PPDU to indicate punctured RU/MRU.
  Option 1: no explicit signaling
    Blind decoding/ Signal detection of pre-EHT modulated fields in all 20MHz subchannels.
  Option 2: explicit signaling
    TB puncturing is explicitly signaled in U-SIG field of EHT TB PPDU
    Detailed TB puncturing signaling is TBD.

## Slide 7
Discussion
As discussed in 20/1886r1, the RU adaptation procedure can improve throughput of TB UL MU transmission with large-size RU/MRU.
Changes in spec may include:
  Signalings in Trigger frame and EHT TB PPDU.
  Ways for AP to decode EHT TB PPDU transmitted on punctured RU/MRU.
    With or without explicit signaling in U-SIG.
  Capabilities elements.
If adopted, the feature will be optional. R1 STAs will not be affected.

## Slide 8
SP#1
Do you agree that 11be should support RU adaptation procedure?
  Non-AP STAs may puncture allocated RU/MRU for EHT TB PPDU according to ED-based CCA results when it is not MU-MIMO transmission.
Y/N/A:

## Slide 9
SP#2
Which signaling option do you prefer for punctured EHT TB PPDU?
  Option 1: no explicit signaling (AP may decode the EHT TB PPDU by blind decoding or preamble detection)
  Option 2: explicit signaling (AP may decode the EHT TB PPDU following TB puncturing information in U-SIG field)
Option 1/Option 2/A:

## Slide 10
Annex:
details about punctured RU/MRU

## Slide 11
Punctured RU/MRU
Associated Punctured RU/MRU for each large-size RU/MRU
  Associated Punctured RU/MRU is a set of possible options of punctured RU/MRU where the STA shall choose from when a large-size RU/MRU is allocated.
  Some restrictions may be enforced, for example, set a threshold for the size.
Example (the size of associated punctured RU/MRU shall not be smaller than 50% of the size of allocated RU/MRU)
BW (MHz) | RU/MRU Larger Than 242 Tones | Associated Punctured RU/MRU
40, 80, 160/80+80, 320 | RU484 | RU484, RU242 (2 options)
80, 160/80+80, 320 | RU242+RU484 | RU242+RU484, RU484
80, 160/80+80, 320 | RU996 | RU996, RU242+RU484 (4 options), RU484 (2 options)
160/80+80, 320 | RU484+RU996 | RU484+RU996, RU996, RU484+RU242 (4 options)
… | … | ...
* When part of the allocated RU/MRU which is detected as idle does not match or cover any of its associated punctured RU/MRU, the allocated RU/MRU shall not be punctured.