## Slide 1: Enhancement of RRCM
Date: 2022-12-1
Authors:

## Slide 2: Abstract
1802r0 provides the enhancement of the current Rule-based Random and Changing MAC (RRCM) proposal 818/r4
  Basically, enhancement is that when a non-AP STA associates with AP, non-AP STA and AP generate and store a secret key (i.e. RMAK, the key that is the same key to generate RMAs) to protect some of the pre-association management frames when the non-AP STA returns to the same ESS.
This document provides a detailed description of the protection mechanism:
  In short, the non-AP STA and AP should send an IE (i.e.Validation information Element - VIE) attached to (some) pre-association management frames.
    Some pre-association management frames may include authentication/association frames.
  VIE should include Packet Number IPN (to avoid replay attack), MIC (for validation) that is calculated based on the stored key, and keyID.

## Slide 3: Basic idea
Non-AP STA
AP
1st Assoc
Send frames with RMAs and VIE
2nd Assoc
Generate and store RMAs (RRCM procedure)
- Use RMA key (RMAK) to generate RMAs, and store RMAK
Use stored RMAK to construct VIE

## Slide 4: RMA key (RMAK)
RMAK is already defined to generate RMAs.
RMAK will be used to construct VIE as well.
RMAK = KDF-Hash-256(KDK, "RMA Key", Min(ANonce, SNonce) || Max(ANonce, SNonce) This key is generated at AP and non-AP STA, and stored at both sides.

## Slide 5: Validation Information Element (VIE)
VIE has a similar format to MME (Management MIC element)
Some differences between MME and VIE include:
  MME is constructed based on IGTK, BIGTK, or WIGTK; VIE is constructed based on RMAK (note that both schemes use AES-128-CMAC)
  IPN (Integrity Packet Number) values should be kept differently, i.e. different replay counters
MME
Element ID | Length | IPN | MIC
VIE
1 | 1 | 6 | 8
*Previously known as MMIE

## Slide 6: Validation Information Element (VIE)
Construction of MPDU with VIE (similar to BIP MPDU construction)
Header | Payload with VIE | FCS
Obtain the key RMAK: 4e a9 54 3e 09 cf 2b 1e ca 66 ff c5 8b de cb cf
Construct - AAD (FC | A1 | A2 | A3): d0 04 | aa aa aa aa aa aa | bb bb bb bb bb bb | cc cc cc cc cc cc - Frame Body: 02 00 - VIE (with MIC=0): 4c 10 00 00 00 00 00 00 00 00 00 00 00 00 00 00
Element ID | Length | IPN | MIC
1 | 1 | 6 | 8
Calculate MIC using RMAK: MIC=AES-128-CMAC(AAD | Frame Body | VIE (with MIC=0): a1 b1 c1 d1 e1 f1 g1 h1
Construct the MPDU
Header | Payload with VIE | FCS
Payload | VIE
Element ID | Length | IPN | MIC
4c | 10 | 00 00 00 00 00 00 | a1 b1 c1 d1 e1 f1 g1 h1

## Slide 7: Putting all together (e-RRCM)
Non-AP STA
AP
1st Assoc
Send frames with RMAs and VIE
2nd Assoc
Generate RMAK
Header (RMA1) | Payload | VIE
Generate RMAK
Send {Counter, Seed} in 4-way HS Msg2
Generate RMA(s) (e.g. RMA1)
Generate RMA(s) (e.g. RMA1)
Store RMA(s) and RMAK
Store RMA(s) and RMAK
Non-AP STA uses stored RMAK to construct VIE
AP check VIE to validate non-AP STA.

## Slide 8: Summary
An enhanced mechanism is provided for RRCM solution.
  In the enhancement, when the non-AP STA associates with AP and generates RMAs for future use, it stores RMA(s) and RMAK for future use.
  When non-AP STA associates with AP again, in addition to using previously generated(stored) RMA(s), non-AP STA attaches VIE to its management frames (constructed with stored RMAK)
  By attaching VIE into management frames, AP makes sure (validate) that the frames come from the legitimate non-AP STA. (avoiding MAC spoofing, replay attack etc).

## Slide 9
Thanks 