## Slide 1: How to Use the Opaque Blob
Date: 2022-11-15
Authors:

## Slide 2: Abstract
Explanation of the intent of the opaque identifier scheme in Appendix Z

## Slide 3: Background
Opaque identifier is generated by network for STA
To the STA, it’s just a blob, not the real identity
To the network, the blob is not an identity either
The blob is a mechanism to transport the device’s identity in a secure manner that prevents tracking:
  A passive attacker cannot determine a device identity
  A passive attacker cannot connect device identities across associations
  Identifiers can be arbitrarily padded to foil passive traffic analysis
  Identities are secure under a reasonable birthday bound (which will depend on the size of the tweak and the how the pad size varies)
  An attacker cannot substitute identifiers to connect distinct associations
  An AP needs to only manage a single symmetric secret, used to protect all identities used in the ESS, and 8 octets per allocated device ID
  All APs in the ESS can share the same symmetric key (in an out-of-band fashion)
  Minimal overhead—e.g. 16 octet tag + 8 octet tweak + 1 octet pad length + padding = 25 octets plus padding
  Uses symmetric cryptography for speed and DOS resistance
  Each identifier is unique to the ESS it was obtained from, a given ESS will have no knowledge of the identifiers used in other ESSs
  Identifiers cannot be tracked across networks

## Slide 4: Blob Must Be Used Outside of 4way HS
DevIDs passed in 4way
4way requires PMK
PMK uniquely identifies STA already*
How is PMK est.?
  Some authentication protocol
That protocol will use the blob to hide its ID
STA AP
DevID
DevID
*Assuming not WPA-PSK
blob

## Slide 5: How It works
There is a bootstrapping step that’s not in the draft
  the “first” blob can be provisioned– e.g. with DPP– or it can be obtained on first connection when real ID is passed in the clear
The blob is used when the device wants to inform the network of it’s true identity in a manner that is not trackable
Blob will be passed outside of 4way HS by whatever protocol needs a non-trackable identifier
Assuming an opaque blob exists
  Let’s say the user is bob@example.com, that’s his true identity
  The opaque blob is 891b52f0725635f3abc8a6b13159df5afbf0a
Bob’s identity for himself and the network is always bob@example.com but he can use the blob like this…

## Slide 6
891b52f0725635f3abc8a6b13159df5afbf0a
bob
AP (“the network””)
SAE auth req, id= 891b52f0725635f3abc8a6b13159df5afbf0a
de-blobification
891b52f0725635f3abc8a6b13159df5afbf0a
bob@example.com
“Oh, it’s bob, I’ll
authenticate him”
Finish SAE authentication
blobification
4way Handshake
Message 2 : 891b52f0725635f3abc8a6b13159df5afbf0a
SAE
“It’s still bob, I’ll
give him a new blob”
bob@example.com
Message 3: a35792f3492ce34b7923f4619a2dd2343ca4752349f52
a35792f3492ce34b7923f4619a2dd2343ca4752349f52
“my new blob!”

## Slide 7
a35792f3492ce34b7923f4619a2dd2343ca4752349f52
bob
AP (“the network””)
SAE auth req, id= a35792f3492ce34b7923f4619a2dd2343ca4752349f52
de-blobification
a35792f3492ce34b7923f4619a2dd2343ca4752349f52
bob@example.com
“Oh, it’s bob, I’ll
authenticate him”
Finish SAE authentication
blobification
4way Handshake
Message 2 : a35792f3492ce34b7923f4619a2dd2343ca4752349f52
SAE
“It’s still bob, I’ll
give him a new blob”
bob@example.com
Message 3: 983a95c47f63bb945396624726394fac34763de4973499a46
983a95c47f63bb945396624726394fac34763de4973499a46
“my new blob!”

## Slide 8: More Text May Be Needed
Description of using blobs in current protocols for which identifiers are important but allow tracking
  Candidate protocols use an ID and a credential
  SAE password identifiers definitely, but what else?
Do we need to explain how blobs are bootstrapped?
  Add an “I’d like a blob so I don’t have to use that cleartext identifier I used when authenticating” message in the 4way HS? Opt-in!
  Have informative text describing out-of-band bootstrapping?

## Slide 9: Backup

## Slide 10: Generation of Blob
Slide 10
AES-SIV
key
device identifier:
bob@example.com
4000bob@example.com
padded:
tweaked:
71a08cf14000bob@example.com
blob:
891b52f0725635f3abc8a6b13159df5afbf0a

## Slide 11: References
11-21/0488
11-21/0541