## Slide 1: mmWave Phase Feedback
Date: 2023-02-15
Authors:
Name | Affiliation | Address | Phone | Email
Kevin Tsunghan Tsai | Mediatek Inc | 2840 Junction Ave, San Jose, CA 95134, USA |  | kevin.tsai@mediatek.com
Dennis Liu |  |  |  | dennis.liu@mediatek.com
Shuling (Julia) Feng |  |  |  | julia.feng@mediatek.com

## Slide 2: Introduction
Vital sign det. includes breathing rate and heart rate detection and can be used in many health applications
Vital sign is one of 11BF use cases [1]
  Health case - remote diagnostics measurements
  of breathing rate, heart rate etc.
STA1
STA2
STA3
AP: Initiator
feedback
feedback
feedback
detection
detection
detection

## Slide 3: Vital Signs Detection by Phase
Chest up and down is a small distance variation
  Small distance variations cause signal traveling different distances and result in phase variations at target bin
  Hence, we propose to add target bin phase as a report type for vital sign detection
velocity
time
Distance
inhale
exhale
Freq
FMCW
time
Range
Mag.
Phase=
Phase=
Phase=
Phase=
time
Phase of bin
inhale
exhale
  FMCW , ,
  =
Find the variation period of target bin can get breathing rate
TX chirp
RX chirp
= ,=
frame0
frame1
frame2
frame3
velocity
Range
Mag.
velocity
Range
Mag.
velocity
Range
Mag.

## Slide 4: Breathing rate detection by doppler
Breathing rate is 0.1-0.6 Hz (6-36 times per minute) [3][4]
Chest displacement due to respiration between 0.004 and 0.012m[3]
time (sec)
exhale
-
inhale
1
2
3
4
time (sec)
exhale
inhale
1
2
3
4
-
Assume it need resolution 0.004m/sec to detect respiration rate
If we use 40us chirp and 1ms interval per chirp,
  Vres=/2Tf=C/Fc/2Tf=3e8/60e9/(2*1e-3*1024)=0.0024m/s
  Vmax=/4Tc=C/Fc/4Tc=3e8/60e9/(4*1e-3)=1.25m/s
It need 1.024 sec to get a measurement for such high resolution , it can detect rate< 0.5Hz (Breathing rate is 0.1-0.6 Hz )
Example for respiration rate 0.25Hz

## Slide 5: Heart rate detection by doppler
Heart rate is 0.8–3 Hz(60 to 180 times per min)[3][4]
Chest displacement due to Heart rate alone ranges between 0.0002 and 0.0005 m[3]
time (sec)
exhale
1/4
2/4
3/4
1
time (sec)
Example for Heartbeat 1Hz
inhale
1/4
2/4
3/4
1
-
Assume it need resolution 0.0002m/sec to detect heart rate
If we use 40us chirp and 1ms interval per chirp,
Vres=/2Tf=C/Fc/2Tf
=3e8/60e9/(2*1e-3*16384)=0.00015m/s
Vmax=/4Tc=C/Fc/4Tc=1.25m/s
It need 16.384 sec to get a measurement for such high resolution ,so it’s impossible to be used to detect a 0.8~3Hz signal (Heart rate )
Using phase to detect heartbeat don’t need such high velocity resolution, hence it can detect higher freq. signal

## Slide 6: mmRadar for Breathing/Heartbeat[2]
This page describe the equation for radar T/Rx Signal for next page’s
The transmitted signal of the FMCW radar can be expressed as
  is the starting frequency of the chirp signal, is the bandwidth, TX is the amplitude of the transmitted signal, (t) is the phase noise, is the width of chirp signal pulse
The distance from the chest to the radar is , is the motion displacement of the chest , d0 is the distance from the radar sensor to the human body ,and the time delay is ,causing by the distance ,where c is the light speed. Then, the received signal is

## Slide 7: mmRadar for Breathing/Heartbeat[2]
The echo signal and the transmission signal are mixed by two orthogonal I/Q channels, and then passed through a low-pass filter to obtain an IF signal
  Detect can get distance
  (t) varies with R(t) phase varies with R(t), the displacement of chest
R(t) will be very small, and it approximates a constant in a single chirp
Multiple chirps should be transmitted in sequence to obtain the chest displacement information, which is equivalent to sampling R(t)

## Slide 8: Vital Sign Report
Phase report has not yet been defined in 11bf mmWave image report or target report
  Vital sign detections can be obtained by FFT operations on phases of target range bins during a Range-Doppler like processing.
Image Report
NO | Feedback inform
1 | Range in mm
2 | Range Span
3 | Azimuth in 360/2048 degree
4 | Azimuth Span
5 | Elevation in 360/2048 degree
6 | Elevation Span
7 | Radial Velocity in mm/sec
8 | Azimuth Velocity in (360/2048 degree)/sec
9 | Elevation Velocity in (360/2048 degree)/sec
Target Report
    9.4.2.329.4 DMG Sensing Targets Report Data subelement

## Slide 9: mmRadar for Breathing/Heartbeat
Breathing Detection test
  Using phase variation to calculate breathing rate
FFT
Breathing rate~=17 per min

## Slide 10: Signaling
During sensing measurement setup, let responder know to feedback phase
  Extend original option with phase or use Reserved bit in Measurement Setup Control field format
  Table 9-401w—Report Type subfield definition(#84)
Value | Description
0 | No report
1 | CSI
2 | DMG Sensing Image Direction
3 | DMG Sensing Image Range-Doppler
4 | DMG Sensing Image Range-Direction
5 | DMG Sensing Image Doppler-Direction
6 | DMG Sensing Image Range-Doppler Direction
7 | DMG Sensing Image Direction Phase
8 | DMG Sensing Image Range-Doppler Phase
9 | DMG Sensing Image Range-Direction Phase
10 | DMG Sensing Image Doppler-Direction Phase
11 | DMG Sensing Image Range-Doppler Direction Phase
12 | Target
9-255 | Reserved
Figure 9-1002bm—Measurement Setup Control field format

## Slide 11: Signaling
An indicator to enable report phase or not
    Figure 9-1002cb—DMG Sensing Image Report Data element format
    Figure 9-1002cc—Axis & Phase Present field format
Subelement ID | Length | Data Block SN | Axis Present | Reflection Power Bias | Reflection Power Slope
Number of Reflection Subelements | Reflection Subelements | Reserved
Octets: 1 1 1 1 1 1
Octets: 3 variable variable
Range Axis Present | Doppler Axis Present | Receiver Beam Index Present | Transmitter Beam Index Present | Reflection Phase Present | Reserved
Bits: 1 1 1 1 1 3
B0 B1 B2 B3 B4 B5 B7

## Slide 12: Phase Report for Vital Sign Detection
Axis #1 | Axis #2 | Reflection Power | Reflection Phase
Bits: S1 S2 12 11
Figure 9-1002cd—Reflection subelement format for 2 axes
Axis #1 | Axis #2 | Axis #3 | Reflection Power | Reflection Phase
Bits: S1 S2 S3 12 11
Figure 9-1002ce—Reflection subelement format for 3 axes
Axis #1 | Axis #2 | Axis #3 | Axis #4 | Reflection Power | Reflection Phase
Bits: S1 S2 S3 S4 12 11
Figure 9-1002cf—Reflection subelement format for 4 axes
Refer to Azimuth/Elevation angle report, using (360/2048) ° resolution

## Slide 13: Summary
Vital sign detection is one of 11BF use cases
Propose to add phase report in (E)DMG report elements for vital sign detection
  Add phase report in image report or target report

## Slide 14: SP1
Do you agree to add the following to 11bf SFD:
  The 11bf amendment shall add an option to report Phase in image report
    Y
    N
    Abstain

## Slide 15: SP2
Do you agree to add the following to 11bf SFD:
  Add one option field “Reflection Phase” in Reflection subelement format , the number of bits is 11bits
    Y
    N
    Abstain

## Slide 16: Reference
[1] 11-20-1712-01-00bf-wifi-sensing-use-cases
[2] Y. Wang, W. Wang, Mu Zhou, A. Ren, Z. Tian, “Remote Monitoring of Human Vital Signs Based on 77-GHz mm-Wave FMCW Radar”, Sensors, 2020
[3] D. Obeid, S. Sadek, G. Zaharia, and G.E. Zein,”Doppler radar for heartbeat rate and heart rate variability extraction”, E-Health and Bioengineering Conference (EHB), 2011
[4] M. Alizadeh, G. Shaker, J. C. M. De Almeida, P. P. Morita and S. Safavi-Naeini, "Remote monitoring of human vital signs using mm-wave fmcw radar", IEEE Access, 2019.