## Slide 1: Device Identifier Status Codes
Date: 2023-01-10
Authors:
Name | Affiliations | Address | Phone | E-mail
Kurt Lumbatis | Commscope |  |  | Kurt.Lumbatis@commscope.com

## Slide 2: Abstract
Definition of Device Identifier Status Codes and locations.

## Slide 3: Versions
R0 – Initial Version
R1 – Discussion 1/10/2023

## Slide 4: Overview
Suggestions to Add Device Identifier Status Field to
  Device ID element in (Re)Association Request frame
  Device ID element in Association Response frame
  Device ID KDE Message 2
  Device ID KDE Message 3
This proposal seeks to Define this Status Field

## Slide 5: Device ID Element
Per 9.4.2.296a of the IEEE P802.1bh D0.2, 9.4.2.296a Figure 9-1002a the Device ID element is defined as:
I propose the following change
 | Element ID | Length | Element ID Extension | ID Blob
Octets | 1 | 1 | 1 | variable
 | Element ID | Length | Element ID Extension | Identifier Status | ID Blob
Octets | 1 | 1 | 1 | 1 | variable

## Slide 6: Device ID Element Status Code Table
An additional Table will be necessary to define the contents of the Identifier Status in 9.4.2.296. I propose a table be added to this section. Note this table may be utilized as both a Status Indication as well as a command.
Status Code | Name | Meaning
0 | Success/NOP | Identifier recognized or assigned
1 | Not Recognized | Identifier not recognized
2 | Request/Provide Text Based Identifier | STA Requests a new Textual Identifier
3 | Request MADD MAC Address (e.g.) | STA wants to utilize MADD Address

## Slide 7: Device ID KDE Element
Per 12.7.2 EAPOL-Key frames of the IEEE P802.1bh D0.2, 9.4.2.296a Figure 12-48a the Device ID KDE element is defined as:
I propose the following change
The Status will cross reference the table added in 9.4.2.296a
 | ID BLOB
Octets | Variable
 | Identifier Status | ID BLOB
Octets | 1 | Variable

## Slide 8: References