## Slide 1: AIML TIG Status Report
Date: 2023-01-10
Authors:

## Slide 2: Abstract
Status report for the AIML (Artificial Intelligence Machine Learning) TIG

## Slide 3
Overview
AIML TIG and its mandate
AIML TIG goals and activities
Highlights of AIML use cases identified for IEEE 802.11 WLANs
Conclusions
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 3

## Slide 4
AIML TIG and its mandate
The AIML TIG is formed by the following WG motion in the July 2022 session [1]:
  Motion 5: TIG Re: AI/ML use in 802.11
  Approve formation of a Topic Interest Group (TIG) to:
  (a) describe use cases for Artificial Intelligence/Machine Learning (AI/ML) applicability in 802.11 systems and
  (b) investigate the technical feasibility of features enabling support of AI/ML.
  The TIG is to complete a report on this topic at or before the March 2023 session.
  Moved: Stephen McCann, Second: Marc Emmelmann
  Result: Yes: 119, No: 22, Abstain: 27 (Motion passes)
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 4

## Slide 5
AIML TIG Goals and Activities
The goals for the AIML TIG are NOT to define or standardize AIML models
AIML TIG has been fortunate to have some AIML experts providing tutorials
Tutorials are valuable to provide background on AIML and academic research available on the topic
Tutorials provide an understanding of AIML, supporting the TIG’s standards-focused work
The goals and work for the AIML TIG closely follow our mandate
Study and describe AIML use cases that are applicable to 802.11 networks
With a strong focus on standards impact on IEEE 802.11 specs
For each use case, the following aspects are being defined:
  Standards impact
  KPIs
  Requirements
  Technical feasibility
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 5

## Slide 6
Highlights of AIML Use Cases Identified for WLANs (1)
We highlight in this report AIML use cases that have technical report text proposals
  AIML-based CSI Feedback Compression [3]
  Deep-learning based distributed channel access [4]
  Efficient AIML model sharing [5]
Additional use cases may be included in the technical report when technical report text proposal is available
  E.g., ML-based adaptive subcarrier grouping for beamforming feedback [6]
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 6

## Slide 7
Highlights of AIML Use Cases Identified for WLANs (2)
AIML-based CSI Feedback Compression [3]
Sounding procedures in WLANs represent large overhead particularly with potential new features:
  Higher number of spatial streams, e.g., 16
  Multi-AP features such as joint transmissions
Study has shown that AIML algorithms may efficiently reduce CSI feedback and improve system throughput
  E.g., using unsupervised learning algorithms to significantly reduce CSI feedback into clusters while maintaining similar PER performance
Standards impact:
  Additional signaling between AP an STAs required by AIML process to provide feedback and cluster information
KPIs:
  CSI airtime reduction/additional AIML process overhead
  PER
  Computation complexity/latency
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 7

## Slide 8
Highlights of AIML Use Cases Identified for WLANs (3)
Deep-learning based distributed channel access [4]
Performances of traditional WLAN channel access designs such as DCF degrade in dense deployment, unable to support stringent QoS requirements such as
  Ever increasing throughput
  Low latency
Study has shown that deep learning algorithms can efficiently increase throughput and reduce latency and jitter while maintain fairness to other devices
  E.g., using Deep reinforcement learning for contention window optimization
  E.g., AIML algorithm selects whether to transmit after the channel has been idle for DIFS
Standards impact:
  Signaling and protocols related to parameter exchange between AP and non-AP STAs, e.g., capability indication, data report to facilitate training, neural networks parameters distribution, etc.
KPIs:
  Throughput improvement
  Latency and jitter reduction
  Additional complexity
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 8

## Slide 9
Highlights of AIML Use Cases Identified for WLANs (4)
Efficient AIML model sharing/distribution [5]
Efficient AIML model distribution is essential for many AIML-based operations in WLANs and for performance of WLANs
  In centralized learning/federated learning, large amount of traffic are used to distribute AIML models/training data among participating devices (STAs and APs), in UL, DL and P2P links
  Efficient AIML model distribution protocols are needed to enable support AIML operations
    Including sharing of all AIML models (e.g., for other applications; these model sharing is expected to be carried by WLANs anyway), not just for models used to improve WLAN performance
Efficient AIML model distribution can leverage the broadcast nature of WLANs
  802.11bc defines UL/DL broadcast services for both associated and unassociated STAs/APs, providing a good set of baseline tools for AIML model distribution
Standards impact:
  Architecture that enables AL/ML model sharing on the MAC layer
  Signaling and protocols related to AIML model sharing support/capability indication and management
KPI: medium occupation time saving compared to model sharing using application layer data
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 9

## Slide 10
Conclusion
The AIML TIG’s activities closely follow our mandate
Study and describe AIML use cases that are applicable to 802.11 networks
With a strong focus on standards impact on IEEE 802.11 specs
  i.e., changes needed to enable/utilize/facilitate AIML operations in current 802.11 specs
AIML TIG is not defining/specifying AIML models
AIML TIG is diligently working on the technical report to the WG
For a better understanding of AIML TIG’s effort, WG members are invited to read the proposed AIML TIG technical report text [2][3][4][5]
AIML TIG plans to discuss the next steps soon
For any questions, please feel free to reach out to me
Xiaofei.wang.us@ieee.org
January 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 10

## Slide 11: References
[1] 11-22/597r3: May 2022 Working Group Motions, May 18, 2022
[2] 11-22/987r3: AIML TIG Technical Report Draft
[3] 11-22/1934r5: Proposed AIML TIG Technical Report Text for the CSI Feedback Compression Use Case
[4]11-22/2119r1: Proposed AIML TIG Technical Report Text for the Distributed Channel Access Use Case
[5] 11-23/0050r2: Proposed AIML TIG Technical Report Text for the AIML Model Sharing Use Case
[6] 11-23/0032r3: ML-based Adaptive Subcarrier Grouping for Beamforming Feedback