## Slide 1: PAR discussion
Date: 2023-01-14
Authors:

## Slide 2: Focus on PAR section 5.2.b. Scope of the project
This is the section in the PAR that defines the objectives/KPIs of the project
  Example for 11be:
    This amendment defines standardized modifications to both the IEEE Std. 802.11 physical layers (PHY) and Medium Access Control Layer (MAC) that enable at least one mode of operation capable of supporting a maximum throughput of at least 30 Gbps, as measured at the MAC data service access point (SAP), with carrier frequency operation between 1 and 7.250 GHz while ensuring backward compatibility and coexistence with legacy IEEE Std. 802.11 compliant devices operating in the 2.4 GHz, 5 GHz, and 6 GHz bands.
    This amendment defines at least one mode of operation capable of improved worst case latency and jitter.
Few questions to answer:
  Do we list other objectives in addition to throughput and latency objectives?
  Do we quantify the objectives?
  Can we make objectives independent on band support?

## Slide 3: Do we list other objectives in addition to throughput and latency objectives?
Main objectives/KPIs should be along those lines:
  Improve worst-case latency
  Increase throughput at different SNR levels
Term “reliability” is hard to define but good to include in the text
  Mostly seen as ensuring throughput/latency constraints in a defined environment (including dense environments for instance), points to multiple objectives
  Solution is to mention it as the high level objective and is achieved through the resolution of the main objectives mentioned above
Do we need to add other objectives/KPIs:
  We need to make sure we keep the number of objectives as low as possible
  Manageability is very blurry/unclear: suggest to not mention it
  Many requests to mention reduced power consumption or enhanced P2P operation

## Slide 4: Do we quantify the objectives/KPIs?
Latency and jitter targets are very difficult to quantify in a meaningful way:
  The only-really-quantifiable value would be the min latency obtained without contention just by calculating the over the air transmission of a predefined payload
    This however doesn’t capture the real goal of the latency improvements which needs to account for all factors influencing latency: channel access delays in congested environments and so on…
    Therefore not useful nor relevant
  If we include mmWave in the scope, such value would be more realistic as, even in dense environments, a pair of STAs can find a channel free of interference
    That however makes quantification dependent on whether mmWave is supported or not.
Throughput targets are also hard to quantify if we move away from peak throughput
  In lower band, peak throughput increase will be difficult to obtain realistically
  With mmWave, such peak throughput increase would be easy to quantify
    That however makes quantification dependent on whether mmWave is supported or not
  Better to qualify throughput improvements as throughput at different SNR levels, and likely stay vague on quantification of improvements compared to previous amendments
Unless really needed for marketing reasons (which doesn’t seem to be the case), the work in UHR TG will be the same whether we quantify or not the objectives/KPIs, and not quantifying them is simpler and more pragmatic

## Slide 5: Can we make objectives/KPIs independent on band support decision?
Decision on inclusion of mmWave in the scope of UHR will happen in March
  Decision with important implications and the analysis takes time
It would be very valuable to decorrelate the definition of objectives/KPIs from the decision on band support
  Can make good progress on objectives/KPIs in January
That implies not quantifying the objectives, which as expressed in previous slide, is recommended anyway
This way, only the sentence mentioning the target bands will need to be adjusted depending on the decision on mmWave support

## Slide 6: Convergence on KPI/Objectives in section 5.2
Comments/Requests received from the SG regarding KPI/Objectives in section 5.2
  Some request for quantification Note with TBD included – will be resolved later
  Ensure RvR is captured Included
  More efficient use of medium Included
  Request for M-AP being captured As agreed with commenters, features are not included in scope section
  Request for OBSSs scenario Included as scenario description
  Improve roaming topic included as scenario description
Issue of UHR naming to respect Nescom convention
  Raised by Lei/Dorothy
  Orthogonal from discussion in section 5.2
  Working on a solution for this

## Slide 7: Initial proposal for discussion
Objectives/KPI part (can be finalized in January):
This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control (MAC) that enhance Wireless Local Area Network (WLAN) reliability by enabling:
  at least one mode of operation capable of increasing throughput, as measured at the MAC data service, at different SINR levels (Rate-vs-Range), compared to 802.11be
  at least one mode of operation capable of improving tail latency and jitter compared to 802.11be including scenarios of overlapping BSSs and mobility between BSSs
  more efficient use of the medium compared to 802.11be
  Additionally, the amendment will also provide mechanisms for enhanced power save and improved P2P operation.
  Note: quantifying target values and corresponding metrics (units) are TBD

## Slide 8: Initial proposal for discussion
Band support/coex… part (simply adjusted based on mmWave support decision in March):
with carrier frequency operation between 1 and 7.250 GHz and between 42.5 and 71 GHz. This amendment shall ensure backward compatibility with legacy IEEE802.11 devices in the 2.4, 5 and 6 GHz unlicensed bands, and coexistence with legacy IEEE802.11 devices in all unlicensed bands.
  Italic part to capture mmWave bands

## Slide 9: Straw Poll
Do you agree to use the following as an initial draft for the description of the objectives/KPI part in section 5.2.b. Scope of the project of the UHR PAR (band support part will be discussed separately in March):
This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control (MAC) that enhance Wireless Local Area Network (WLAN) reliability by enabling:
  at least one mode of operation capable of increasing throughput, as measured at the MAC data service, at different SINR levels (Rate-vs-Range), compared to 802.11be
  at least one mode of operation capable of improving tail latency and jitter compared to 802.11be including scenarios of overlapping BSSs and mobility between BSSs
  more efficient use of the medium compared to 802.11be
  Additionally, the amendment will also provide mechanisms for enhanced power save and improved P2P operation.
  Note: quantifying target values and corresponding metrics (units) are TBD
Notes: at least one mode of operation capable of improved support, compared to 802.11be, for applications with stringentworst-case latency and jitter requirementscompared to 802.11be // i.e., avoid “worst-case”