## Slide 1: Follow-up on 320MHz NTB/TB ranging
Authors:
Name | Affiliations | Address | Phone | email
Yanjun Sun | Qualcomm |  |  | 
Ali Raissinia |  |  |  | 
Steve Shellhammer |  |  |  | 
George Cherian |  |  |  | 
Christine Zhang |  |  |  | 
Youhan Kim |  |  |  | 
Date: 2023-03-15
March 2023

## Slide 2: Introduction
Background:
  802.11az has been developed over 802.11ax and supports up to 160 MHz bandwidth
Motivation:
  320 MHz operation has been defined in 802.11be
  320 MHz BW can offer better resolution than 160 MHz BW in ranging
Objective:
  Expand appropriate 11az frames and procedures with 320 MHz support
Jan 2023

## Slide 3: Scope of This Contribution
Focus on MAC related changes
Explore options to indicate 320 MHz BW in the following frames:
  Ranging NDPA
  Ranging Trigger variants
  IFTMR/IFTM for session negotiation
Assumptions:
  May support some non-OFDMA puncturing patterns (see [1])
    Some regions may only have 240 MHz bandwidth
    Still offers better accuracy than 160 MHz BW
  Frame exchange sequence are expected to remain the same as in 11az to maximize the reuse of existing logics
Jan 2023

## Slide 4: NDPA Enhancement

## Slide 5: Recap: 11az Ranging NDPA
With secure LTF
NOTE: AIDs of 2044 and 2045 also have unique formats
Jan 2023

## Slide 6: Recap: 320 MHz indication in EHT NDPA
For NDPA in non-HT Duplicate PPDU:
  B7 in the SERVICE field is set to 1 to indicate 320 MHz based on the following 11be spec text:
    “If the CH_BANDWIDTH_IN_NON_HT parameter in the TXVECTOR primitive is present and is equal to CBW320, then bit 7 of the SERVICE field is set to 1. The remaining 8 bits (8–15) of the SERVICE field shall be reserved for future use.”
For NDPA in EHT MU PPDU:
  The U-SIG field can indicate 320 MHz
Jan 2023

## Slide 7: Proposal #1: 320 MHz for Ranging NDPA
Use existing Ranging NDPA variant encoding in 11az and existing 320MHz indication in 11be
  No change to the Ranging NDPA MAC content
  non-HT dup PPDU: set B7 in SERVICE field to 1 to indicate 320 MHz
  EHT MU PPDU: set PHY header to indicate 320 MHz
Non-HT Duplicate PPDU
PSDU
Service
PHY preamble
Set B7 to 1 as defined in 11be
Use the existing Ranging NDPA format defined in 11az
EHT MU PPDU or
Future PPDU
PSDU
Service
PHY preamble
Use the Bandwidth field in the U-SIG field to indicate 320 MHz as defined in 11be
Use the existing Ranging NDPA format defined in 11az
Jan 2023

## Slide 8: Trigger Enhancement

## Slide 9: Recap: 11az Trigger frame variants
Jan 2023

## Slide 10: Recap: 320 MHz indication in EHT Trigger
Jan 2023

## Slide 11: Proposal #2: 320 MHz for Ranging Trigger
Add the Special User Info field defined in 11be to the Ranging Trigger frame variants defined in 11az, with B54 and B55 set to 0 to solicit 320 MHz EHT TB PPDU
  Benefit: simple
Set trigger type subfield to 8 to indicate the Ranging variant
Set B55 to 0 to indicate the presence of the following Special User Info field, which uses the format defined in 11be to indicate 320 MHz
Jan 2023

## Slide 12: Proposal #3 Clarification on PPDU Types for Ranging Trigger frame
Use-case: a BSS often has a mix of HE STA and EHT STAs
Issue: if the TF Ranging Poll frame is sent in EHT PPDU, the TXOP will be wasted if no EHT STA responds, even if some HE STAs want to participate in the ranging sequence.
Candidate solution:
  RSTA should transmit TF Ranging Poll in non-HT duplicate PPDU instead of EHT PPDU to serve both EHT/HE STAs
  Based on received CTS response, subsequent PPDUs (Ranging sounding, NDPA) may use EHT/HE/non-HT dup PPDUs

## Slide 13: Session Negotiation Enhancements

## Slide 14: Recap: Negotiation with IFTMR
From 11md and 11az:
New subelement(s) for 11be related info
Expansion is needed
Jan 2023

## Slide 15: Recap: Negotiation with IFTM
New subelement(s) for 11be related info
Expansion is needed
Jan 2023

## Slide 16: Proposal #4: Additional Info for IFTMR/IFTM
Use the reserved entries in the Format And Bandwidth subfield to indicate 320 MHz
Candidate entries for 320 MHz
  Value 6 to indicate EHT (single RF LO) for 320 MHz
    This value indicates that the STA also supports values of 5, 2, 1 and 0
    NOTE: an EHT BSS does not support 80+80 or 160+160
Add entries for 320 MHz
Jan 2023

## Slide 17: Puncturing Pattern Update
Issue: if an AP updates its puncturing pattern, how to handle a session that has already been established?
    For associated STAs: can learn the updated pattern through Beacon
    For unassociated STAs: cannot learn the change if they don’t monitor the Beacons continuously
Discussion from Nov meeting:
  Need a way to adopt the latest puncturing pattern
Proposal:
  FTM parameter modification or session termination is used to avoid using the old puncturing pattern
  Similar solution can be used for Transmit Power Envelop (TPE)
Define a new subelement for puncturing and another for TPE

## Slide 18: Summary
This contribution explored options to indicate 320 MHz BW in the following frames by an 11be STA
  Ranging NDPA
  Ranging Trigger variants
  IFTMR/IFTM for session negotiation and re-establishment
  On EHT/HE BSS Configuration with Puncturing
The analysis showed that the indications of 320 MHz defined in 11be can be applied to the above frames from 11az
  As the 11be indications are outside the fields that carries the 11az-specific info
Jan 2023

## Slide 19: Straw Poll #1
Do you agree that the 320 MHz NDP Announcement frame of 802.11bk will use existing Ranging NDP Announcement variant encoding in 802.11az and existing 320MHz indication in 802.11be?
  No change to the 802.11az Ranging NDP Announcement MAC content
  For a non-HT dup PPDU: set B7 in SERVICE field to 1 to indicate 320 MHz
  For an EHT MU PPDU: use the Bandwidth field in the U-SIG field to indicate 320 MHz
Yes: 16
No: 0
Abstain: 1

## Slide 20: Straw Poll #2
Do you agree that a 320 MHz Ranging Trigger frame in 802.11bk sets the Trigger Type subfield in the Common Info field to 8 as in 802.11az and includes the Special User Info field immediately after the Common Info field as defined in 802.11be?
Yes: 14
No: 0
Abstain: 2

## Slide 21: Straw Poll #3 (updated in r3)
Do you agree that IFTMR/IFTM frames of 802.11bk will use only a single reserved entry in the Format And Bandwidth subfield to indicate 320 MHz?
  The entry is for 320 MHz with a single RF LO;
  If the entry is included in an IFTRM or IFTM frame, it indicates that the transmitter of the frame supports 320 MHz with a single RF LO, 160 MHz with a single RF LO, 80 MHz, 40 MHz and 20 MH..
Yes:
No:
Abstain:

## Slide 22: Straw Poll #4
Do you agree that IFTMR/IFTM frames of 802.11bk will use a reserved subelement to indicate information on transmit power envelop of the BSS for 320 MHz?
Yes: 9
No: 0
Abstain: 14

## Slide 23: Straw Poll #5 (run out of time, tele call)
Do you agree that 802.11bk will extend IFTMR and IFTM frames to indicate puncturing pattern of the BSS in the Ranging Parameters field?
Yes
No
Abstain

## Slide 24: References
[1] Thoughts on 320 MHz Ranging NDP, 22/1981r0, https://mentor.ieee.org/802.11/dcn/22/11-22-1981-00-00az-thoughts-on-320-mhz-ranging-ndp.pptx, Steve Shellhammer et al.
Jan 2023

## Slide 25: Backup

## Slide 26: On 320 MHz-1 and 320 MHz-2
36.3.24.2 Channelization for 320 MHz channel
  The 320 MHz channel consists of any two adjacent 160 MHz channels in the 6 GHz band. Two type of channelizations for 320 MHz channel are defined: 320 MHz-1 and 320 MHz-2.
  320 MHz-1 is defined as 320 MHz channel with channel center frequency numbered 31, 95, and 159. 320 MHz-2 is defined as 320 MHz channel with channel center frequency numbered 63, 127, and 191.
Credit: source of the image