## Slide 1: Layered QoS and multi-layer transmission follow-up
Date: 2023-01-13
Authors:
Name | Affiliation | Address | Phone | Email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Wei Ruan |  |  |  | 
Mengyao Ma |  |  |  | 
Ying Li |  |  |  | 
Dan Wang |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2
In [3], a detailed description on cloud VR use case have been presented, which needs high requirement on Tput and latency. Moreover, two aspects regarding latency reduction have been presented:
  QoS enhancement
  Unequal error protection (multi-layer/coding transmission)
In [1], we show multi-layer transmission has the following benefits:
  Provide different protections for frames of different importance.
  Take advantage of the channel selective gains
  Good for interference environment, errors happened in one RU layer doesn’t affect the other RU.
There were some comments received regarding the simulation results we show for MC (Multiple Coding)-MIMO vs SU-MIMO. In this contribution, further simulation results are provided in response to those comments.
Recap

## Slide 3: Simulation setup
In previous simulations, we show the comparison of 4Tx, 4Rx, 4SS transmission between MC (Multiple Coding)-MIMO vs SU-MIMO where MC code can apply different MCS on different streams. Different PSDU are transmitted in different streams. The MC-MIMO shows at least 10%~15% gain over SU-MIMO.
We receive the following comments regarding the simulations:
  For baseline SU-MIMO, 3SS sometimes can achieve higher Tput than 4SS for a 4Tx, 4Rx transmission.
  With unequal power allocation (waterfilling), the baseline SU MIMO can achieve better performance.
Hence in this simulation, we compare the following four cases:
  MC-MIMO
  SU-MIMO 4SS (with equal power)
  SU-MIMO 3SS (with equal power)
  SU MIMO 4SS with unequal power*
  SU MIMO 3SS with unequal power*
  Other parameters are the same as before: 4 Tx and 4 Rx, 20MHz channel
*With unequal power allocation, the transmit power imbalance of each antenna increases. The power of some RF channels may exceeds a preset value, and the power of some channels is not fully used.

## Slide 4
Simulation results
  X-axis: channel SNR, Y-axis: Tput
MC-MIMO still shows obvious gain over baseline SU-MIMO.

## Slide 5: Summary
In this contribution, we show more simulation results to show the benefits of multi-layer transmission.

## Slide 6: Reference
[1] 11-22/1930r0, Layered QoS and multi-layer transmission
[2] 11-22/1518r0, 802.11 UHR SG Proposed PAR, Ming Gan et.al., Huawei
[3] 11-22/0952r0, Cloud VR use case and requirements, Ross Jian Yu et.al., Huawei

## Slide 7: Appendix

## Slide 8: Multi-layer transmission
In [2], it mentions multi-layer transmission is one kind of unequal error protection at PHY layer that can provide different robustness to different services.
  The base layer (I frame) is protected better with lower rate whilst the enhancement layer (P/B frame) is protected with higher rate.
  Multi-layer transmission can achieve a good tradeoff between data rate and robustness. It can further reduce transmission latency.
One way of enabling unequal error protection (UEP) is to use different MCS for different frames in different PPDUs (time domain). An alternative way is to enable multiple PSDUs with different MCS within one PPDU.
PHY
Resources
PHY
Resources
PHY
Resources
PHY
Resources
PPDU
Multi-layer transmission (QAM, coding rate, NSS, ReTx times)
Control Info
I frame
Other frame
P/B frame
In different SSs/RUs/
Constellation points

## Slide 9: Multi-layer transmission
Besides UEP for frames of different importance, multi-layer transmission can also take good advantage of the channel selective gain (e.g., divergence of eigenvalues between different spatial streams).
In 11n, UEQM (unequal modulation) MIMO enables different QAMs for different streams with the same coding rate. Here, we further assume coding rate can also be different. Below is an example.
Post SNR
SS0
SS0
Post SNR
SS1
SS1
Post SNR
SS2
SS2
Post SNR
SS3
SS3
Post SNR
Tput of SSx for MC-MIMO
Tput of SSx for SU-MIMO
MCS11
vs
MCS6
MCS10
vs
MCS6
MCS9
vs
MCS6
MCS6
vs
MCS6
Legend
Figure: MC (Multiple Coding)-MIMO vs SU-MIMO
Tput/MCS
PostSNR

## Slide 10: Multi-layer transmission
Below we show some simulation results comparing MC-MIMO and SU-MIMO.
  4 Tx and 4 Rx and a 4SS MIMO, 20MHz channel.
  X-axis: channel SNR, Y-axis: Tput
  MC-MIMO has 10%~15% gain over baseline SU-MIMO.
(a) Channel B
(b) Shielding room
(c) Home environment

## Slide 11: Multi-layer transmission
Below we also show some simulation results comparing MC-MIMO and SU-MIMO regarding different directions.
  2 Tx and 2 Rx and a 2/1 SS MIMO, 20MHz channel.
  Tput regarding different directions are compared (omni-direction antennas)