## Slide 1: Preemption for Low Latency Application
Date: 2023-03-13
Authors:

## Slide 2: Introduction
Objectives of UHR SG [1]:
  Improve reliability of WLAN connectivity
  Reduce latency
  Increase manageability
  Increase throughput including at different SNR levels
  Reduce device level power consumption
This contribution reviews one of the main challenges to reduce latency and discusses one general solution

## Slide 3: Problem statement
How to enable low latency (LL) applications in 802.11 networks that are heavily loaded with other clients’ high throughput transmissions; while at the same time minimize the performance impact to the high throughput traffic?
  In other words, how to reconcile the contradicting need:
    to allow long and efficient TXOPs for high throughput traffic
    to restrict TXOP limit for latency reduction

## Slide 4: Two main cases with large delay due to large PPDU transmission in TXOP
Case A: LL transmitter is the TXOP holder [2-3]
Case B: LL transmitter is not the TXOP holder [4]:
  DL TXOP UL LL data; UL TXOP DL LL data
  UL TXOP UL LL data

## Slide 5: General solution for case A and case B (Event-based or periodic LL traffic with jitters)
Divide the large PPDU into small PPDUs with maximum length limitation and xIFS ( ) gaps to provide preemption opportunity for the LL transmitter
Case A: TXOP holder can insert DL LL packet within the TXOP
Case B: LL transmitter can preempt the on-going transmissions in a TXOP during a xIFS time
  Further considerations: xIFS length; collisions and hidden node problem between multiple LL STAs
Case A: LL transmitter is the TXOP holder
Case B: LL transmitter is not the TXOP holder

## Slide 6: Simulation results
Traffic information:
4 DL/UL non-LL streams to/from 4 STAs
  Full buffer traffic
  Priority : AC_BE
LL stream
  160 bytes every 12ms to/from 1 LL STA
  Priority : AC_VO
Comparison:
Legacy (TXOP=6ms):
  LL transmitter has to wait until the end of an ongoing TXOP in any direction to do EDCA
Proposed solution (TXOP=6ms):
  Maximum PPDU length = 1ms
  In the DL, AP can insert the DL LL PPDU within DL TXOP
  LL transmitter can use xIFS gaps between PPDUs to preempt the next PPDU transmission
 | Aggregated TPT(Mbps) | Throughput degradation
Legacy | 1215 | 
Proposed | 1101 | -9%
The proposed solution can improve the latency performance with low throughput degradation to non-LL traffic while the LL traffic is not frequently generated
Notes: proposed case: Almost does not use EDCA to transmit data as nearly all transmissions happen as a part of preemption.

## Slide 7: Summary
It is challenging to support low latency applications in 802.11 while maintaining good performance for high throughput traffic.
  In other words, how to reconcile the contradicting need:
    to allow long and efficient TXOPs for high throughput traffic
    to restrict TXOP limit for latency reduction
We propose a preemption technique to support low latency while there is a long TXOP transmission

## Slide 8: References
[1] 11-22/0708r3, ‘Beyond be – Proposed Next Step’, Rolf de Vegt
[2] 11-22/1393r0, “uhr-latency-reduction-scheme-for-uhr”
[3] 11-22/1880r1, “Latency and Reliability enhancements for UHR”
[4] 11-23/0018r1, “uhr-low-latency-support-in-uhr”