## Slide 1: Discussion on MC-OOK
Date: 2023-01-16
Authors:

## Slide 2: Abstract
This contribution discusses the resolution of LB 270 CIDs: 3067-3068, 3070-3072, 3095-3096, 3278, 3283, 3458.
At the TGme ad hoc meeting in Piscataway NJ – Dec 5-7 resolutions were proposed for these CIDs: 11-22/2090r0 and 11-22-2083r1.
A straw poll supported continuing in the direction proposed by 1-22/2090r0.
This contributions questions that direction.

## Slide 3: Status of the MC-OOK discussion
Proposals have been made to clarify that MC-OOK is a modulation technique and that it is not a wave form or required to generate the specified WUR OOK modulation. These proposal have not been agreed.
There have been no technical arguments made to support that MC-OOK is a modulation or that it is required to generate WUR OOK transmissions.
Proposals have been made to make MC-OOK a required technique for generating the WUR OOK transmissions. These proposals seem to have significant support.

## Slide 4: A technical discussion of MC-OOK
Is MC-OOK a technique for generating the OOK wave form used in WUR?
  Yes – the OOK waveform can be generated by MC-OOK
Is MC-OOK a type of wave form?
  No – MC-OOK is a technique for generating an OOK waveform using a multi-carrier transmitter
Is MC-OOK the only technique able to generate the WUR OOK signal?
  No – the WUR OOK signal can be generated by any modulation technique that will meet the WRU OOK requirements provide in 30.3.12
Will a WUR receiver be able to receive any WUR OOK signal meeting the requirements 30.3.12
  Yes – a WUR receiver will receive any WUR OOK signal independent on how it was generated, if it meets the reequipments in 30.3.12 and is encoded with an valid WUR-Sync field and a valid WUR-Data field – (Contrary to the current spec which seems to require MC-OOK modulation technique, the technique is not technically required to encode the WUR OOK signal.)
Therefore MC-OOK is a modulation technique – it is not a waveform or required.

## Slide 5: What is the “problem” with making MC-OOK a requirement
IEEE Standards strictly require adherence to Antitrust, Competition and Commercial Terms Policies:
“There are less obvious kinds of anticompetitive conduct. Technical standards necessarily include technical content, but that content must be technically justified. Technical requirements should never be included for the purpose of unreasonably impeding a company’s ability to compete, or unreasonably creating an advantage for one or a group of companies. This does not mean that the technical requirement has to be written so that all competitors can implement the standard without satisfying what would be a more rigorous standard’s requirement. But it does mean that you should guard against technical content being inserted for anticompetitive purposes.“ [1]

## Slide 6: References
[1] – IEEE SA: “Antitrust and Competition Policy What You Need to Know”, pamphlet