## Slide 1: Some Thoughts on Backscatter Modulation
Date: 2023-01-16
Authors:

## Slide 2: Abstract
This document briefly introduces the principle of backscatter modulation. Additionally, it shows potential issues wrt. frequency regulation.

## Slide 3: Possible Backscatter System Configuration
Bi-Static Configuration:  Full duplex with other device
RX signal of device is ~60dB below RX signal of carrier
Mono-Static Configuration: Identical antenna for TX and RX  Full duplex with same device
 RX signal is 100dB below TX signal

## Slide 4: Modulation of the Backscatter Device
Backscatter is done by switching the load of an antenna between two states, e.g. open circuit and shortcut
As the “load” switches between open and shortcut all signals are reflected, but with different phase
Ideally, the transmit power of the device is identical to the received power
The modulation is normally a rectangular carrier with modulated on-off-keying or BPSK for the payload data modulation (e.g. Miller in UHF RFID)
The output signal is: , where s(t) is the AP signal
s
y

## Slide 5: Some Backscatter Theory ( I / II )
We can describe the square wave by means of a Taylor series (we exclude the DC component) [1]:
The corresponding frequency spectrum results in:
f
|X(f)|
f0
-f0
-3f0
-5f0
3f0
5f0
…
…

## Slide 6: Some Backscatter Theory ( II / II )
f
|Y(f)| Backscattered Signal
f0+fs
-f0+fs
-3f0+fs
-5f0+fs
3f0+fs
5f0+fs
f
|S(f)| AP TX Signal
fs
…
…
The multiplication in the time domain leads to a convolution in the frequency domain [2].

## Slide 7: What does the AP Receive?
A higher f0 simplifies the decoding, but increases the out of band emissions  problems with frequency regulation
The bandwidth of classical UHF-RFID readers is typically very low (CW)
f
f0+fs
-3f0+fs
-5f0+fs
3f0+fs
5f0+fs
…
…
-f0+fs
fs
AP TX Signal
e.g. 100dB for monostatic, 60dB for bistatic

## Slide 8: Summary
Backscatter modulation typically uses a rectangular modulation
The rectangular modulation with frequency f0 shifts the backscatter-signal out of the original AP TX signal  simplifies decoding
Backscatter modulation typically at least doubles the spectrum, additional harmonics are typically present
 Issues with the frequency regulation (e.g. in Europe)

## Slide 9: References
[1] https://en.wikipedia.org/wiki/Fourier_series
[2] John G. Proakis, and Masoud Salehi. Digital communications. McGraw-Hill., 2008.