## Slide 1: TG bh Way Ahead Decisions
Date: 2022-12
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2
Based on presentation 22/2150r2 options and decisions were provided
This presentation simply lists those options and proposes Straw Polls and Motions

## Slide 3: Straw Polls/Motions
Clarify “11aq” text to be clear that every ESS STA uses same MAC Address?
  If non-AP STA wants to be identified, it uses same address at the same ESS every time.
  STA maintains list of ESS/SSIDs and MAC Addresses.
  Needs an “opt-in” mechanism
ADs
  Simple, easy to implement
  Meets every Use Case
  No computations
DIS
  As same address every time, trivial to copy.

## Slide 4: Straw Polls/Motions
Adopt MAAD MAC scheme
  STA uses the MAC Address that was provided by the AP at previous association – new address every association
  STA maintains list of ESS/SSIDs and latest MAC Addresses.
  Needs an “opt-in” mechanism
ADs
  Simple, easy to implement
  Provides good protection against copying
  Meets every Use Case
  No computations

## Slide 5: Straw Polls/Motions
Adopt a more complex scheme, ID Encoding, RRCM, IRMA
  Random MAC with encrypted identifier in an IE
  Keys exchanged
  Range of computational complexity
  STA maintains list of ESS/SSIDs and latest ID/keys
  Needs an “opt-in” mechanism
ADs
  Provides highest level protection
  Meet every Use Case
DIS
  Requires computations

## Slide 6: Straw Polls/Motion
TGbh draft shall include text related to:
Clarified “11aq” text (slide 25)
MAAD MAC (slide 26)
More complex scheme (slide 27)
Take each in turn.
THEN
Motion option with highest YES vote (assuming majority).
(Hopefully members would support a majority view)