## Slide 1: EN 301 893 EDT Update
Date: 2023-01-17
Authors:
Name | Affiliations | Address | Phone | email
David Boldy | Broadcom |  |  | david.boldy@broadcom.com

## Slide 2: Abstract
Updates from ETSI BRAN Meeting#117 (related to EDT in the EN 301 893 standard).

## Slide 3
Background
At BRAN#117 EN 301 893 stable draft v2.1.50 was sent for EC assessment. This version included the accepted text for a new PSD scaled proposal for EDT from BRAN(22)116e003r3. TC BRAN agreed that further work needs to be done prior to submission to ENAP to address the “Maximum PSD levels for transmissions within a larger configured BW” issues highlighted in the Broadcom contribution BRAN(22)117009 response document and captured for further work in clause 4.2.7.3.2.5 by the square bracketed text:
[For concurrent operation on more than 4 channels, 3 dB shall be added to PSDmax.].

## Slide 4: PSD scaled proposal from BRAN(22)116e003r3
The following was included in draft v2.1.50 sent of EC assessment:
4.2.7.3.2.5 Energy Detection Threshold (EDT) (LBE)
…
The EDT shall be −85 dBm/MHz + (PSDlimit – PSDmax) with a minimum of −85 dBm/MHz and a maximum of −75 dBm/MHz, where PSDmax is the maximum PSD when using all channels in the configured combination/grouping of channels and PSDlimit is the PSD limit in the sub-band of operation. [For simultaneous operation in more than 4 channels, 3 dB shall be added to PSDmax.]
…
The [square bracketed text] needs addressing by ETSI BRAN prior to sending into Public Enquiry/ENAP (EN Approval Process)

## Slide 5: Broadcom concern raised in contribution BRAN(22)117009
The proposed language in BRAN(22)116e003 allows partial use of a full configured bandwidth without limiting the PSD to this configured BW. This allows devices to use a higher EDT to gain access to the channel but then have actual transmissions at lower bandwidths with much higher PSDs.
For example: the proposal allows a 160MHz AP (or LAA/NRU) to sense the channel at ED at ­-63dBm at 23dBm max transmit power considering the lower PSD over 160MHz, but then transmit on 20MHz with an 8 times higher PSD.

## Slide 6: Proposed solution
If the actual transmission bandwidth of the device is lower than the configured BW it should either:
be limited to the same PSDmax as that of the higher configured BW ( i.e. similar to WiFi spatial reuse based on OBSS PD) or
the EDT level should be reduced in accordance with the equation −85 + (PSDlimit – PSDmax) dBm/MHz where PSDmax is the PSD for the actual transmission BW.
The following additional text for clause 4.2.7.3.2.5 was proposed to address the above:
For multi-channel operation, where transmissions can occur only in a part (i.e. "n" used channels in a group of adjacent channels) of the total bandwidth (N), the maximum EDT that applies prior to transmission shall be based upon the maximum PSD (PSDmax) that applies for the total bandwidth (N). At this maximum EDT, the PSD of such (n x 20 MHz) partial bandwidth transmissions shall not be greater than the PSDmax corresponding to the total bandwidth (N). Lower EDT may be used to increase the PSD on partial data transmissions according to the equation above.

## Slide 7: Theoretical vs pragmatic (1)
Although it was not contested that from a theoretical perspective the approach on slide 6 addresses the concern highlighted some were looking for a more pragmatic approach.
Offline discussions to try and find a pragmatic compromise to the PSD scaled proposal led to the addition of the square bracketed text in the draft standard:
[For simultaneous operation in more than 4 channels, 3 dB shall be added to PSDmax.]
NOTE: Broadcom made it clear during the BRAN#117 meeting that they did not agree with the proposed text in square brackets but agreed to including this bracketed text on the understanding that TC BRAN continue to work on new text to address Broadcom concerns prior to finalization of the standard.

## Slide 8: Theoretical vs pragmatic (2)
The bracketed text does not fully address the problem highlighted and further language is required to close out potential misuse of the specification and unfair sharing of the spectrum.
After further investigation since BRAN#117 it is not seen that there would be significant burden to regulatory testing when comparing a slide 6 based approach and other pragmatic approaches proposed. Any non-mandatory testing would not be significant and would be proportional to the complexity of the driver (e.g. Dynamic EDT) and any channel access benefits that a manufacturer is trying to achieve fairly.

## Slide 9: Next steps
Highlighted issue needs to be resolved prior to sending into ENAP.
Next scheduled meeting BRAN#118 (27th Feb – 3rd March)
Note: Broadcom are working on an updated proposal with a simplified test to socialize prior to BRAN#118 but open to other new pragmatic solutions that prevent misuse and enable fair sharing.

## Slide 10: Related information
Extract from BRAN#118 meeting minutes - BRAN(22)117002
The following guidance is agreed in BRAN(22)116e003r3 and is listed below:
  With respect to IEEE 802.11ax equipment only, ETSI TC BRAN agrees that such equipment could be treated under the existing rules for option 1 EDT defined in EN 301 893 v2.1.1 clause 4.2.7.3.2.5 until the date of withdrawal of that standard.
  ETSI TC BRAN will contact the EC before ENAP to discuss the acceptance of an extension to the default date of withdrawal to at least 36 months after listing of the new version of the standard in the Official Journal.
Typical transition period to of standard to new EDT requirements (at least 18 months after citation in OJEU) ~mid 2025. Above increases transition to early 2027.