## Slide 1: Packet Extension
Date: 2023-01-18
Authors:
Name | Affiliations | email
Steve Shellhammer | Qualcomm | shellhammer@ieee.org
Ali Raissinia |  | alirezar@qti.qualcomm.com
Yanjun Sun |  | yanjuns@qti.qualcomm.com
Bin Tian |  | btian@qti.qualcomm.com

## Slide 2: Background
The packet extension (PE) in the EHT NDP depends on the number of spatial streams
From 802.11be D2.0, subclause 36.3.18 (EHT sounding NDP) it states:
The EHT sounding NDP has a PE field that is given as follows:
— 4 µs when the PPDU bandwidth is less than or equal to 160 MHz and the number of spatial streams is less than or equal to 8.
— 8 µs for all the other cases.

## Slide 3: Proposal
Since the EHT Ranging NDP and the EHT TB Ranging NDP both have a bandwidth greater than 160 MHz, we propose to use an 8 µs PE duration for both the EHT Ranging NDP and the EHT TB Ranging NDP

## Slide 4: Straw Poll
Do you agree that in 802.11bk an 8 µs PE duration will be used in both the EHT Ranging NDP and the EHT TB Ranging NDP?
Yes
No
Abstain