## Slide 1: Considering Unscheduled AP Power Save
Date: 2023-02-13
Authors:
Name | Affiliations | Address | Phone | email
Guogang Huang | Huawei |  |  | huangguogang1@huawei.com
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Yousi Lin |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Introduction
The AP MLD power saving has been discussed in UHR SG due to the following factors [1]
  Power consumption increases with the number of links/APs
  Operators are committed to be net 0 carbon by 2040
  Customers are concerned about their devices power consumption (both on health and economical point of view)
We believe the AP MLD power save can be well supported by exploiting the multi-link operation (MLO).
In this presentation, we further present an unscheduled AP power save solution.

## Slide 3: Recap：AP Power Management
Scheduled AP power save
  Link Disablement defined in 11be
  TWT
    When the AP set the Responder PM Mode subfield to 1, then the AP might not be available outside TWT SPs.
  Cons. These scheduled power save mechanisms cannot well address the non-AP MLD’s traffic requirement especially for non-periodic traffic.
Similar to the current power save of both the STA and S1G AP, the author in [2] defines the AP power management mode as
  Active mode
  Power Save mode
    Doze state
    Awake state

## Slide 4: Unscheduled AP MLD Power Save
In order to save AP MLD power, the simplest way is to have only one link operating in the active mode and other links operating in the PS mode if the traffic load is low.
  All APs affiliated with the AP MLD shall announce the change on the AP power management mode in advance
  No need to send Beacon frame if an AP affiliated with an UHR AP MLD is in PS mode
The ‘active’ link can address the follow potential issues [2]
  Provide access service to the pre-EHT STA
  Provide Discovery, Active Probing, Association to EHT/UHR non-AP MLD

## Slide 5: Unscheduled AP MLD Power save (Cont.)
Once high throughput is needed, a non-AP MLD can send a request through the ‘active’ link to wake up one or more affiliated APs in the PS mode with the doze state
An affiliated AP in PS mode with the doze state shall enter the awake state after receiving a wakeup request for frame exchange
The affiliated AP in PS mode with the awake state can switch back to the doze state if either of the following conditions is met
  There is no STA who operates on this link and sets the More Data subfield of the latest frame transmitted to 1
  The channel is idle for a given time

## Slide 6: Conclusions
We have discussed an unscheduled AP MLD power save scheme
  Which can make a good trade-off between non-AP MLDs’ traffic requirement and AP MLD’s power consumption

## Slide 7: References
[1] Alfred Asterjadhi, et al. Considerations for enabling AP power save, DCN 11-23/10r0
[2] Liwen Chu, et al. AP MLD Power Management, DCN 11-22/0015r0