## Slide 1: Reducing Latency & Link Adaptation Convergence Time
Date: 2023-02-20
Authors:

## Slide 2: Introduction
Improved latency, reliability and more efficient use of the spectrum are important goals of UHR [1]
Link Adaptation (LA) is directly related to these aspects
  Transmission parameters are adapted to (possibly changing) channel conditions, which improves the reliability
  Reacting to changing conditions, in particular reducing MCS, limits impact on latency
  Transmitting at highest possible rate (while maintaining some desired error or retransmission rate) improves spectrum efficiency
Improvements to link adaptation have already been proposed for UHR and EHT, including:
  Issues in the field related to link/rate adaptation [2]
  Introduction of additional, finer MCS values [3]
  Fast link adaptation [4]
In this contribution we recall existing issues & limitations in practical link adaptation mechanisms, and propose that the group consider addressing them in UHR

## Slide 3: Link Adaptation Overview
Link adaptation is a mechanism which adapts the transmission parameters (e.g. MCS, N_SS, allocated RU) to the link conditions
There are various approaches and solutions/implementations
The standard defines ‘tools’ which can be used (in an implementation-dependent manner) to determine how to adapt the transmission parameters
  Example #1: an ACK (or B-ACK) indicates to the transmitter if the (individual data or management) frame was successfully decoded by the receiver
  Example #2: the sounding mechanism can be used to solicit feedback with respect to the SNR per RU
Link adaptation is important for both downlink and uplink, since physical channels (including TX/RX chains) and transmission schemes (e.g. usage of BF) are not necessarily symmetric
  In the uplink, TCP Acknowledgements (which constitute data MPDUs in MAC) are in many cases the bottleneck, since an unsuccessfully received TCP ACK leads to an immediate reduction in goodput
    Transmission at lowest (and hence most robust) MCS is not a good solution, in most cases

## Slide 4: Issues and Challenges
Some of the computations and measurements defined in the standard over the years, which are performed and fed back by the intended receivers, are not completely ‘trusted’ by the transmitters
  For example: ELA, HLA, MCS feedback (MFB), SNR, etc.
The transmitter is accountable for the successful transfer of data to the receiver; however, the computations & measurements are performed at the receiver, and do not necessarily provide reliable indication of the expected performance
On the other hand, ACK-based mechanisms (e.g. Minstrel, AARF, etc.) that don’t rely on the receiver lead to a very long convergence time (can reach 100s of msec)
  This means that such mechanisms do not adapt fast to changes and do not use the spectrum resources very efficiently

## Slide 5: Need for new LA Enablers in UHR
Based on the previous slides, we propose that new LA ‘tools’ should be developed in UHR; these tools would allow adaptation of the transmission parameters based on the expected performance
The group should work on finding link performance metrics and their reporting mechanisms that would address the issues and challenges
Important goals are clearly shortening convergence time – orders of magnitude shorter than existing ACK-based link adaptation mechanisms, as well as reducing latency (particularly when channel conditions are getting worse)

## Slide 6: Conclusions
Link adaptation is an important mechanism in both DL and UL
  The physical channels and transmission schemes are not necessarily symmetric
The transmitter is the one entity that is accountable for the successful transfer of data to the receiver
  The current computations & measurements (SNR, ELA, HLA, etc.) are performed at the receiver, and do not necessarily provide reliable indication of the expected performance
  On the other hand, ACK-based mechanisms (e.g. Minstrel, AARF, etc.) that do reflect the performance, lead to a very long convergence time
We propose that the group work on developing new metrics & mechanisms for LA in UHR
  Reported metrics that are based on the expected performance, and would allow the transmitter to adapt transmission parameters
  Goals should be latency reduction and short convergence time – significantly (orders of magnitude) shorter than existing mechanisms

## Slide 7: References
[1] 11-23/0028r6: PAR Discussion (Laurent Cariou)
[2] 11-23/0011r0: Considerations on the Enhanced Link Adaptation (Xiaogang Chen et al)
[3] 11-20/0083r0: Impacts of MCS set expansion on 11be link adaptation (Yan Zhang et al)
[4] 11-20/1005r1: Yet Another Fast Link Adaptation Attempt (Jinjing Jiang)
Notes: at least one mode of operation capable of improved support, compared to 802.11be, for applications with stringentworst-case latency and jitter requirementscompared to 802.11be // i.e., avoid “worst-case”