## Slide 1: Study on AI CSI Compression
Date: 2023-07
Authors:

## Slide 2: Abstract
In r1 [5], we introduced a new vector quantized variational autoencoder (VQVAE) method for CSI compression and discussed its performance.
In r2 [6], we have a follow-up discussion on
  Further feedback overhead reduction and goodput improvement,
  Model generalization under different channel conditions and different numbers of antennas/spatial streams，
  Workflow of AI CSI compression using VQVAE.
In this revision (r3), we continue the study on
  Model generalization under different bandwidths,
  Lightweight encoder that reduces computation complexity and model deployment overhead.

## Slide 3: R1 - Background
The AP initiates the sounding sequence by transmitting the NDPA frame followed by a NDP which is used for the generation of V matrix at the STA.
The STA applies Givens rotation on the V matrix and feeds back the angels in the beamforming report frame.
Ntx=Nrx=Nss | BW=20MHz | BW=40MHz | BW=80MHz | BW=160MHz | BW=320MHz
2 | 0.12 (KBytes) | 0.24 | 0.50 | 1.00 | 1.99
4 | 0.73 | 1.45 | 2.99 | 5.98 | 11.95
8 | 3.39 | 6.78 | 13.94 | 27.89 | 55.78
16 | 14.52 | 29.04 | 59.76 | 119.52 | 239.04
The total feedback overhead is . Larger bandwidth and number of antennas lead to significantly increased sounding feedback overhead, which increases the latency and limits the throughput gain.
Visualization of the precoding matrix after FFT shows its sparsity and compressibility.
20MHz, 8*2

## Slide 4: R1 - Existing Work on AI CSI Compression
ML solutions: no neural network
  [1][2] adopted a traditional machine learning algorithm, i.e., K-means, to cluster the angle vector after Givens rotation
  Beamformer and beamformee need to exchange and store the centroids
  Only transmit the centroid index during inference
  2dB PER loss, up to 50% goodput improvement
AI solutions: use neural network
  [3] adopted two autoencoders to compress two types of angles after Givens rotation separately
  Beamformer and beamformee need to exchange the store neural network models
  Only transmit the encoder output during inference
  Up to 70% overhead reduction and 60% throughput gain for 11ac system

## Slide 5: R1 - Our Study on AI CSI Compression
Vector quantization variational autoencoder (VQVAE) [4] is proposed for CSI compression
  Consists of encoder, codebook, decoder
  Learn how to compress and quantize automatically from the data
Convolutional neural network (CNN) or transformer could be used for both the encoder and decoder.
Input of NN could be the V matrix or the angles after Givens rotation.
Beamformer and beamformee need to exchange and store the codebook and half of the NN model.
Only transmit the codeword index during inference.

## Slide 6: R1 - Performance Evaluation
Simulation setup:
  Training data are generated under SU MIMO, channel D NLOS, BW=80MHz, Ntx=8, Nrx=2, Nss=2, Ng=4
  TNDPA=28us, TNDP=112us, TSIFS=16us, Tpreamble=64us, MCS=1 for BF report, MCS=7 for data, payload length=1000Bytes
  Comparison Baseline:
    current methods in the standard, Ng=4 (250 subcarriers) and Ng=16 (64 subcarriers) with and
Performance Metric:
  Goodput: GP =
  Compression ratio: Rc =
  SNR-PER curve
NDPA
NDP
BF
Data
ACK
SIFS
SIFS
SIFS
SIFS

## Slide 7: R1 - Performance Evaluation
, MCS=7
Method | overhead Ng=4 (bits) | overhead Ng=16 (bits) | overhead VQVAE (bits) | Rc vs Ng=4 | Rc vs Ng=16 | Loss @ 0.01 PER (dB) vs Ng=4 | loss @ 0.01 PER (dB) vs Ng=16 | GP Ng=4 (Mbps) | GP Ng=16 (Mbps) | GP AI (Mbps) | GP gain (%) vs Ng=4 | GP gain (%) vs Ng=16
VQVAE-1 | 32500 | 8320 | 2560 | 12.70 | 3.25 | 0.16 | 0 | 5.07 | 10.77 | 14.70 | 189.64 | 36.48
VQVAE-2 | 32500 | 8320 | 1280 | 25.39 | 6.50 | 0.5 | 0.4 | 5.07 | 10.77 | 16.00 | 215.20 | 48.53
Rc=25 (CB size 1024)
Rc=12 (CB size 1024)
Notes: Train the VQVAE model based on generated V matrices
Apply the trained model to do precoding
Run PER curve under

## Slide 8: Further Study in R2
Reduce the feedback overhead and improve the goodput
  Different neural network architecture
  Reduce codebook size and dimension
More complex scenarios
  More simulations under different configurations
  MU-MIMO scenarios
Increase model generalization
  One neural network can exhibit robustness to different channel models
  One neural network can exhibit robustness to different bandwidth
  One neural network can exhibit robustness to number of antennas

## Slide 9: R2 - Feedback overhead reduction and goodput improvement
Simulation setup:
  SU MIMO, channel D NLOS, BW=80MHz, Ntx=8, Nrx=Nss=2
  Higher compression ratio and more MCS are considered
Comparison baseline：
  Standard: Givens, Ng=4/16, =6, =4
VQVAEs with different compression ratios achieve less than 1dB PER loss compared with standard method.
Rc=25 (CB size 1024)
Rc=36 (CB size 128)
Rc=12 (CB size 1024)

## Slide 10: R2 - Goodput improvement and feedback overhead reduction
Performance Metric:
  Goodput: GP =
  Compression ratio: Rc =
  Parameters for goodput calculation: TNDPA=28us, TNDP=112us, TSIFS=16us, Tpreamble=64us, MCS=1 for BF report, MCS=7 for data, L=1000Bytes, PER=0.01
Method | VQ size | overhead Ng=4 (bits) | overhead Ng=16 (bits) | overhead VQVAE (bits) | Rc vs Ng=4 | Rc vs Ng=16 | Loss @ 0.01 PER (dB) vs Ng=4 | loss @ 0.01 PER (dB) vs Ng=16 | GP Ng=4 (Mbps) | GP Ng=16 (Mbps) | GP AI (Mbps) | GP gain (%) vs Ng=4 | GP gain (%) vs Ng=16
VQVAE-1 | 1024 | 32500 | 8320 | 2560 | 12.70 | 3.25 | 0.16 | 0 | 5.07 | 10.77 | 14.70 | 189.64 | 36.48
VQVAE-2 | 1024 | 32500 | 8320 | 1280 | 25.39 | 6.50 | 0.5 | 0.4 | 5.07 | 10.77 | 16.00 | 215.20 | 48.53
VQVAE-3 | 128 | 32500 | 8320 | 896 | 36.27 | 9.29 | 0.9 | 0.8 | 5.07 | 10.77 | 16.43 | 223.77 | 52.57
NDPA
NDP
BF
Data
ACK
SIFS
SIFS
SIFS
SIFS

## Slide 11: R2 - Generalization of different channel models
Simulation setup:
  Training data are a combination of V matrices generated under channel model B, C, and D
  The trained model is tested by data of channel B, C, and D, respectively
Comparison baseline：
  VQVAE-chX: NN model is trained and tested using data of channel X
  Standard-chX: Ng=4, =6, =4
Compared with standard method, the generalized NN model has no PER loss for channel B and C, and 0.5dB PER loss for channel D.
A well-trained neural network model is robust to different channel conditions.
Legend | Train data | Test data
VQVAE-generalized-chB | B, C, D | B
VQVAE-chB | B | B
VQVAE-generalized-chC | B, C, D | C
VQVAE-chC | C | C

## Slide 12: R2 - Generalization of different Nrx/Nss
Simulation setup:
  Training data are a combination of V matrices of different Nrx (i.e., Nrx=2 and 4)
  The trained model is tested by data of Nrx=2 and Nrx=4, respectively
Comparison baseline：
  VQVAE: NN model is trained and tested using data of certain Nrx
  Standard: Ng=4, ,
Compared with standard method, the generalized NN model has 0.2/0.8dB PER loss for Nrx=2/4.
A well-trained neural network model is robust to different number of receive antennas.
Legend | Train data | Test data
VQVAE-generalized-8x4 | 8x2 + 8x4 | 8x4
VQVAE-8x4 | 8x4 | 8x4
VQVAE-generalized-8x2 | 8x2 + 8x4 | 8x2
VQVAE-8x2 | 8x2 | 8x2

## Slide 13: R2 - Workflow of AI CSI compression using autoencoder
AP
STA
NDP
V or
encoder and codebook
Train the encoder, codebook and decoder
NN model training and sharing
Infrequently: hours, days or even months
Original V can be feedbacked to facilitate training if possible
Standardize the encoder architecture; alternatively, negotiate encoder architecture using existing format such as NNEF[6] and ONNX[7]
NDP
Channel estimation, SVD
Encoder,
codebook
V
Index
Decoder,
codebook
beamforming
Data
AP
STA
Training and model sharing
Channel estimation, SVD, Givens rotation

## Slide 14: Further Study in R3
For AIML based CSI compression, if one AIML model, e.g., a set of parameters, is required for one specific scenario, e.g., bandwidth, channel condition or spatial stream, it will bring challenges for the practical implementation.
AIML model generalization is one of the key factors need to be considered. In R2, we have studied the model generalization of different channel conditions and different number of spatial streams. In this version, we continue to study the model generalization of different bandwidths.
As discussed in [8][9], complexity reduction is discussed as another objective for CSI compression use case. In this contribution, we also introduce our study on lightweight encoders, which significantly reduces the computation complexity and model deployment overhead while maintaining the goodput performance.

## Slide 15: Generalization of different bandwidth
Simulation setup:
  The training data contain only V matrices of BW=160MHz
  After training, the model is tested by data of BW=20MHz, 40MHz, 80MHz, 160MHz, respectively
Comparison baseline：
  VQVAE: the NN model is trained and tested using data of certain BW
  Standard: Ng=4, ,
Compared with standard method, the generalized model achieves similar performance (less than 1dB loss and 12 times overhead reduction).
A single neural network model can effectively handle the inputs of different bandwidths.
Legend | Train data | Test data
generalized-20 | 160 MHz | 20 MHz
VQVAE-20 | 20 MHz | 20 MHz
generalized-40 | 160 MHz | 40 MHz
VQVAE-40 | 40 MHz | 40 MHz

## Slide 16: Computation complexity and model deployment overhead reduction
AP
STA
NDP
V or
encoder and codebook
Train the encoder, codebook and decoder
NDP
Channel estimation, SVD
Encoder,
codebook
V
Index
Decoder,
codebook
beamforming
Data
AP
STA
Training and model sharing
Channel estimation, SVD, Givens rotation
Efficient ways to reduce the overhead and computation complexity:
Lightweight encoder
Direct quantization without codebook

## Slide 17: Computation complexity and model deployment overhead reduction
Previous VQVAEs adopt symmetric encoder and decoder architecture and vector quantization (codebook-based).
A transformer-based decoder is used to enable lightweight encoder.
Codebook-based quantization is replaced by uniform quantization to reduce transmission overhead.
The number of encoder parameters (weight and bias) as well as the computation complexity are reduced by more than 1000 times.
ENC
DEC
codebook
codebook
DEC
LW-ENC
quantize
dequantize

## Slide 18: Computation complexity and model deployment overhead reduction
Two CNN-based lightweight encoders (LW-ENC) are studied
Reduce computation complexity and model and codebook sharing overhead significantly
Achieve same compression ratio and goodput performance compared to previous model
Method | Feedback overhead (bits) | Goodput (Mbps) | Codebook size | Codebook dimension | # params of codebook | # params of encoder | Computation complexity of encoder (MACs)
VQVAE-2 | 1280 | 16.00 | 1024 | 32 | 32768 | 5.0M | 2.2G
LW-ENC-1 |  |  | 0 | 0 | 0 | 3.9K | 0.7M
LW-ENC-2 |  |  | 0 | 0 | 0 | 2.9K | 1.6M
The overhead and goodput of standard method (Givens rotation, Ng=4, , ) are 32500bits and 5.07Mbps.
MACs: Multiply–accumulate operations

## Slide 19: Computation complexity and model deployment overhead reduction
We discuss possible ways of encoder sharing the corresponding overhead.
If the encoder architecture is standardized, only need to share the parameters. For LW-ENC-1, the overhead is 7.8KBytes if 16-bit quantization is used. Simulation shows that there is no performance loss using 16-bit encoder for CSI feedback.
Alternatively, need to negotiate encoder architecture using existing format such as NNEF[6] and ONNX[7]. For LW-ENC-1, the overhead is 22KBytes if ONNX is used.
Other model deployment/quantization method can be further studied.
AP
STA
NDP
V or
encoder
Train the encoder, codebook and decoder
Channel estimation, SVD, Givens rotation

## Slide 20: Summary
In this contribution, we showed performance enhancement for autoencoder-based CSI compression scheme proposed in [5], including
  Model generalization under different bandwidths,
  Lightweight encoder that reduces computation complexity and model deployment overhead by more than 1000 times, and maintains the goodput performance
Further Study
  More complex scenarios, e.g., MU-MIMO
  Other quantization methods for more efficient model sharing

## Slide 21: References
[1] M. Deshmukh, Z. Lin, H. Lou, M. Kamel, R. Yang, I. Güvenç, “Intelligent Feedback Overhead Reduction (iFOR) in Wi-Fi 7 and Beyond,” in Proceedings of 2022 VTC-Spring
[2] 11-22-1563-02-aiml-ai-ml-use-case
[3] P. K. Sangdeh, H. Pirayesh, A. Mobiny, H. Zeng, “LB-SciFi: Online Learning-Based Channel Feedback for MU-MIMO in Wireless LANs, ” in Proceedings of 2020 IEEE 28th ICNP
[4] A. Oord, O. Vinyals, “Neural discrete representation learning,” Advances in neural information processing systems, 2017.
[5] 11-23-0290-01-aiml-study-on-ai-csi-compression
[6] The Khronos NNEF Working Group, “Neural Network Exchange Format”, https://www.khronos.org/registry/NNEF/specs/1.0/nnef-1.0.5.html
[7] Open Neural Network Exchange (ONNX), https://onnx.ai
[8] 11-23-0755-00-aiml-aiml-assisted-complexity-reduction-for-beamforming-csi-feedback-using-autoencoder
[9] 11-23-0906-02-aiml-proposed-ieee-802-11-aiml-tig-technical-report-text-for-the-csi-compression-use-case