## Slide 1: 320 MHz EDCA ranging PPDU support
Date: March 11, 2023
Authors:

## Slide 2: 320 MHz EDCA Ranging PPDU Support (1)
FTM legacy ranging, a.k.a. EDCA ranging in 802.11az, is currently the most implemented and deployed Wi-Fi time-of-flight ranging method.
The non-TB and TB 802.11az style ranging protocols are only beginning to be implemented with no market presence to date.
In the long run we would like to transition to the non-TB and TB 802.11az ranging protocols but for the time being many devices will only be supporting EDCA ranging.
Thus, just as for non-TB and TB ranging, support for EDCA ranging at wider bandwidths is important to achieve sub meter range measurements reliably.

## Slide 3: 320 MHz EDCA Ranging PPDU Support (2)
Non-TB and TB ranging requires many more HW and FW changes than ECDA ranging and therefore takes longer time to realize in the market.
As such, it makes sense to enable the same wider bandwidths in EDCA ranging that we aim to realize in 11bk.
We therefore propose to enable the EHT 320 MHz PPDUs for EDCA ranging as part of 11bk.

## Slide 4: Enabling 320 MHz EHT PPDU support
The changes needed in the standard to enable EHT PPDUs for EDCA ranging are small.
Mainly we need to add one or more rows to Table 9-320 (Format and Bandwidth subfield).
This would include one or more rows for the 320 MHz EHT PPDU(s).
  Any extra rows are those that might be needed to support split bandwidths and/or multiple LO options.

## Slide 5: Straw Poll
Do you support adding support for 320 MHz ranging using the EHT PPDUs to EDCA ranging?
Y/N/A:

## Slide 6
Thank You!