## Slide 1: ML Model Sharing between STAs
Date: 2023-03-11
Authors:

## Slide 2: Abstract
In this contribution, we discuss the technical feasibility of AIML model sharing between STAs.

## Slide 3: Introduction
One task of AIML TIG is to investigate the technical feasibility of features enabling support of AI/ML [1].
In order to enable support of AI/ML, we need to define signaling of AI/ML related information exchange between STAs [2-6], including
  capability indication, data report to facilitate AI/ML model training, AI/ML model and model parameters distribution/sharing, management information, additional granularity of Ng value
AI/ML model sharing seems the most significant standard impact and its technical feasibility needs to be well discussed.
In this contribution, we discuss how to distribute/share the AI/ML model or AI/ML model parameters between STAs.

## Slide 4: Components of ML model
We can regard a ML model as a black box, which consists of
  Algorithm: the algorithm, such as linear regression, deep learning, that the ML model uses to calculate the output by given the input. It can be an executable code.
  Model parameter: the parameters that are used to configure the algorithm, which are updated by model training
  Training data: the data is used to train the model and decides the ML model parameters
  Input and output: the input and output of the ML model algorithm, which are decided by the purpose (use case) of ML model
ML algorithm
(model parameter)
Training Data
Input
Output

## Slide 5: Use case of ML model sharing
Autoencoder
  Autoencoder is popular ML model for CSI compression  input and output are known
  Assume that the encoder and decoder are trained offline.
  Encoder and decoder are a pair of ML algorithms that are deployed at STA1 and STA2.
The ML model algorithms and model parameters between STAs have to be shared.
Decoder
STA1
Encoder
Encoded CSI feedback bits
STA2
Recovered CSI feedback
Original CSI feedback

## Slide 6: Challenges of sharing ML algorithm
It is difficult to pre-install the same AIML algorithm on the two devices
  It is difficult to have one or several universal ML models used by all devices even for a same use case.
    Each company has its own team to develop ML model and may prefer to keep the model secret.
    Machine learning is a popular topic and the improvement of ML model happens frequently.
Then, it requires one device to share its ML algorithm with other device to enable the ML functionality.
  Proposal 1: transmit the ML algorithm over the air
  Proposal 2: download the algorithm from verified server
We are going to discuss the above two proposals.

## Slide 7: Proposal 1: transmit ML algorithm over-the-air
Advantage:
  ML model algorithm can be shared within IEEE 802.11 network.
Difficulties: how to execute ML algorithm received from the frame?
    Compatibility issue: the ML algorithm may not be able to execute at firmware
    Security issue: the ML algorithm may include backdoors which causes security issue
  A uniform and independent processing unit is needed to ensure that the ML algorithm can be executed and the execution does not interfere the communication process.
Frame (ML model algorithm)
STA1
STA2
Install ML algorithm from frame
Frame (Input of ML model)
Run ML algorithm
Frame (Output of ML model)
Uniform & Indep. processing unit for ML only
input
output

## Slide 8: Proposal 2: download the algorithm from verified server
Advantage:
  Cloud server can stores a large amount of ML algorithms and updates the ML algorithms frequently.
  Cloud server can verify the ML algorithms to ensure the security of those ML algorithms.
Difficulties:
  Interaction with a cloud server for ML algorithms may be out of scope of IEEE 802.11
  Cloud server requires additional cost and it is not clear who should be responsible to maintain the cloud server.
Frame (ML model ID)
STA1
STA2
Install ML algorithm from server
Frame (Input of ML model)
Run ML algorithm
Frame (Output of ML model)
Cloud Server

## Slide 9: Summary
ML model sharing requires to share the model algorithm between STAs
We discussed several proposals to share ML algorithms between STAs.
  Proposal 1: share ML model by sending frames over the air
  Proposal 2: share ML model by downloading model from a cloud server
Each proposal has difficulties that we need to solve in the future.

## Slide 10: References
[1] 11-22/0597r3 May 2022 Working Group Motions, May 18, 2022
[2] 11-22/1934r5 Proposed IEEE 802.11 AIML TIG Technical Report Text for the CSI Compression Use Case
[3] 11-23/0050r3 Proposed Technical Report Text for AIML Model Sharing Use case
[4] 11-22/2119r5 Proposed IEEE 802.11 AIML TIG Technical Report Text for the Distributed Channel Access Use Case
[5] 11-23/0227r1 Proposed IEEE 802.11 AIML TIG Technical Report Text for the Multi-AP Coordination Use Case
[6] 11-23/0217r0 Proposed IEEE 802.11 AIML TIG Technical Report Text for the Subcarrier Grouping Use Case