## Slide 1: Obfuscation of Multiple CPE Parameters
Date: 2023-03-13
Authors:

## Slide 2: Revisions
R0 – Initial Version –

## Slide 3: Abstract
Current contribution describes a method for changing simultaneous multiple CPE parameters (e.g. OTA MAC Address, SN, PN, TID) of a CPE STA while it is associated with an AP by using a standard pseudo random generator based on shared private information allowing no explicit exchange of the changed CPE parameters.

## Slide 4: 11bi Requirements
R7 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection.
R9 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted SN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.
R10 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted PN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.
R11 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection.
R30 | 11bi shall define a mechanism for a CPE Client and CPE AP to obfuscate the transmitted TID to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.

## Slide 5: Overview
22/0114r3 specifies a Enhanced RCM (ERCM) procedure allowing the dynamic change of the MAC address of a non-AP STA when it is associated with an AP.
Extend this procedure to obfuscation of multiple CPE parameters of a CPE STA specified by the 802.11i task group(OTA MAC Address, SN, PN, TID, AID)

## Slide 6: Enhanced RCM (SERCM) procedure
Specifying a Seamless Enhanced RCM (SERCM) procedure allowing the dynamic change of the MAC address of a non-AP STA when it is associated with an AP.
  During, or after association, encrypted information (SERCM key) is shared between AP and non-AP STA.
  Upon AP or non-AP STA request, both AP and non-AP STA compute a new transient MAC address for the changing STA, without sharing it, by using same pseudo random generator with same parameters.
    Alternative scenario without any exchange between AP and non-AP STA (see slide 9)
  At the starting of the transition period, both AP and non-AP STA initiate the MAC address change for the changing non-AP STA.
  During the transition period, both current and new values for the MAC address are valid.

## Slide 7: New transient OTA MAC address
Upon AP or non-AP STA request, both AP and non-AP STA compute a new transient MAC address for the changing STA, without sharing it, by using the standardized PRF-128 (section 12.7.1.2 -IEEE Std 802.11-202) with same parameters.
@MAC (n+1) = PRF-128/46( ERCM Key, “ERCM”, @MAC (n) , 128)
  From the generated 128 bits, the leftmost 46 bits (i.e. the 46 most significant bits) are selected
  In addition to the 46 bits, the U/L bit of the new MAC address is set to 1, the I/G bit is set to 0
  @MAC (n) corresponds to the current address MAC of the non-AP STA

## Slide 8: CPE Parameters
As explained in 23/0166 [2], two obfuscation procedures shall be considered
Some (reset-based) CPE parameters as MAC Address, SN, AID can be obfuscated by resetting their value with new uncorrelated (and randomized) values
Other (reset-free) CPE parameters as PN and TID shall not be reset, their original setting being used to initiate and launch specific mechanism
  For them, generate and use masks for obfuscating them

## Slide 9: Multiple CPE Parameters
Both AP and non-AP STA compute simultaneously a list of CPE Parameters CPE_PARAM (including the OTA MAC address), without sharing them, by using the standardized PRF (section 12.7.1.2 -IEEE Std 802.11-2020) with same parameters in order to generate the same output CPE_PARAM (n+1) from which the CPE Parameters are obtained.
CPE_PARAM (n+1) = PRF-M\L( ERCM Key, “ERCM”, @MAC (n))
M = 128, 192, 256, 384, 512 or 704
L the leftmost bits corresponding to the sum of the lengths of the CPE parameters

## Slide 10: Multiple CPE Parameters
The output CPE_PARAM (n+1) is split into predetermined chunks, each chunk corresponding to for a reset-based CPE parameter or a new value of the mask of the reset-free CPE parameter
For MAC address, SN and AID, the chunks correspond to new values
For TID and PN, the chunks correspond to masks to be applied to generate the transmitted OTA_PN and OTA_TID
OTA_PN = PN XOR PN_Mask
OTA_TID = TID XOR TID_Mask
The PN (resp. TID) are recovered by the receiver by XORing OTA_PN and PN_Mask (resp. OTA_TID and OTA_Mask)
1 1 ……… 0 1 …….. 1 0 …………0………0 1………1 0 ………1
bit 1 ……… 47……… 59 ……… 107 ……. 123 ……. 130…….133
OTA MAC
address
OTA
SN
Mask
PN
OTA
AID
Mask
TID
OTA
Scrambler
Seed

## Slide 11: Benefits
User privacy is enhanced by allowing a station to change simultaneously a set of its CPE parameters
Implementation complexity and costs reduction as only single execution of the PRF is necessary to obfuscate the multiple CPE parameters

## Slide 12
Straw Poll #1
Do you agree 11bi should incorporate the proposed method described in slides 9 and 10?
Y/N/A
Yes
No
Abstain

## Slide 13: References
[1] IEEE 802.11-21/114r3 – Enhanced Randomized and Changing MAC address (ERCM)
[2] IEEE 802.11-23/166r0 - Mechanism of simultaneous changes to SN scrambler seed PN AID and TID