## Slide 1: TG bh IRM
Date: 2023-03
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
The default scheme in use is Same MAC Address (SMA)
When a STA returns to a network it uses the same MAC Address each time.
Problem is that the copying of the address is simple, and this possibly does not meet our privacy requirement.

## Slide 3: IRM cf SMA
IRM scheme is:
STA provides a (random) MAC Address to the AP/ESS in each association (msg 2)
STA uses that address in the next association.
One step further to SMA, (STA controls)
Simple, NO computations
STA controls the MAC Address (same as SMA)
  STA remembers address in same manner as SMA
Meets all use cases
Complements Device ID
  STA identified early (returning STA), then ID can be used

## Slide 4: IE/ID method(s)
STA adds new IE (to association request) which includes an ID
Different ID to Device ID
  Device ID can be fixed, but IE/ID must change every association
  STA and AP need to keep them separate - Device ID/IEID
  What ‘rules’ are required (look how Device ID grew)
What length?
  If not defined and fixed length, then is a simple fingerprint.
  How long? 6 octets for uniqueness?
    Why add a new IE? (What is advantage over IRM? )
Further divorced from SMA.

## Slide 5: Opaque ID in IE
Opaque ID tends to be long,
How it may be used in IE has not been defined
Same comments as IE/ID on previous slide.
Requires computations on AP side.
  Not sure if STA needs also to carry out computations.

## Slide 6: Why IRM?
IRM is one step beyond SMA - very much a “TGbh solution”
  No extra work required for STA cf SMA (one address stored per network)
  No extra work required for AP cf SMA (one address stored per STA)
Simple, NO computations –
  “simpler the solution the better the chance to be implemented”
Satisfies all Use Cases
  Option to allow say 2 Addresses, but not required (from discussions).
Complements Device ID
No new IE required (avoid fingerprint) - efficient
Need not use a capability bit (reduce fingerprint)
  Note SMA does not use a capability bit.
Text in 23/0129r0

## Slide 7: Conclusion
IRM ticks all the boxes for a TGbh solution.