## Slide 1: LB272 Comments on Sensing Terminologies
Date: 2023-03-13
Authors:

## Slide 2: Introduction
During the LB272 for 802.11bf D1.0, multiple commentors (~11 CIDs) brought up the concerns about the clarity of the terminologies for WLAN sensing and sensing procedures
This contribution discusses potential issues and an alternative solution

## Slide 3: Current Definitions for Sensing and Procedures in D1.0
In 3.2 (Definitions specific to IEEE Std 802.11)
DMG sensing: The use of PHY and MAC features of DMG stations (STAs) to obtain measurements that …
DMG sensing procedure: A procedure that allows a DMG station (STA) to perform DMG sensing
WLAN sensing: The use of PHY and MAC features of non-DMG stations (STAs) to obtain measurements that …
WLAN sensing procedure: A procedure that allows a non-DMG station (STA) to perform WLAN sensing
In 4.11 (Sensing)
Four procedures are defined to enable sensing:
WLAN sensing procedure (see 11.55.1 (WLAN sensing procedure)),
SBP procedure (see 11.55.2 (SBP procedure)),
DMG sensing procedure (see 11.55.3 (DMG sensing procedure)), and
DMG SBP procedure (see 11.55.4 (DMG SBP procedure)).

## Slide 4: Some comments from LB272 (samples)
CID | Clause | Comment | Proposed Changes
1032 | 4.11 | The name of the first sensing procedure defined in 11bf, "WLAN sensing procedure", is not clearly distinguitable from the 11bf project name, "WLAN sensing". Section 4.11 clearly states that WLAN sensing consists of 4 sensing procedures, i.e., "WLAN sensing procedure" is one of the four. It is really desirable to have a clearly identifiable name for the ""WLAN sensing procedure". | How about changing "WLAN sensing procedure" to "basic WLAN sensing procedure", throughout the 11bf spec?
1821 | 3.2 | Why is sensing procedure referred to as a WLAN sensing procedure? It appears that this should be called a non-DMG sensing procedure. DMG is also a WLAN, so it is rather confusing to use this adjective. | Change "WLAN sensing procedure" to "sensing procedure" throughout the draft.
1328 | 4.11 | … It seems as though WLAN sensing procedure described in 11.55.1 and SBP procedure described in 11.55.2 are for non-DMG STAs. To clarify that those are not describing general procedures including the DMG cases but are different from the ones described in 11.55.3 and 11.55.2, it is better to change the names of those procedures. | Change WLAN sensing procedure to non-DMG WLAN sensing procedure and SBP procedure to non-DMG SBP procedure throughout the draft.

## Slide 5: Terminologies used in IEEE P802.11bf PAR
5.2.b. Scope of the project:
This amendment defines modifications to the IEEE 802.11 medium access control layer (MAC) and to the Directional Multi Gigabit (DMG) and enhanced DMG (EDMG) PHYs to enhance Wireless Local Area Network (WLAN) sensing (SENS) operation in license-exempt frequency bands between 1 GHz and 7.125 GHz and above 45 GHz. This amendment enables:
Stations to perform one or more of the following: to inform other stations of their WLAN sensing capabilities, to request and setup transmissions that allow for WLAN sensing measurements to be performed, to indicate that a transmission can be used for WLAN sensing, and to exchange WLAN sensing feedback and information,
WLAN sensing measurements to be obtained using transmissions that are requested, unsolicited, or both, and
A MAC service interface for layers above the MAC to request and retrieve WLAN sensing measurements.

## Slide 6: Discussion
“WLAN Sensing”
  Better to keep it as a general term for all sensing operations in the scope of 802.11bf over different bands
“non-DMG Sensing” vs “DMG Sensing”?
  Large portion of the spec is about non-DMG sensing; carrying “non-DMG” around looks cumbersome
“SBP procedure” vs “DMG SBP procedure”
  Sound like the latter is part of the former, which is not the case
What we really want to distinguish is the sensing in different frequency bands
  “1 - 7.125 GHz” (or sub-7 GHz, or S7G) vs. “above 45 GHz”
    “Sub-7 GHz” is used in 3GPP community for frequencies from 410 MHz to 7125 MHz
    In 11ah, we used “S1G” for sub-1 GHz band

## Slide 7: Proposal
Replace “WLAN Sensing” in D1.0 by “S7G Sensing”
  Keep “WLAN Sensing” the same meaning as the one in PAR
Rename the three sensing procedures
  “WLAN sensing procedure”  “S7G Basic Sensing procedure”
  “SBP procedure”  “S7G SBP procedure”
  “DMG sensing procedure”  “DMG Basic Sensing procedure”
WLAN Sensing
S7G
Sensing
DMG Sensing
S7G Basic Sensing Procedure
S7G SBP Procedure
DMG Basic Sensing Procedure
DMG SBP Procedure
Note: Using “basic” may help to extend 11bf with new sensing procedures in the future.

## Slide 8: SP
Do you agree the following:
Change “WLAN Sensing” in D1.0 for sensing in 1 – 7.125 GHz bands to “S7G Sensing” in D2.0
Change “WLAN sensing procedure” in D1.0 to “S7G Basic Sensing procedure” in D2.0
Change “SBP procedure” in D1.0 to “S7G SBP procedure” in D2.0
Change “DMG sensing procedure” in D1.0 to “DMG Basic Sensing procedure” in D2.0

## Slide 9: SP
Which term do you prefer to use to replace “WLAN sensing” defined in 3.2 in 802.11bf D1.0:
S7G sensing
Non-DMG sensing
Sensing
Abstain
Result: 1/2/3/4: 2/1/18/6