## Slide 1: AIML-based Roaming Enhancements Use Case
Date: 2023-03-13
Authors:

## Slide 2: Abstract
The current document proposes AIML-based enhancements that can reduce the latency experienced by clients when they are operating in a highly roaming environment.

## Slide 3: Use of AI/ML to improve roaming experience
Campus and entreprise networks experience a high level of roaming clients. Nowadays, client’s QoS is severely impacted due to the time a client takes to decide onto which AP it should roam.
The proposed use case applies AI/ML to determine the probability of a client to roam to a specific AP, based on the learned client roaming patterns.
Multiple possible implementations, e.g., Markov chains, GNN…

## Slide 4: Perspective on 802.11k neighbor reports​
Sent by the AP upon STA request ​
  Indicates neighboring APs BSSID, channel, PHY type and optional elements (see 802.11-2020 9.4.2.36)​
  Useful to assist STA roaming decision (subset of channels and pre-scanned candidate list)
Not all neighbor APs are equally relevant for the clients to make optimal roaming decisions.
  AP can have tens of neighbors, close and far, STA may not roam to the closest or the farthest (depends on the path)​
  AP is not the STA (does not decide for the STA), and ’view from the ceiling’ is different from ‘view from the ground’

## Slide 5: Proposal for roaming-aware neighbor reports​
AIML can help make the 11k neighbor reports more useful by deducting roaming patterns to compute the probability of a client roaming to a given target AP​
  Help clients to prioritize scanning towards APs that are more probable targets​
  Improve roaming speed and reliability​
AI/ML techniques used to compute the neighbour weight​

## Slide 6: Usefulness evaluation: Impact Simulation 1
Computation on real network data:
Dataset info:
  6632 APs
  3 Million roaming events
  Distributed over 3 days
Chart info:
  Circle: group of APs having the same number of RF and roam neighbors
  X-axis: number of RF neighbors
  Y-axis: number of roaming neighbors
  Circle size: number of APs in the group
  Circle color: neighbor list reduction rate, by considering only roam neighbors
Greater impact in high-density environments

## Slide 7: Usefulness evaluation: Impact Simulation 2
Computation on real network data:
6632 APs in total
  Over 90% of APs would benefit an improvement by just by restricting the neighbor report to the roaming neighbors
  30% of APs have a reduction > 33%
  This improvement is not considering the probability assigned to each roam neighbor

## Slide 8: Neighbor List Enhancements – Adding neighbors weight​
The neighbor list can be further enhanced by adding the weight* based on the roaming paths/statistics:
In this example, out of 15 roaming neighbors, only 3 have a probability higher than ~20%
* Fraction of STAs roaming to each APs, and thus likelihood of each AP to be a good roaming candidate -> helps the STA sort the APs
Note: the reported MAC addresses are anonymized for privacy reasons as they come from a real production network​

## Slide 9: Adding neighbors weight​: Impact Simulation
The roaming-based neighbor weight helps further reducing the neighbor list:
Restricting the neighbor list to just APs with a probability higher than 0.2, if there’s at least one, else return all roam neighbors
The neighbor list would be reduced by more than 66% on 88% of the APs

## Slide 10: Adding neighbors weight​: Impact Comparison
The reduction in advertised neighbors improves significantly by adding the roaming-based weight

## Slide 11: Conclusion
Using AIML to compute the 11k neighbor report list can reduce the number of APs returned to the STA​
STA benefits:
  shorter time to discover possible neighbors of roaming
  possible higher confidence in the list returned by the AP

## Slide 12: Implementation Notes​
  The results in the previous slides have been computed modeling the neighbor list as a Markov chain, where the probability distribution is computed using the successful roaming events to each AP’s RF neighbor.
  The advantage of this approach:
  Simple implementation
  Can be centrally computed for each AP and re-computed periodically
  No need to know the full client roaming path

## Slide 13: Possible Additional Enhancements​
  Make the list SSID-specific:
    Clients on different SSIDs may follow different roaming paths (e.g., enterprise scenario; from the building entrance, guests can reach only common areas while employees can also enter the office area)
  Add time information
    e.g., time of the day, day of the week
    The roaming path is likely different at different times of the day, e.g., people entering vs. exiting the building)
  Use GNN to model the full clients’ roaming paths:
    Currently under investigation
    More complex to maintain and generalize
    May not provide significant improvement over a simpler approach, also considering encoding in neighbor reports (e.g., having 2-bits to classify neighbors in 4 buckets)

## Slide 14: Summary
Proposal to include a Roaming Enhancements Use Case to the AIML Technical Report
  AIML can greatly improve the client experience in a roaming scenario by providing a weighted list of AP roaming candidates
  The clients can use this info to prioritize scanning based on the probability to roam to specific neighbours, as computed by the infra​
  Backwards compatibility; clients not supporting this feature will simply use the neighbour report ignoring the weights

## Slide 15: Straw Poll
Do you agree to include a Roaming Enhancements Use Case to the AIML Technical Report?
  Yes
  No
  Abstain