## Slide 1: Coex SC Closing Report
Date: 2023-05-18
Authors:

## Slide 2: Abstract
Closing report for IEEE 802.11 Coex SC (Coexistence Standing Committee) for May 2023.

## Slide 3: Coex SC – ETSI BRAN News
Goal: list EN 301 893 (5 GHz) and EN 303 687 (6 GHz) as Hamonized Standards (HS) in the Official Journal of the EU (OJEU) to ease manufacturers’ self-assessment of products
EN 301 893 (5 GHz)
  Document ready
  Ongoing technical discussions on Energy Detection Threshold (EDT); might conclude in upcoming ETSI BRAN meeting (June session)
  Attn.: Does not consider PHY beyond 11ac; features of IEEE 802.11ax and beyond require notified body approval
EN 303 687 (6 GHz)
  ENAP closes 2023-06-27
  Covers also 5945 MHz to 6425 MHz available for license-exempt operation in Europe
EN 303 753 (60 GHz) – ENAP and HASTAC review requested
TR 103 721 (5.8 GHz coexistence) -- To be published by ETSI
G. Hiertz: “European spectrum regulation and the harmonised market of the European Union—An overview”, 802.18 Tutorial, May 2023, 18-23/0054r0.

## Slide 4: Coex SC – Bluetooth SIG Update
Presented spectrum sharing goals from the Bluetooth SIG perspective
  Successful sharing in the past
  Develop optimal sharing scheme, e.g., in 6 GHz or U-NII-3, 5725 – 5850 MHz
Bluetooth SIG prepared response to FCC FNPRM 20-51 (6 GHz unlicensed use)
  Details of response not discussed as it has not been submitted yet by Bluetooth SIG
  Submission planned in the next day
Bluetooth SIG intends to propose new Work Item in ETSI BRAN (likely at #120 in September 2023), potentially addressing
  (New) channel access scheme for narrowband technologies
  New channelization scheme
  Mechanisms to allow LPI (Low Power Indoor) client-to-client operations
  Development of FBE (Frame Based Equipment) and LBE (Load Based Equipment) parameters for channel access mechanism

## Slide 5: Coex SC – Narrow Band / WiFi Coexistance
Further discussion of Narrow Band / WiFi coexistence simulations from previous Coex SC meeting in March
  Simulations for different parameters as used in the simulations results presented in March
  Enhanced Detect and Avoid (eDAA) performs better than Listen Before Talk (LBT) for Adjacent channels/null’s from NB
Consider further discussion and evaluation of NB / WiFi coexistence highlighting different scenarios / resulting simulation parameters
Notes: Enhanced Detect and Avoid -- eDAA, as proposed in ETSI BRAN as an enhanced version of DAA as defined in EN 300 328 (2.4 GHz))
Listen before talk (LBT)
LBT for Frame Based Equipment (FBE) as defined in EN 303 687

## Slide 6: Topics for next meeting
Receive updates from
  ETSI BRAN
  Bluetooth SIG
Submission: Overview of the Bluetooth SIG response to FCC FNPRM 20-51
Further NB discussion (tbc).
Discuss further interaction 802.11 and 802.15 (15.4ab and 15.6ma (UWB))  Champion needed to push this work item
Other – feel free to contact the Chair if you would like to make a presentation on any additional coexistence topic

## Slide 7: References for this week
Agenda for this week: 11-23/0582
Snapshot Slide: 11-23/0583
Meeting / Chair’s Slide Deck: 11-23/0584
Closing report: 11-23/0585
Meeting minutes: 11-23/0894